## Slide 1
<number>
GRPE Informal Working Group on
Heavy Duty Hybrids
UNITED NATIONS
        Report to GRPE 68
        Geneva, 09 January 2014
Informal document No. GRPE-68-14
(68th GRPE, 07 - 10 January 2014,
agenda item 4(a))

## Slide 2: Contents
<number>
UNITED NATIONS
ECE - GRPE
HDH
  Summary of the 15th and 16th HDH meetings
  Status of HDH validation test program 2
  Open issues list
  Status of drafting group
  Presentation of informal document GRPE 68-12
  HDH timeline, roadmap & project planning
  Next meetings

## Slide 3: Summary of 15th HDH Meeting
<number>
UNITED NATIONS
ECE - GRPE
HDH
The results of the 15th meeting in San Francisco on 24 and 25 October 2013 are summarized, as follows:
  The results of validation test program 1 with the new model structure were presented by the institutes; the new model structure includes a comprehensive component model library, a new signal naming convention and restructured vehicle models
  The next model release is foreseen for 31/10/2013
  No further input on chassis dyno testing has been made; the final decision should be taken at the 16th HDH meeting
  Validation test program 2 at JRC has started in May; so far, the validation criteria of the Japanese regulation could not be met; further work is needed.
  Institutes and JASIC will jointly develop a proposal for fixed slopes
  A specific procedure for plug-in hybrids will not be included
  The OICA proposal on vehicle parameters was agreed
  Weighting factors will not be included
  Discussion on master ECU will continue
  Discussion on work (engine or system) for the emissions calculation will continue at the 16th meeting
  The technical secretary of HDH drafting group has been nominated
  The drafting group will work hard to have the informal document ready for the 68th GRPE

## Slide 4: Summary of 16th HDH Meeting
<number>
UNITED NATIONS
ECE - GRPE
HDH
The results of the 16th meeting in Geneva on 07 January 2014 are summarized, as follows:
  Model version 0.5 was released and some comments received; still minor improvements necessary
  Chassis dyno testing will not be included in this gtr amendment
  Evaluation of validation test program 2 will continue until April 2014 (details see page 5); EPA asked for a transparent validation process incl. availability of detailed test results
  As regards the drive cycle, institutes and JASIC have agreed on the fixed slope minicycle approach; implementation is ongoing with final approval foreseen at 17th HDH meeting
  Definition of rated power for a hybrid system still under discussion
  US EPA raised concerns with the timeline of the current mandate, while Japan supported November 2014 WP.29 adoption in order to have time for transposition into the post-JP09 regulation planned for 2016; EU COM also supported November 2014 adoption, but indicated that further discussion is needed on EU implementation
  Approval procedure for OEM specific models must be defined more clearly
  Discussion on hardware control functions (master ECU) will continue
  While Japan and OICA support total system work as basis for emissions calculation, other CPs have not finalized their position yet. EU-COM and some EU CPs raised reservations; discussion among EU CPs will follow.
  Provided that the ongoing activities deliver according to the expectations, the group expects that the timeline can still be met
  Due to the open issues (details see page 6), there remains a risk that the work program will not be finalized in time

## Slide 5: Status of Validation Test Program 2
<number>
UNITED NATIONS
ECE - GRPE
HDH
JRC test program
  Validation test program 2 with real HVs started at JRC with in May 2013
  Test with two vehicles (Volvo & MAN) completed
  Iveco vehicle will be tested at JRC in February 2014 with torque measurement device installed on vehicle
  Additional dyno testing of MAN vehicle at MAN in January 2014
  So far, problems encountered to meet Japanese verification criteria
  Data evaluation and problem solution still ongoing
  Validation expected to be completed by the end of March 2014
Consequences
  Timely validation is a prerequisite for HDH adoption
  If validation fails or open issues are not solved to the satisfaction of the group, extension of the mandate will be requested at GRPE 69

## Slide 6: Open Issues
<number>
UNITED NATIONS
ECE - GRPE
HDH
Evaluation of validation test program 2
WHVC road gradients (agreed, implemented by March 2014)
HILS verification criteria
Approval procedure for OEM specific models
Basis for brake specific emissions calculation (system work vs. engine work)
Definition of hardware hybrid control functions or master ECU
Hybrid system family concept
  HILS testing

## Slide 7: Drafting Group
<number>
UNITED NATIONS
ECE - GRPE
HDH
Status
  Two meetings in March and May 2013 w/o technical secretary
  Technical secretary was installed in September 2013
  The 3rd meeting was held on 22 and 23 October 2013 in San Francisco
  The 4th to 6th meetings were held in November/December 2013 as web meetings
  The 7th meeting was held on 18 December 2013 in Brussels
Further procedure
  The drafting group will continue to work until April/May 2014
  2 further web meetings planned in January/February 2014
  Next face-to-face meeting on 18/19 February 2014 in Tokyo

## Slide 8: Overview Informal Document 68-12
<number>
UNITED NATIONS
ECE - GRPE
HDH
The following approach was taken for amendment 3 to gtr n° 4
  Preparation of a consolidated version of gtr n° 4 (amendments 1 & 2)
  New annexes 8 (HILS) & 9 (powertrain test)
  Addition of WHVC with road gradients to annex 1
  Amendments to base regulation, where necessary, such as
    definitions
    hybrid powertrain family
    general test procedure
    stop/start approach
In addition, the secretary (former WHDC secretary) is asking to further align gtr n° 4 with gtr n° 11
  Focus on calibration protocols and description of test equipment
  Not yet included in GRPE-68-12

## Slide 9: Informal Document 68-12 Definitions
<number>
UNITED NATIONS
ECE - GRPE
HDH
Hybrid related definitions have been added to § 3.1, which are aligned with the current VPSD draft, as far as possible
  “drivetrain” means the connected elements of the powertrain downstream of the final energy converter
  “energy converter” means the part of the powertrain converting one form of energy into a different one
  “energy storage system” means the part of the powertrain that can store chemical, electrical or mechanical energy, and which can be refilled or recharged externally and/or internally
  “generator” means an energy converter transferring mechanical energy into electric energy
  “hardware-in-the-loop simulation (HILS)” means real time hybrid vehicle simulation running on a computer where a hardware component interacts with the simulation through an interface
  “hybrid vehicle” means a vehicle with a powertrain containing at least two different types of energy converters and two different types of energy storage systems
  “powertrain” means the combination of energy storage system(s), energy converter(s) and drivetrain(s) [for the purpose of vehicle propulsion], and the communication interface (hardware and messages) among the powertrain or vehicle control units
  “rechargeable energy storage system (ReESS)” means a system storing energy carriers other than fuels
  “ReESS subsystem” means any functional assembly of ReESS components
  “stop/start system” means automatic stop and start of the internal combustion engine to reduce the amount of idling

## Slide 10: Informal Document 68-12 Hybrid Powertrain Family
<number>
UNITED NATIONS
ECE - GRPE
HDH

## Slide 11: Informal Document 68-12 General Approach
<number>
UNITED NATIONS
ECE - GRPE
HDH

## Slide 12: Informal Document 68-12 Annex 8
<number>
UNITED NATIONS
ECE - GRPE
HDH

## Slide 13: Informal Document 68-12 Annex 8 – Principal Procedure
<number>
UNITED NATIONS
ECE - GRPE
HDH

## Slide 14: Informal Document 68-12 Annex 9
<number>
UNITED NATIONS
ECE - GRPE
HDH

## Slide 15: Informal Document 68-12 Non-HDH Related Amendments
<number>
UNITED NATIONS
ECE - GRPE
HDH
When adopting gtrs n° 4 and n° 11, alignment could not be completed, but is still desirable to be improved
  Amendment 3 to gtr n° 4 offers this opportunity
  It is assumed that these amendments do not require specific WP.29 approval
  The proposed amendments will not change gtr n° 4 in essence, but focus on improvements of the calibration protocols
  The amendments are not yet included in GRPE-68-12, but the sections affected are marked, as shown below
  The proposed alignment offers an evident advantage to engine/vehicle manufacturers, test laboratories and type approval authorities who deal with both on-highway and nonroad engines
  GRPE is asked to endorse the proposal

## Slide 16: HDH Timeline
<number>
UNITED NATIONS
The HDH group proposes the following timeline to GRPE:
  Informal document GRPE-68-12 is presented to GRPE 68 for consideration; it includes text finalized by December 2013
  The formal document for GRPE 69 will be based on informal document GRPE-68-12
    it will include the drafting progress and those items of the open issues list on page 6 resolved by 01/03/2014
  An informal document will be submitted to GRPE 69 by 15/05/2014, which will
    include the drafting progress after March 2014 and the remainder of the open issues list
    complement the formal document submitted in March 2014
  After adoption of both documents by GRPE 69, a consolidated document will be provided to WP.29 for approval
  The technical report can only be submitted as an informal document to GRPE 69, since the work program will not be completed by March 2014
GRPE is asked to agree to the proposal
HDH is aware that there remains a risk of not being able to meet this timeline
  In that case, an extension of the mandate would be requested at GRPE 69
ECE - GRPE
HDH

## Slide 17: Roadmap & Project Planning
<number>
UNITED NATIONS
ECE - GRPE
HDH

## Slide 18: Next Meetings
<number>
UNITED NATIONS
The next HDH meetings are scheduled as follows:
  The 17th meeting will be on 08 and 09 April 2014 in Madrid
  The 18th meeting will be on 03 June 2014 in Geneva (to be confirmed)
The next drafting group meetings are scheduled as follows:
  The 8th meeting will be on 27 January 2014 (web meeting)
  The 9th meeting will be on 10 February 2014 (web meeting)
  The 10th meeting will be on 18 and 19 February 2014 in Tokyo
  Further web meeting(s) in March 2014
  The final meeting will be on 10 and 11 April 2014 in Madrid
  Further web meeting(s) in April/May 2014, if needed
GRPE is asked to
  Reserve a half day for the 18th HDH meeting during the 69th GRPE session in June 2014
ECE - GRPE
HDH