## Slide 1
Informal document GRPE-68-19
(68th GRPE, 7-10 January 2014, agenda item 11)
Transmitted by the VPSD IWG
Status report
after the 3rd VPSD meeting
Geneva – 7th January 2014
Notes: <number>
07.01.2014
3rd VPSD meeting

## Slide 2
Content
State of play and documentation
Open issues, discussion items
Next steps
Way forward
07.01.2014
3rd VPSD meeting
<number>
Notes: <number>
07.01.2014
3rd VPSD meeting

## Slide 3
1. State of play and documentation
Status report to 66th GRPE – inf.doc GRPE-66-29
Draft VPSD document VPSD-02-03 (with track changes and comments) VPSD-02-04 (additional comments & proposals from EC)
WLTP – draft GTR – ECE/TRANS/WP.29/2014/27
HDH – draft amendment to GTR 4 – GRPE-68-12
EVE – Reference Guide – EVE-08-03
QRTV – GTRQRTV-05-06e.pdf draft GTR
07.01.2014
3rd VPSD meeting
<number>
Notes: <number>
07.01.2014
3rd VPSD meeting

## Slide 4
2. Open issues, discussion items
B. 1 Powertrain
B. 2 Rechargeable Energy Storage System
B. 3.1. Combustion Engine (CE)
B.4. Drivetrain
B. 7.1.-7.4. Mono-, Bi-, Flex-, Dual-Fuel Vehicle
B. 9.2. Hybrid Electric Vehicle (HEV)
B. 10. Characteristics of vehicle powertrains
07.01.2014
3rd VPSD meeting
<number>
Notes: <number>
07.01.2014
3rd VPSD meeting

## Slide 5
B. 1 Powertrain
Approach is still under discussion. Agreed in principle:
One single powertrain system
Including: multiple possible devices (energy storage, energy converter and drivetrain systems, with peripherals) and combinations.
Excluding: ancillary devices.
Specific definitions to be further developed.
The following diagram was outlined as a general scheme based on current conventional vehicle architecture
and need to be further reviewed.
07.01.2014
3rd VPSD meeting
<number>
Notes: <number>
07.01.2014
3rd VPSD meeting

## Slide 6
Ancillaries
POWERTRAIN
Example: conventional vehicle
Energy
Storage(s)
Peri-pherals
Energy
Converter(s)
Peri-pherals
Drivetrain(s)
After-treatment(s)
Heat
07.01.2014
3rd VPSD meeting
<number>

## Slide 7
B. 2 Rechargeable Energy Storage System (no acronym)
REESS - Rechargeable Electric Energy Storage System (already used in WLTP draft GTR)
RMESS - Rechargeable Mechanical Energy Storage System
RHESS - Rechargeable Hydraulic Energy Storage System
RPESS - Rechargeable Pneumatic Energy Storage System
 Needs to be amended in HDH documents
07.01.2014
3rd VPSD meeting
<number>
Notes: <number>
07.01.2014
3rd VPSD meeting

## Slide 8
B. 3.1. Combustion Engine (CE) - Internal Combustion Engine (ICE) / - External Combustion Engine (ECE)
Option 1: To start with ICE (CE and ECE concept can be added later, if needed, in regulations).
Option 2: Directly introduce CE (sub-divided in ICE and ECE).
 Option 1 was agreed upon. Definition still needs to be finalised.
07.01.2014
3rd VPSD meeting
<number>
Notes: <number>
07.01.2014
3rd VPSD meeting

## Slide 9
B.4. Drivetrain
Under discussion: Definition and terminology
„Drivetrain“ or „Power transmission system“ ?
The terminology „drivetrain“ could be used to define all devices downstream of last energy converter.
It has however still to be understood how to consider powertrain transmission devices used in between several energy converters of the powertrains.
07.01.2014
3rd VPSD meeting
<number>
Notes: <number>
07.01.2014
3rd VPSD meeting

## Slide 10
B. 7.1.-7.4. Mono-, Bi-, Flex-, Dual-Fuel Vehicle
Existing UN-Regulations (49, 83, 101) already includes definitions, which are very fuel- and design- specific (gaseous, LPG/Diesel, 15 liter petrol tank, etc.). It would be beneficial to introduce under VPSD more general definitions on the different kinds of fuel operations of powertrains, while regulations could use more specified terminology (but based upon the general definitions) and define related tests or exemptions.
 VPSD upcoming proposal to be discussed by GFV IWG
07.01.2014
3rd VPSD meeting
<number>
Notes: <number>
07.01.2014
3rd VPSD meeting

## Slide 11
B. 9.2. Hybrid Electric Vehicle (HEV)
Currently different definitions exist worldwide
(e.g. HEV is novc/not-externally chargeable
and PHEV is ovc/externally chargeable)
Option 1: HEV covers all HV applications with a powertrain containing at least one electric machine as energy converter (VPSD proposal, used by HDH).
Option 2: HEV means a vehicle using at least one fuel consuming machine and one electric machine for the purpose of vehicle propulsion (current WLTP draft GTR).
 WLTP to provide feedback on HEV definition
07.01.2014
3rd VPSD meeting
<number>
Notes: <number>
07.01.2014
3rd VPSD meeting

## Slide 12
B. 10. Characteristics of vehicle powertrains
Currently about 20 terms and definitions are under discussion. This can be further developed at a later stage. This chapter isn‘t considered as a first priority.
However, the use of harmonized terminology in different regulations might be beneficial.
07.01.2014
3rd VPSD meeting
<number>
Notes: <number>
07.01.2014
3rd VPSD meeting

## Slide 13
3. Next steps
Consolidated VPSD proposal document will be prepared by secretary (Daniela Leveratto) and chairman (Christoph Albus), reviewing VPSD-02-04 and taking into account the outcome of the 3rd VPSD and the 68th GRPE session.
It will be further elaborated by email and teleconference by VPSD-experts (*).
A further session of the IWG is not yet scheduled.
(*) Experts willing to contribute shall request the Secretary to be added to the distribution list
07.01.2014
3rd VPSD meeting
<number>
Notes: <number>
07.01.2014
3rd VPSD meeting

## Slide 14
4. Way forward
Introduction of an annex into R.E.3 / S.R.1, as a first step and basis, with a view to continue the work in a second step (with or without VPSD IWG), adapting it to technical progress and keeping legislation harmonized.
Request WP.29 to extend the mandate of VPSD IWG (June 2015).
07.01.2014
3rd VPSD meeting
<number>
Notes: <number>
07.01.2014
3rd VPSD meeting