## Slide 1
Progress report of GRSG
informal group on Accident
Emergency Call System
(AECS)
Transmitted by the Chair of
AECS IWG
Informal document GRSG-106-31
106th session, 5-9 May 2014,
Agenda item 14
Denis Zagarin
Chairman of the GRSG informal group AECS
Notes: We would like to explain about a summary of Fourth progress report of the informal group on Phase 2 of gtr No. 9 (IG GTR9 - PH2) instead of IG GTR9-PH2 chair.
<number>

## Slide 2
  1st stage: 159th WP.29 - March 2013 Geneva
  The presentation of Russian Federation (WP.29-159-22)
  The announcement to propose a draft UN Regulation on accident emergency call systems ( ECE/TRANS/WP.29/2013/67)
  2nd stage: 160th WP.29 – June 2013 Geneva
  The presentation of the 1st Draft UN Regulation for the requirements of accident emergency call systems
  (ECE-TRANS-WP29-2013-067)
  WP.29 approved the request of the Russian Federation to establish a new GRSG informal group on Automatic Emergency Call Systems (AECS) (WP.29 report ECE/TRANS/WP.29/1104)
Foundation of the informal working group

## Slide 3
AECS informal group meetings
Period | Meeting title | Place | Key points
October 2013 | 1st meeting | Geneva | Russian Federation presented the revised draft UN Regulation on the ECE-TRANS-WP29-2013-067/rev.1 basis (Document: AECS 01-05e) The following items were addressed: - Limited to M1/N1 - 3-parts structure: (a) type approval of AECS devices for vehicles of categories M1 and N1 (b) type approval of vehicles with regard to the installation of approved AECS devices (c) the type approval of vehicles with regard to AECS function
December 2013 | 2nd meeting | Paris | OICA provided the updated proposal for the draft UN Regulation based on AECS 01-05e (Document: AECS 02-02e) Presentations: Effective dates for the mandatory requirements on installed ERA-GLONASS systems/devices (Russian Federation) Current situation of Accident Emergency Call System in Japan (Japan)
Notes: IG GTR9-PH2 meetings were held 6th times in total so far from Dec. 2011.
We would like inform recent and future activity of IG GTR9-PH2 in the next slide.
<number>

## Slide 4
Period | Meeting title | Place | Key points
February 2014 | 3rd meeting | Moscow | Russian Federation provided the updated proposal for further development of the draft UN Regulation on AECS 02-02e base (Document: AECS 03-04) Presentations: ERA-GLONASS (Russian Federation) HELPNET System (Japan) OICA proposal for AECD and AECS requirements Antenna requirements (CETECOM) The following items were addressed: Scope of the draft UN Regulation Communication with mobile phone networks Data transmission mechanism Minimum set of data AECS triggering conditions (UN R94/R95 environment) EMC, climate resistance and mechanical resistance Navigation module requirements
AECS informal group meetings

## Slide 5
AECS informal group meetings
Period | Meeting title | Place | Key points
April 2014 | 4th meeting | Paris | Presentations: European Commission's position on the GNSS (EC) Automatic triggering of emergency call (TRL) OICA position on homologation procedure (OICA) Justification Climatic, Mechanical resistance and EMC requirements (Russian Federation) The following items were addressed: Climatic, Mechanical resistance and EMC requirements Scope of the draft UN Regulation AECS triggering conditions GNSS aspects Possible solutions for general approach
Next meetings will be held on: Turin 2-4 September 2014 |  |  | 

## Slide 6
  1. Mobile communication standards are regulated nationally and are not compatible in different regions
  Key issues which should be put into GRSG consideration:
Background:
AECD/AECS need mobile phone communication for sending MSD and establishing voice communication.
Mobile phone networks are currently not compatible worldwide.
Mobile phone technology evolves quickly.
Existing technology (Quad band) may provide basic performances almost anywhere, with maximum performance in one particularly aimed area.
Possible solutions:
Frequency requirements to be out of the AECS regulation, i.e. AECD/AECS shall fulfil the national requirements for what concerns the communication standards.
Quad band technology.
Introducing different classes for AECD/AECS per each set of applicable regional communication standards (favoured by the AECS informal group)
Another solution from GRSG.

## Slide 7
  2. Data transmission mechanism – there is no technology which can support all Contracting Parties
  Key issues which should be put into GRSG consideration:
Background:
MSD,VIN, transmission process and protocols are not harmonized worldwide and depend on deployed infrastructure.
Possible solutions:
limiting the regulation to a list of data, and letting the transmission process and protocols to the national legislation.
Introducing different classes for AECD/AECS per each set of regional protocol and data transmission mechanism (favoured by the AECS informal group)
Another solution from GRSG.

## Slide 8
  Introducing different classes of Type Approvals for AECD/AECS per each set of applicable regional communication standards in one Regulation
R XXX (AECS)
90% of harmonized requirements
Class I
Mobile communication standards: GSM-900/1800, UMTS-900/2100
Regional protocol and data transmission mechanism: 2G/3G and in-band modem + SMS as a backup mechanism (Technology in application in Russia)
Class II
Mobile communication standards: GSM-900/1800, UMTS-900/2100
Regional protocol and data transmission mechanism: 2G/3G and in-band modem
(Technology in application in EU)
Class III
Mobile communication standards: UMTS 1700/2100
Regional protocol and data transmission mechanism: CDMA for voice communication and package data transmission via LTE (Technology in application in Japan)
10% of non-harmonized requirements can be defined thrоugh different classes:

## Slide 9
  Key issues which should be put into GRSG consideration:
  3. Global Navigation Satellite Systems.
Background:
Principle of 1958 Agreement supposes technology neutral approach
The only one global positioning technology available at the moment is satellite related (Global Navigation Satellite Systems)
Existing test methods for positioning are GNSS constellation dependant
Request for guidance:
Can we mandate the use of GNSS in a UN Regulation?

## Slide 10
  Terms of Reference and Rules of Procedure of the informal Group of GRSG on Accident Emergency Call System (AECS).
Document GRSG 106-18, item 6. “The target completion date for the work of the informal group shall be the 109th session of GRSG in October 2015. Vehicles of categories N2, N3, M2, and M3 may be covered in a later stage.”
AECS request to GRSG to postpone the target completion date for the work:

## Slide 11
Thank you for your attention!
Notes: Read above sentences.
<number>