## Slide 1
Ref. paragraphs of UN-Reg. No. 58 |  | OICA (GRSG/2014/11) Vehicle Categories |  | Germany (GRSG/2014/18) Vehicle Categories | 
 |  | N1, N2, O1, O2 | N3, O3, O4 1) | M, N1, N2, O1, O2, G, and veh. with platform lift | N3, O3, O4
7.1. / 25.4. | Height of cross member | ≥ 100 mm | ≥ 120 mm | ≥ 100 mm | ≥ 120 mm
7.4.2. / 25.8.2. | Effective Surface | ≥ 350 cm² | ≥ 420 cm² 6) | ≥ 350 cm² | ≥ 420 cm²
16.3. / 25.6. | Horizontal distance | ≤ 400 mm | ≤ 400 mm | ≤ 300 mm (incl. N3), bef. defo. ≤ 400 mm (incl. N3), aft. defo. Determination by excl. of resilient buffers (max. 50 mm) | ≤ 200 mm (O3, O4), bef. defo. ≤ 300 mm (O3, O4,), aft. defo. Determination by excl. of resilient buffers (max. 50 mm)
16.1. / 25.1. | Ground clearance | ≤ 550 mm | ≤ 450 mm 2) ≤ [500/550] mm 3) ≤ 550 mm 5) | ≤ 550 mm (M, N1, N2, O1, O2) ≤ 10°, 20°, 25° (cat. G) | ≤ 450 mm (autom. levelling) ≤ 500 mm (no autom. lev.) ≤ 550 mm (for dep. angle 8°)
16.1. / Annex 5, 3.1. | Test force application | ≤ 600 mm | ≤ 510 mm 2) ≤ [560/610] mm 3) ≤ 610 mm 5) | ≤ 600 mm | At horizontal center line of crossbeam [≤ 510 mm, ≤ 560 mm]
Annex 5, 3.1.1. | Test force | 100 kN or 50 % max. gross weight 4) | 180 kN or 85 % max. gross weight 4) | 180 kN or 85 % max. gross weight 4) (total force levels may be red. to 80 % for veh. with tipp.-bod. or platf.) | 180 kN or 85 % max. gross weight 4) (total force levels may be red. to 80 % for veh. with tipp.-bod. or platf.)
Annex 5, 3.1.2. | Test force | 50 kN or 25 % max. gross weight 4) | 100 kN or 50 % max. gross weight 4) | 100 kN or 50 % max. gross weight 4) (total force levels may be red. to 80 % for veh. with tipp.-bod. or platf.) | 100 kN or 50 % max. gross weight 4) (total force levels may be red. to 80 % for veh. with tipp.-bod. or platf.)
Annex 5, 3.1.3. | Test force | 50 kN or 25 % max. gross weight 4) | 100 kN or 50 % max. gross weight 4) | 100 kN or 50 % max. gross weight 4) (total force levels may be red. to 80 % for veh. with tipp.-bod. or platf.) | 100 kN or 50 % max. gross weight 4) (total force levels may be red. to 80 % for veh. with tipp.-bod. or platf.)
UN R58 - RUPD requirements – comparison of proposed requirements of doc. GRSG/2014/11 and GRSG/2014/18
Submitted by the expert from Germany | Informal document GRSG-106-32 (106th GRSG, 5 – 9 May 2014 agenda item 6)

## Slide 2
1) Vehicles with rearward tipping bodies or special purpose vehicles of category N3 or vehicles of category N3G
are considered the same values as for N1, and N2 vehicles.
2) Vehicles with hydropneumatic, hydraulic or pneumatic spring.
3) Vehicles with other than hydropneumatic, hydraulic or pneumatic spring at the rear axle.
4) Whichever is the lower value.
5) On vehicles with a departure angle more than 8°according ISO 612:1978.
6) According items 7.4.2 or 25.8.2, it is possible to reduce the effective surface to not less than 350 cm²