## Slide 1: Proposal for amendment of UNR34
Informal document GRSG-106-33
(106th GRSG, 5-9 May 2014,
agenda item 3)
Submitted by the expert from Japan

## Slide 2: Contents
Purpose of this amendment
Contents of amendment
Justification
Summary

## Slide 3
１．Purpose for the amendment
There are two main purposes for this amendment proposal;
Prevention and mitigation of vehicle fire breaking out by rear-end collision (enhancing safety).
Considering establishment of IWVTA at the end of 2016, we would like to make it easier to adopt UNR34 for countries who haven’t yet (harmonization).
Japan thinks not only ① but also ② are important.

## Slide 4: ２． Contents of the amendment
Present
After amendment
① collision speed : 34Km/h
② Manufacturers’ selection
① collision speed : 50Km/h
② Mandatory

## Slide 5: ３．Justification
 | Impact speed | Collision type | Option/mandatory
USA | 80km/h ※implement rollover test after the test. | Off set | mandatory
Canada | 80km/h ※implement rollover test after the test. | Off set | mandatory
Japan | 50km/h | Full wrap | mandatory
China | 50km/h | Full wrap | mandatory
Korea | 46.8～48.2km/h | Full wrap | Mandatory
UNECE R34 | 35～38km/h | Full wrap | Option (manufacture’s option)
① Present UNR34 can be said lax comparing other countries’ regulations for vehicle fire risks, because of it’s lower Impact speed and the test is optional.
Therefore, Impact speed and test option should be amended to be higher and as mandatory.

## Slide 6: ３．Justification
② We can see a certain effect by raising the speed.
Survey Conditions
* Years of data: 2001-2006
Subject vehicles:
Ordinary & light passenger cars
Accident type:
Vehicle-to-vehicle rear-end collision
Subject accidents:
Accidents causing injury or death by fire
Years of first registration:
Before & after rear-end collision
regulation tightening
* Number of vehicles: 1,196,686
In Japan, after the tightening of the rear-end collision regulation (collision speed 35 km/h  50 km/h), the severe injury and death incidence rate of rear-end collisions by fire has reduced to about 1/3, indicating that the regulatory tightening is effective.
0.48 (N=9/188,549)
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1.0
Severe injury and death incident rate of rear-end collisions
(No. of vehicles with fire incidence per 10,000 vehicles with accidents causing severe injury or death)
Before
tightening Collision speed 35 km/h
After
tightening Collision speed 50 km/h
0.14 (N=14/1,008,137)
※Rear-end collisions

## Slide 7: ３．Justification
③ The speed by 50km/h will cover 97% of the whole accidents of rear-end collision.
（35km/h covers only 77%)
Survey Conditions
* Years of data: 2010
* Subject vehicles: Ordinary & light passenger cars
* Accident type: Vehicle-to-vehicle rear-end collision
* Subject accidents: Accidents causing death, serious injury or minor injury
* Subject occupants: Occupants in rear-ending & rear-ended vehicles
All accidents:
No. of persons: 157,891
20
40
60
80
100
10
20
30
40
50
60
70
80
90
100
Cumulative total of injured persons (%)
0
0
Collision speed (km/h)
(The rear-ending vehicle driver’s danger recognition speed with the rear-ended vehicle being stationary)
All accidents
(N=157,891)
９７％
35
77
97

## Slide 8: ４．Summary
・Purpose of Japan’s proposal of amendment are:
Not only prevention and mitigation of vehicle fire by rear-end collision(enhancing safety),
But also making it easier for countries who haven’t adopted UNR34 yet, on the basis of establishment of IWVTA(harmonization),
Therefore,
・we would like to propose to raise the collision speed’ and ‘ to make it mandatory’
・comparison with other regulations and analysis of decline of numbers of accidents in Japan showed it’s efficiency.
・We would like your understanding and supporting our proposal.

## Slide 9
Thank you for your attention!