## Slide 1
Controls, Tell-tale and Indicator (ECE N° 121.00) Focus on common space regarding the current Regulation
Informal document GRSG-106-35
(106th GRSG, 5-9 May 2014
agenda item 10))

## Slide 2: §5.5 Common Space for Displaying Multiple Information
"Common space" means an area on which two or more information functions (e.g. symbol) may be displayed but not simultaneously.
A common space may be used to show information from any source, subject to the following requirements:
  The tell-tales and indicators in the common space shall provide relevant information at the initiation of any underlying condition.
§ 5.5.1
§ 5.5.1.1
All tell-tales located in a Common space for Displaying Multiple Information shall respect requirements of each safety regulation (e.g. lighting, Tire Pressure Monitoring (TPMS), Braking, etc.). In these regulatory boundries the vehicle manufacturer is free to define the location of the tell-tale and the contents of the message.
§ 2.4
Illustration with an example from TPMS regulation (ECE 64)
General case for the usage of Paragraph 5.5.1
For TPMS, ECE 64 indicates that the tell-tale shall be displayed when the pressure of the tire is low or when a malfunctioning of the monitoring system is detected. The Common space may be used to satisfy ECE 64 requirements.

## Slide 3: §5.5 Common Space for Displaying Multiple Information
§ 5.5.1
A common space may be used to show information from any source, subject to the following requirements:
  When the underlying condition exists for actuation of two or more tell-tales, the information shall be either:
    Repeated automatically in sequence, or
§ 5.5.1.2
For TPMS tell-tale, two possibilities are allowed:
Preserve continuously the display of the tell-tale in the Common space if vehicle manufacturer doesn’t decide to install this tell-tale in the instrument panel, or
Manage sequentially the display occurrence between TPMS tell-tale and for example Brake lining wear-out condition tell-tale.
§ 5.5.1.2.1

## Slide 4: §5.5 Common Space for Displaying Multiple Information
§ 5.5.1.2.1
Illustration: display alternatively in the same order.
Common Space sketch
Possible tell-tale Locations
(1)
(2)
(3)
(4)
(5)
(6)
Example step 1: There is a sole TPMS failure event, then TPMS tell-ale is continuously displayed (for example in location 1).
Example step 2: Following step 1, a Brake lining wear-out event occurs. If manufacturer chose to display the relevant tell-tale in another location than location 1, for example in location 5, then Brake lining wear-out tell-tale shall be displayed continuously.

## Slide 5: §5.5 Common Space for Displaying Multiple Information
§ 5.5.1.2.1
(1)
(2)
(3)
(4)
(5)
(6)
Example step 1: There is a sole TPMS failure event, then TPMS tell-ale is continuously displayed (for example in location 1).
Example step 2: Following step 1, a Brake lining wear-out event occurs. If manufacturer chose to display the relevant tell-tale in the same location 1, then the two tell-tale shall be displayed alternatively in this location.
Common Space sketch
Possible tell-tale Locations
Illustration: display alternatively in the same order.

## Slide 6: §5.5 Common Space for Displaying Multiple Information
§ 5.5.1
A common space may be used to show information from any source, subject to the following requirements:
  When the underlying condition exists for actuation of two or more tell-tales, the information shall be either:
    Indicated by visible means and capable of being selected for viewing by the driver under the conditions of paragraph 5.6.2;
§ 5.5.1.2
 Allows customizing the order of appearance of the failures tell-tale, with a control for example.
§ 5.5.1.2.2

## Slide 7: §5.5 Common Space for Displaying Multiple Information
§ 5.5.1
A common space may be used to show information from any source, subject to the following requirements:
  When the underlying condition exists for actuation of two or more tell-tales, the information shall be either:
    Indicated by visible means and capable of being selected for viewing by the driver under the conditions of paragraph 5.6.2;
    Indicating the most safety-relevant failure, or
    When two or more functions are integrated as a single function, or when functions are related to each other such as to be considered as a single function, the information relative to that single function may be indicated by one tell-tale.
§ 5.5.1.2
§ 5.5.1.2.2
§ 5.5.1.2.3
§ 5.5.1.2.4

## Slide 8: §5.5 Common Space for Displaying Multiple Information
Illustration: Indicating the most safety-relevant failure
(1)
(2)
(3)
(4)
(5)
(6)
Example step 1: A malfunction in the Brake System occurs (ECE 13H #5.2.21.1.2), the relevant tell-tale is displayed with the relevant yellow color.
Example step 2: After step 1 a failure of the Brake System occurs (ECE 13H #5.2.21.1.1). A red color tell-tale must be displayed, and this could be done for example in location 3. But this could be also confusing for the driver.
§ 5.5.1.2.3
Possible tell-tale Locations
Common Space sketch

## Slide 9: §5.5 Common Space for Displaying Multiple Information
Illustration: Indicating the most safety-relevant failure
(1)
(2)
(3)
(4)
(5)
(6)
§ 5.5.1.2.3
Possible tell-tale Locations
Common Space sketch
Example step 1: A malfunction in the Brake System occurs (ECE 13H #5.2.21.1.2), the relevant tell-tale is displayed with the relevant yellow color, in this case in location 3.
Example step 2: After step 1 a failure of the Brake System occurs (ECE 13H #5.2.21.1.1). A red color tell-tale must be displayed, and this could be done for example in location 3. No confusion for the driver.

## Slide 10: §5.5 Common Space for Displaying Multiple Information
§ 5.5.1.2.4
Illustration: information of functions considered as functions related to each other as a single function  may be indicated by one tell-tale
(1)
(2)
(3)
(4)
(5)
(6)
Example step 1: Driver activates “Headlamp passing beams”, the relevant voluntary tell-tale is displayed (status of headlamp function)
Example step 2: Driver activates “Headlamp main beams”, then relevant mandatory tell-tale is displayed instead, at the same location. This is the new status of the headlamp function.
Possible tell-tale Locations
Common Space sketch

## Slide 11: §5.5 Common Space for Displaying Multiple Information
§ 5.5.1
A common space may be used to show information from any source, subject to the following requirements:
  The tell-tales for the brake system malfunction, when required to be red, headlamp driving beam, direction indicator and driver seat safety belt shall not be shown in the same common space.
§ 5.5.1.3
Brake system malfunction
Headlamp driving beam
Direction indicator
Driver safety belt
(1)
(2)
(3)
(4)
(5)
(6)
Each priority tell-tale has its own location. Consequently, only the location (1) and (2) may be used for the non priority tell-tale.
Possible tell-tale Locations