## Slide 1
Submitted by the expert from Republic of Korea
Informal document GRSP-56-21
(56th GRSP, 9-12 December 2014,
agenda item 3(a))
Clarification of Test Methods for Active Devices in Pedestrian Protection
Notes: <number>

## Slide 2: Table of Contents
1. Current Statement (text)
2. Open Issues and Justifications
3. Proposed Test Procedures
Notes: <number>

## Slide 3: 1. Current Statement
ECE/TRANS/180/Add.9 (26 January 2009) –GTR 9
6.2.2. All devices designed to protect vulnerable road users when impacted by the vehicle shall be correctly activated before and/or be active during the relevant test. It shall be the responsibility of the manufacturer to show that any devices will act as intended in a pedestrian impact.
Notes: <number>

## Slide 4
2. Open Issues and Justification
Clarification of Test Methods for
Active Devices in Pedestrian Protection
Justification:
Recently, the active deployable devices for pedestrian protection are available in the market.
Republic of Korea, both 1958 and 1998 agreement member country, implements the vehicle self-certification system. The system requires the precise test procedure. Therefore, clarification of test procedures for the active devices (such as active hood, pedestrian airbag) is needed.
For the active devices, there are the detailed test procedures being practiced in EuroNCAP and KNCAP
EuroNCAP or KNCAP procedures can be considered as a reference materials to amend GTR No.9.
Notes: <number>

## Slide 5
2. Proposed Test Procedures
Start
Test at Minimum Speed
OK
Effectiveness
Test under
Un-deployed condition
Verification(2) :
Detection Performance
PDI Test
Active Hood Works ?
Verification (3) :
Deployment Time
HIT( Vs TRT
Comparison
HIT>TRT
Static Test
End
Dynamic Test
No
Yes
No
Yes
Yes
No
Verification[1) : Effectiveness
Test at Maximum Speed
Find Maximum Deformation
※ Pedestrian Airbag must be tested in Dynamically
Maker Data
Impact Test
PDI: Pedestrian Detection Impactor
HIT: Head Impact Time
TRT: Total Response Time(Sensing Time+Deploy Time)
Test under
Un-deployed condition
Notes: <number>

## Slide 6: Thank you for your attention.
Notes: <number>