## Slide 1: Pedestrian Safety
Effects of Bumper Test Area Determination Using the Old vs. the New Method
Presented by the experts of OICA
Informal document GRSP-56-30
(56th GRSP, 9-12 Dec. 2014,
agenda item 3(a))

## Slide 2: Benefits of the Method Using Corner Gauges Only
27 Nov. 2014
2
For most vehicles, the test area will be extended (as suggested by several authorities) and will at least remain unchanged for a very few
For only very few vehicles, the bumper beam will continue to extend beyond the test area, as is the case today
  The new method:
    Is feasible, repeatable, reproducible, less sensitive to specific design features
    Can be performed without disassembling parts
    Is suitable also in self certification framework
  OICA therefore supports this method

## Slide 3
Comparison: Old and New Method vs. Bumper Beam Width
Data were delivered by 9 OEM‘s for 103 vehicles in total.
27 Nov. 2014
3

## Slide 4
Thank you!
For detailed questions please refer to the authors, Mr. Thomas Kinsky / General Motors Europe Engineering, Mr. Winfried Schmitt / BMW and Mr. Jörg Kusche / Porsche, as representatives of the International Organization of Motor Vehicle Manufacturers OICA
27 Nov. 2014
4

## Slide 5
27 Nov. 2014
For the determination of the bumper corners, „current method“ or „old method“ refer to the method used today in gtr No. 9 and UN R127: vertical planes make angles of 60° with the vertical longitudinal plane of the vehicle and are tangential to the outer surface of the bumper, the contact points are the corners of bumper
„New proposal“ or „new method“ refer to the method proposed by the Task Force Bumper Test Area (TF-BTA) in their documents: 236 x 236 mm corner gauges are moved parallel to vertical planes with angles of 60° to the vertical longitudinal center plane of the vehicle, the outermost points of contact are the corners of bumper
„Bumper beam“ refers to the structural cross member under the bumper fascia protecting the front of the vehicle but does not include foam, cover support or any pedestrian protection devices
Back-up
5