UN/SCETDG/47/INF.26

| Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals 10 June 2015 |
| --- |
| Sub-Committee of Experts on the Transport of Dangerous Goods |  |
| Forty-seventh session Geneva, 22 – 26 June 2015 Item 3 of the provisional agenda Listing, classification and packing |  |

Introduction of a new entry for Phosphorothioic acid, O-[(cyanophenylmethylene)azanyl]O,O-diethyl ester (“Phoxim”) in n-Butanol

Transmitted by the European Chemical Industry Council (CEFIC)

Introduction

- The title compound is the active ingredient of a formulation used in veterinary medicine as an insecticide and acaricide for the treatment of farm animals. The mixture consists of the (E) and (Z) isomers with an assay of 82-91 % Z isomer in n-butanol.

Figure 1: Chemical structure of Phosphorothioic acid,  O-[(cyanophenyl methylene) azanyl] O,O-diethyl ester (“Phoxim”), (E) and (Z) isomers

- By request from industry, the German Competent Authorities had issued a temporary approval for the transport of the mixture classified as UN 3227 SELF-REACTIVE LIQUID, TYPE E. This paper is meant to inform the Subcommittee about industry’s intention to submit a formal proposal for the December session with the request for the creation of a corresponding new entry in the list of self-reactive substances of  chapter 2.4.2.3.2.3.

- Members of the Subcommittee are requested to review the data submitted in this paper and to forward any comments to the CEFIC delegation.

Test data

- All tests were performed according to the methods specified in the UN Recommendations on the Transport of Dangerous Goods, Manual of Tests and Criteria, fifth revised edition, with amendments 1 and 2.

5.	The classification procedure led to the final result (Figure 20.1 of the UN Test Manual)

Exit E, accepted for transport in packages of not more than 400 kg/ 450 litres.

Details are specified in the test report in Annex I.

Proposal

6.	In chapter 2.4.2.3.2.3, create an entry in the list of self-reactive substances as follows

| SELF-REACTIVE SUBSTANCE | Concen-tration (%) | Packing method | Control tempe-rature (°C) | Emergencytempe-rature (°C) | UN generic entry | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| Phosphorothioic acid, O-[(cyanophenyl methylene) azanyl] O,O-diethyl ester | 82-91 (Z isomer) | OP 8 |  |  | 3227 | (10) |

7.	Add a new remark (10) at the end of the same chapter as follows:

(10) This entry applies to the technical mixture in n-Butanol with the concentration limits of the (Z) isomer.

Justification

8.	The fact that the product is carried in large quantities and is used worldwide justifies a new entry in the list of self-reactive substances. The test results are clear, and a formal temporary approval has been issued for all modes by the German authorities. The concentration limits apply to the product as registered for veterinary purposes.

Annex I

Test report

1.	Name of substance 				Phosphorothioic acid,  O-[(cyanophenyl

methylene) azanyl] O,O-diethyl ester

2.	General data

2.1	Composition				88.1 % active ingredient

2.1 % sum of impurities

Solution in n-Butanol

2.2	Molecular formula:				C12H15N2O4PS

2.3	Available oxygen content			Not applicable

2.4 	Activator content				Not applicable

2.5	Physical form				Liquid

2.6	Colour				Dark yellow

2.7	Apparent density				1130 kg/m³

2.8	Particle size				Not applicable

3. 	Detonation (test series A)

Box 1 of the flow chart				Does the substance propagate a detonation?

3.1 	Method				BAM 50/60 steel tube test (test A.1), test in

cavitated state (German method)

3.2	Sample conditions				Ambient temperature

3.3	Observations				190 mm of tube fragmented, unreacted
							substance remained in the tube

3.4	Result		No

3.5	Exit		1.3

4.	Deflagration (test series C)

Box 5 of the flow chart	Does the substance propagate a deflagration?

4.1 	Method 1		Time/pressure test (test C.1)

4.2	Sample conditions		Ambient temperature

4.3 	Observations		Time 310-330 ms

4.4	Result		Yes, slowly

4.5 	Method 2		Deflagration test (test C.2)

4.6	Sample conditions		Temperature  40 °C

4.7	Observations		Deflagration rate 0.30 mm/s

4.8 	Result		No

4.9	Overall result		No

4.10 	Exit		5.3

5. 	Heating under confinement (test series E)

Box 9 of the flow chart	What is the effect of heating it under defined

confinement?

5.1	Method 1	Koenen test (test E.1)

5.2	Sample conditions	Mass 32.1 g

5.3 	Observations	Limiting diameter 1.0 mm

(time to reaction 28 s, duration of reaction 14 s)

5.4	Result	Low

5.5	Method 2	Dutch pressure vessel test (test E.2)

5.6	Sample conditions	10.0 g

5.7 	Observations	Limiting diameter 2.0 mm

(time to reaction 51 s)

No rupture of the disc with an orifice of 3.5 mm

but rupture of the disc with an orifice of 2.0 mm

5.8	Result	Low

5.9	Overall result	Low

5.10	Exit	9.3

6. 	Box 11 of the flow chart	Is the self-reactive substance to be considered

for transport in IBCs or tanks, or for exemption?

6.1 	Result	No

6.2 	Exit	11.2

Accepted for transport in packages of not more

than 400kg/450 litres

7.		Thermal stability (test series H)

7.1	Method	Heat accumulation storage test (H.4)

7.2		Sample conditions	400 ml substances in Dewar vessel, heat loss

35-42 mW/kgK

7.3	Observations	Auto-accelerating decomposition at 75 °C,

No reaction at 50°C and 60 °C

7.4	Result	No temperature control required

8. 	Additional data (see 20.5.3)

8.1 	Method	BAM fallhammer test (test 3 (a) (ii))

8.2	Sample conditions	Ambient temperature

8.3	Observations	No explosion up to an impact energy of 40 J

8.4 	Result	Not sensitive to impact

8.5	Method	BAM friction apparatus (test 3 (b) (i))

8.6	Sample conditions	Ambient temperature

8.7	Observations	No explosion up to a friction load of 360 N

8.8 	Result	Not sensitive to friction

8.9	Method	DSC

8.10	Sample conditions	Closed glass crucible, heating rate 3 K/min)

8.11	Observations	Exothermic decomposition of about 1100 kJ/kg,

onset of 90 °C.

9. 	Proposed assignment

9.1 	Proper shipping name	SELF-REACTIVE LIQUID, TYPE E

9.2	UN number	3227

9.3	Division	4.1

9.4 	Technical name	Phosphorothioic acid,  O-[(cyanophenyl 
			methylene) azanyl] O,O-diethyl ester

9.5	Concentration	82-91 % (Z isomer)

9.6	Diluent	n-Butanol

9.7	Subsidiary risks		None

9.8	Packing group

9.9	Packing method		OP8

9.10	Control temperature		Not required

9.11	Emergency temperature	Not required

Annex II

Data sheet to be submitted to the United Nations for new or amended classification of substances

Submitted by Bayer HealthCare AG, 51368 Leverkusen, Germany          	Date:      May 12th, 2015

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions - if necessary state “not known” or “not applicable” - If data is not available in the form requested, provide what is available with details. Delete inappropriate words.

Section 1:	Substance identity

1.1	Chemical name		Phosphorothioic acid,  O-[(cyanophenyl 						methylene) azanyl] O,O-diethyl ester, mixture of 					(E) and (Z) isomers dissolved in n-Butanol 					(concentration of Z isomer 82-91 %)

1.2	Chemical formula		(C6H5)-C(CN)=N-O-PS(OEt)2

1.3	Other names/synonyms	Phoxim VL, Phoxim VL 80, Sebacil VL 80, Volaton;

1.4.1	UN number:	  3227

1.4.2	CAS number ……..	14816-18-3 (Phoxim), CAS 71-36-3 (butanol)

1.5	Proposed classification for the Recommendations

1.5.1	Proper shipping name (3.1.2)	SELF-REACTIVE LIQUID, TYPE E

1.5.2	class/division 4.1	subsidiary risk(s) ………………………………

packing group …………………………………………………………

1.5.3	proposed special provisions, if any                 274

1.5.4	proposed packing instruction(s) P520, OP8

Section 2:	Physical properties

2.1		Melting point or range  -90 	°C (n-butanol)

2.2		Boiling point or range 116 °C – 118 °C (n-butanol)

2.3		Relative density at:

2.3.1	15 °C	not known

2.3.2	20 °C	1.13 g/cm3

2.3.3	50 °C	not known

2.4		Vapour pressure at:

2.4.1	20 °C  	0.35 kPa

2.4.2	50 °C	not known

2.4.3	65 °C	not known

2.5		Viscosity at 20 °C 	not known

2.6		Solubility in water at 20 °C	: not miscible

2.7		Physical state at 20°C (2.2.1.11)		liquid2

2.8	Appearance at normal transport temperatures, including colour and odour:  	yellow-brownish liquid, aromatic odour 
	….……………………………………………………………………………

2.9	Other relevant physical properties: pH 3.9 at 10 g/l

……………………………………………………………………………….

……………………………………………………………………………….

Section 3: Flammability

3.1		Flammable vapour

3.1.1	Flash point (2.3.31)  38 °C (closed cup)

3.1.2	Is combustion sustained? (2.3.1.31)		yes

3.2	Autoignition temperature      not known

3.3		Flammability range (LEL/UEL) 1.4 / 11.3	% (n-butanol)

3.4		Is the substance a flammable solid? (2.4.21)		no

3.4.1	If yes, give details   not applicable ……………………………….
		………………………………………………………………………..
		……………………………………………………………………….
		……………………………………………………………………….

Section 4: Chemical properties

4.1		Does the substance require inhibition/stabilization or other treatment such as nitrogen 		blanket to prevent hazardous reactivity ?			no

If yes, state:

4.1.1	Inhibitor/stabilizer used     not applicable …………………………….

4.1.2	Alternative method            not applicable …………………………….

4.1.3	Time effective at 55 °C     not applicable ……………………………..

4.1.4	Conditions rendering it ineffective      not applicable …………………

4.2		Is the substance an explosive according to paragraph 2.1.1.1? (2.11)        no

4.2.1	If yes, give details      not applicable …………………………………...
			…………………………………………………………………………….
			…………………………………………………………………………….
			…………………………………………………………………………….

4.3		Is the substance a desensitized explosive? (2.4.2.41)	no

4.3.1	If yes, give details     not applicable ………………………………………….

…………………………………………………………………………………………….

…………………………………………………………………………………………….

4.4		Is the substance a self-reactive substance? (2.4.11)          yes

If yes, state:

4.4.1	exit box of flow chart:  E

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package?

60 °C < SADT < 75 °C

Is the temperature control required? (2.4.2.3.41)	no

4.4.2	proposed control temperature for a 50 kg package          not applicable

4.4.3	proposed emergency temperature for a 50 kg package    not applicable

4.5		Is the substance pyrophoric? (2.4.31)      no

4.5.1	If yes, give details       not applicable

………………………………………………………………………………………………

……………………………………………………………………………………………….

……………………………………………………………………………………………….

4.6		Is the substance liable to self-heating? (2.4.31)                 no

4.6.1	If yes, give details      not applicable

……………………………………………………………………………………………….

……………………………………………………………………………………………….

……………………………………………………………………………………………….

4.7		Is the substance an organic peroxide (2.5.11)        no

If yes state:

4.7.1	exit box of flow chart        not applicable ………………………………………

What is the self accelerating decomposition temperature (SADT) for a 50 kg package?	°C

Is temperature control required? (2.5.3.4.11)      no

4.7.2	proposed control temperature for a 50 kg package          not applicable

4.7.3	proposed emergency temperature for a 50 kg package    not applicable

4.8		Does the substance in contact with water emit flammable gases? (2.4.41) 	no

4.8.1	If yes, give details           not applicable

………………………………………………………………………………………………

……………………………………………………………………………………………….

……………………………………………………………………………………………….

4.9		Does the substance have oxidizing properties (2.5.11)		no

4.9.1	If yes, give details         not applicable

……………………………………………………………………………………………….

……………………………………………………………………………………………….

………………………………………………………………………………………………..

4.10	Corrosivity (2.81) to:

4.10.1           mild steel     not known     at ………………………………..C

4.10.2          aluminium    not known      at………………………………..C

4.10.3          other packaging materials (specify)

not known	             at	……………………………….C

4.11	 Other relevant chemical properties: see test report in Annex I

Section 5. Harmful biological effects

5.1  LD50, oral (2.6.2.1.11) 300 – 2000 mg/kg	Animal species	rat (Phoxim (ISO))

5.2  LD50, dermal (2.6.2.1.21) > 2000 mg/kg	Animal species	rat (Phoxim (ISO))

5.3	  LC50, inhalation (2.6.2.1.31)	> 4 mg/litre       Exposure time 4 hours

Animal species	rat (Phoxim (ISO))

5.4	  Saturated vapour concentration at 20 °C (2.6.2.2.4.31)    not known

5.5	  Skin exposure (2.81) results	Exposure time 	 hours/minutes

Animal species

5.6	  Other data: Causes skin irritation (GHS H315)

5.7	Human experience             not known

Section 6. Supplement information

6.1		Recommended emergency action

6.1.1	Fire (include suitable and unsuitable extinguishing agents)

Suitable: alcohol-resistant foam, dry chemical or carbon dioxide; unsuitable: water

6.1.2	Spillage	 Keep away from sources of ignition. Cover spilled product with liquid-binding 
			material (sand, silica gel, acid binder, universal binder, hybilat).
			Take up mechanically and fill into labelled, closable containers.

6.2		Is it proposed to transport the substance in:

6.2.1	Bulk Containers (6.81)                                 no

6.2.2	Intermediate Bulk Containers (6.51)             no

6.2.3	Portable tanks (6.71)?	                   no

If yes, give details in Sections 7, 8 and/or 9.

Section 7:	 Bulk containers (only complete if yes in 6.2.1)

7.1		Proposed type(s)                   not applicable

Section 8:	 Intermediate bulk containers (IBCs) (only complete if 	yes in 6.2.2)

8.1		Proposed type(s)       not applicable

Section 9:	 Multimodal tank transport (only complete if yes in 6.2.3)

9.1		Description of proposed tank (including IMO tank type if known)     not applicable

9.2		Minimum test pressure           not applicable

9.3		Minimum shell thickness       not applicable

9.4		Details of bottom openings, if any      not applicable

9.5		Pressure relief arrangements       not applicable

9.6		Degree of filling             not applicable

9.7		Unsuitable construction materials         not applicable

# Footnotes

This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

See definition of "liquid" in 1.2.1 of the Model Regulations on the Transport of Dangerous Goods.

1 		This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1		This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1 		This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.