## Slide 1: Traffic noise and motorway pavements
W. Alberts, CEDR Road Noise,
Geneva, 28.01.2015
Transmitted by the Conference
of European Directors of Roads
Informal document GRB-61-16
(61st GRB, 27-29 January 2015,
agenda item 10)
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 2: Question
W. Alberts
Traffic noise and motorway pavements
<number>
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 3: Overview
W. Alberts
Traffic noise and motorway pavements
<number>
objectives
CEDR
road noise
pavements
figures on use, noise, lifetime and costs
conclusions and final remarks
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 4: Objectives
W. Alberts
Traffic noise and motorway pavements
<number>
To inform about:
CEDR
pavements used on motorways in Europe and their noise reduction, lifetime and costs
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 5: CEDR: profile
W. Alberts
Traffic noise and motorway pavements
<number>
What is CEDR:
  the Conference of European Directors of Roads (CEDR) is a forum for the discussion and promotion of improvements to the road system and its infrastructure
  members represent their national road authorities (NRAs) in Europe
Now there are 27 CEDR member states (MS)
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 6: CEDR: mission
W. Alberts
Traffic noise and motorway pavements
<number>
to analyze future developments of the road system
to promote international networks of personal contacts
to provide a platform for responding to common problems
to develop a strong involvement in EU developments
to use existing representations in international groups
to make use of the results of common understandings
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 7: CEDR: structure
W. Alberts
Traffic noise and motorway pavements
<number>
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 8: CEDR: Road Noise
W. Alberts
Traffic noise and motorway pavements
<number>
The two main goals of CEDR Road Noise 2013-2017 are:
improve noise quality in close proximity to road infrastructure
reduce costs in planning, building, maintaining and researching road infrastructure
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 9: Road traffic noise
W. Alberts
Traffic noise and motorway pavements
<number>
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 10: Road traffic noise
W. Alberts
Traffic noise and motorway pavements
<number>
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 11: Road: layers
W. Alberts
Traffic noise and motorway pavements
<number>
a road has several layers (courses)
for road noise the surface layer (pavement) is important
surface layer consists of aggregates (stones) bound together with bitumen (asphalt)
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 12: Pavements
W. Alberts
Traffic noise and motorway pavements
<number>
wide range of motorway pavements available:
these pavements differ for functional aspects like lifetime, costs, noise reduction and driver comfort (splash and spray)
these pavements meet MS standards for skid resistance
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 13: Pavements: use
W. Alberts
Traffic noise and motorway pavements
<number>
pavements on motorways in CEDR MS (in %)
DAC and SMA are preferred pavements in most CEDR MS
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 14: Pavements: use
W. Alberts
Traffic noise and motorway pavements
<number>
pavements on motorways in CEDR MS (in %)
DAC and SMA are preferred pavements in most CEDR MS
noise reducing pavements like PA, TL and TLPA are used in some CEDR MS
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 15: Pavements: noise
W. Alberts
Traffic noise and motorway pavements
<number>
initial noise reduction (in dB, MS standard pavement is zero)
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 16: Pavements: noise
W. Alberts
Traffic noise and motorway pavements
<number>
initial noise reduction (in dB)
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 17: Pavements: noise
W. Alberts
Traffic noise and motorway pavements
<number>
initial noise reduction (in dB)
transition from much used pavements (DAC/SMA) to noise reducing pavements (PA/TL) reduces noise with 2 to 3 dB
average lifetime noise reduction is less than initial reduction
acoustic properties of pavements are covered in regulation and noise calculation model in CEDR MS
harmonization at EU level (END and CNOSSOS-EU)
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 18: Pavements: lifetime
W. Alberts
Traffic noise and motorway pavements
<number>
lifetime (average in years)
lifetime of noise reducing pavements is less than lifetime of non-noise reducing pavements
MAIN PAVEMENTS: | AT | BE-F | DE | DK | EE | ES | FR | GR | IE | IT | LV | NL | SE |  | range | average
Dense Asphalt Concrete | 15 |  | 12/18 | 15/17 | 20 | 6/10 | >12 | 20 | 20/22 | >20 | 20 | 18 |  |  | 12-22 | 17
Stone Mastic Asphalt | 10/15 | 15 | 16/22 | 15/17 | 20 |  |  |  | 16/17 |  | 20 |  | 6/12 |  | 6-22 | 16
Cement Concrete | 30/40 | 40 | 26/30 |  |  | 15/20 |  |  |  |  |  |  |  |  | 15-40 | 30
Porous Asphalt | 8/10 |  | 8 |  |  | 6/10 |  | 8/10 | 15/16 | 10/15 |  | 17 |  |  | 6-17 | 11
Thin Layers |  |  |  | 12 |  | 6 |  |  |  |  |  | 13 |  |  | 6-13 | 10
Two Layer Porous Asphalt |  |  |  |  |  |  |  |  |  |  |  | 13 | 5/8 |  | 5-13 | 10
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 19: Pavements: costs#1
W. Alberts
Traffic noise and motorway pavements
<number>
all-in investment costs (EUR/m2)
little information and wide range of all-in investment costs
investment costs of noise reducing pavements is higher than costs of non-noise reducing pavements
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 20: Pavements: costs#2
W. Alberts
Traffic noise and motorway pavements
<number>
all-in maintenance costs (EUR/m2/year)
very little information
average maintenance costs of noise reducing pavements is more or less comparable with costs of most non-noise reducing pavements
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 21: Conclusions
W. Alberts
Traffic noise and motorway pavements
<number>
In general:
there is no standard pavement on motorways in Europe
the use of pavements is based on NRA policy and CEDR MS regulation
main reason for using a pavement: costs and lifetime
constraints like winter circumstances limit the choice of pavements
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 22: Conclusions
W. Alberts
Traffic noise and motorway pavements
<number>
Regarding the use of noise reducing pavements:
some CEDR MS use noise reducing pavements
in acoustic hot spots to lower noise levels
noise reducing pavements are more cost-effective than noise barriers
noise reducing pavements lower noise levels with 2 to 3 dB (max. 6 dB)
do not overestimate the possibilities of using noise reducing pavements
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 23: Final remarks
W. Alberts
Traffic noise and motorway pavements
<number>
the best way to lower traffic noise levels is by reducing noise production
three domains in traffic noise production: vehicles, tyres and pavements
reducing traffic noise production is a shared responsibility
CEDR, its NRAs and the paving industry are doing a lot of research to improve noise reducing pavements
at EU level CEDR is working on cooperation with the other domains
Notes: Bern
29.07.26
cocodrillotour
<number>

## Slide 24: End
W. Alberts
Traffic noise and motorway pavements
<number>
THANK YOU FOR YOUR INTEREST
Notes: Bern
29.07.26
cocodrillotour
<number>