## Slide 1
Draft interstate standard
“Automotive vehicles. Internal noise. Admissible levels and test methods”
Developer: Testing centre FSUE “NAMI”
Speaker: Cand. Sc. (Engineering) Y. V. Galevko
Transmitted by the expert from
the Russian Federation
Informal document GRB-61-17
(61st GRB, 27-29 January 2015 ,
agenda item 9)
Notes: <number>

## Slide 2: Historic reference (regulatory requirements for automotive vehicles)
1965 – 2000
ON 025 304-67 Vehicles and road-trains. Noise measurement methods.
GOST 19358-85 (ST EIC 4864-84) External and internal noise of vehicles.
ISO 5128-80 Acoustics-Measurement of noise inside motor vehicles
TRANS/SC1/WP29/R.235 UNECE Draft regulation on internal noise (April 13,1981)
GOST 27435-87 Vehicles internal noise. Admissible levels and test methods.
GOST R 51616-2000 + (amendment No.1, 2009)
Is used as obligatory in the national vehicle certification system and covers all vehicle categories intended for operation on roads of Russia.

## Slide 3: Historic reference (regulatory requirements for driver’s workplace and interior environment)
GOST 12.1.003-83 (latest issue of 2008) Occupational safety standards system. Noise. General safety requirements (method reference is GOST R 51616)
Admissible levels, set in SN 2.2.4/2.1.8.562-96 (GOST 12.1.003.-83)
  60 dB(A) (PS65) for busses and passenger vehicles (driver’s place + passengers)
  70 dB(А) (PS 65) for cargo vehicles (driver’s place + operator)
  limiting values in octave bands
  These norms characterize admissible harm which can be put on a driver under the condition of constant noise influence during a labor shift
Health regulations on occupational health of drivers No.4616-88
SN 2.2.4/2.1.8.562-96 Noise at workplaces, in residential and public buildings.
Lack of the standardized test methods in sanitary standards and the standards "Occupational safety standards systems" results in ambiguity of interpretation of assessment results of the normalized indicators entered by these normative documents and impossibility to carry out comparative tests.
OST 37.001.492-93 Vehicle internal noise. Determination methods of equivalent levels.

## Slide 4: Hygienic regulation (regulatory requirements for driver’s workplace and interior environment)
Federal Law No. 52-FZ of 30.03.1999 “On Sanitary and Epidemiological Welfare”
HYGIENIC REQUIREMENTS FOR PHYSICAL FACTORS OF INDUSTRIAL AND NATURAL ENVIRONMENT. Sanitary Rules and Regulations (SanPiN) 2.2.4/2.1.8……-15 ??????
GOST 12.1.003-……. 2015 ????

## Slide 5: Technical regulation (regulatory requirements for driver’s workplace and interior environment)
Federal Law No. 184-FZ of 27.12.2002 “On Technical Regulating”
The technical regulation — is the document (regulatory legal act) establishing requirements obligatory for application and execution to objects of technical regulation (products) unlike ISO, GOST, TU and other standards having voluntary application.
Technical Regulation on Safety of Wheeled Vehicles (Enforced by the Governmental Decree No. 720 of 10.09.2009)
List of standards:
GOST R 51616-2000 (+ Amendment No.1, 2009)

## Slide 6: Technical regulation (regulatory requirements for driver’s workplace and interior environment)
Customs Union
Technical Regulation of Customs Union on Safety of Wheeled Vehicles (CU TR 018/2011) (Approved by the Decision of the Customs Union Commission No. 877 of 09.12.2011)
List of standards:
GOST R 51616-2000 (amendment No.1, 2009)
STB GOST R 51616 -2002 (amendment No.1, 2010)
Draft interstate standard GOST……..- 2015 – to be developed

## Slide 7: Technical regulation (External noise - CU TR 018/2011)
Annex 2
Item 7 - Regulation No. 9-06
Item 23 Regulation No. 28-00
Item 33 Regulation No. 41-03
Item 41 Regulation No. 51-02 (+ 3dBA is permitted for all-wheel-drive vehicles of N2G,N3G, М2G, M3G categories)
Item 52 Regulation No. 63-01
Item 88 Regulation No.117-02 (stage 2 from 2017)

## Slide 8: Annex 3 Paragraph 2 Table 2.1 - Limiting values for sound level (CU TR 018/2011)

## Slide 9: Annex 3 Paragraph 2 Table 2.1 - Limiting values for sound level (CU TR 018/2011)

## Slide 10: Annex 3 Paragraph 2 Table 2.1 - Limiting values for sound level (CU TR 018/2011)

## Slide 11: Terms of development of the standard
The Eurasian Interstate Council for Standardization, Metrology and Certification (EASC)
Armenia, Azerbaijan, Belarus, Georgia, Kazakhstan, Kyrgyzstan, Moldova, Russian Federation, Tajikistan, Turkmenistan, Ukraine, Uzbekistan
Draft interstate standard GOST February 2015 – completion of discussion
May 2015 – final edition

## Slide 12
The objective and goals of the draft standard development
Provision of regulatory base of the Technical Regulation On Safety of Wheeled Vehicles
Establishment of uniform requirements for internal noise measurement for vehicles within the to methods of measurement of internal noise of automotive vehicles within the ICS (the Interstate Council for Standardization, Metrology and Certification)

## Slide 13: Tasks to be solved in the course of the draft standard development
Taking into consideration in the test methods the development of automotive vehicles at an invariance of the fundamental test principles under GOST R 51616 (ISO 5128);
The establishment of new limiting values of admissible levels taking into account the development of automotive vehicles and gradualness of terms of their introduction within ICS;

## Slide 14: Test methods
Acceleration
Constant speed
Noise of the stationary vehicle (ventilation, engine noise, noise of pneumatic systems)
Basic test methods
The internal noise shall be measured under intense acceleration of the vehicle at a high gear. The maximum speed at the end of acceleration corresponding 0.9nnom doesn't exceed 120 km/h, as well as at constant speeds on the highest gear.

## Slide 15: Additions and refinements introduced into the methodology
The arrangement of microphones measurement points are more precisely defined. Requirements for arrangement and adjusting of seats are defined.
The procedure of noise measurement of the air expiration from pneumatic devices after their operation is specified.
Regulation of the heating system noise. Change is included following the increased responsibility connected with transportation of people, and also the existence of big number of noise sources (heaters, air conditioners).

## Slide 16: Additions and refinements introduced into the methodology (Noise measurement at the moment of acceleration)
Vehicles with manual gearbox having manual control and vehicles with automatic transmission with the possibility of forced gear selection.
For vehicles of М1, М2 and N categories, in case the speed at the end of acceleration (Vk) does not exceed 100 km/h, additional tests shall be conducted. Changes shall be introduced for full coverage of the most common driving modes peculiar to this vehicle category and for vehicles comparison in identical speed limits.
In case when the engine speed at the maximum power exceeds 6000 min-1, acceleration to the engine speed shall be applied corresponding to 80% of the engine speed at which the maximum engine power is declared, but not less than 5400 min-1.

## Slide 17: Additions and refinements introduced into the methodology (Noise measurement at the moment of acceleration)
Vehicles with automatic transmission with no possibility of forced gear selection.
The changes introduce more comprehensive and specific testing methodology, having a clear sequence of test actions, eliminating ambiguity and different interpretations of the vehicle mode.

## Slide 18
Additions and refinements introduced into the methodology (constant speed)
The drive mode for vehicles with automatic transmission is concretized.
The vehicle speed regime has been specified.

## Slide 19: New admissible levels
The admissible levels according to GOST R 51616 can be interpreted as maximum admissible. And they are technically achievable.
The proposed new levels are based on statistic data, obtained from processing of tests results of a large number of objects of various categories and also taking into account that rationing has to reflect the latest developments in automotive industry and to be the tool for competitive fight.
The proposed norms are more strict but not obligatory.

## Slide 20
Admissible levels of internal vehicle noise
(draft)
 | Vehicle | Admissible sound level, dB A | 
 |  | Before 1 January [2018 ] | After 1 January [2018 ]
1. | [Vehicles of М1 category with wagon-type or bonneted body layout] | 79 | 78
2. | Vehicles of М1 category except those provided in paragraph 1 | 77 | [76/73[1]]
 | For other vehicle categories – minus 1 dB after 1 January [ 2018] |  | 
[1] – [ vehicle’s length does not exceed 4.6 м, vehicle’s width does not exceed 1.7 м]

## Slide 21
Admissible levels of internal vehicles noise
(draft)
For (all-wheel drive) vehicles off-road capacity of [М1G] M2G, M3G, N1G, N2G and N3G categories the excess of admissible sound levels of no more than 1 dB A is allowed.
For vehicles of М1 category with technically admissible maximum weight up to 2 tones with power-to-rate ratio more than 75 kW/t in acceleration mode the excess of admissible sound levels of no more than 4 dB A is allowed.
For vehicles of М1 category with power-to-rate ratio more than [125] [number of seats is four or less and the R-point of less than 450 mm above the ground] the admissible sound levels are set only for testing mode at a constant speed.
In case if sound levels measured at the moment of acceleration exceed the admissible values provided in table 1, then these values shall be specified in vehicle operation manual.

## Slide 22: Statistics for internal noise levels Data before 2008 М1 category

## Slide 23: Statistics for internal noise levels Data from 2008 till 2013 М1 Category

## Slide 24: Statistics for internal noise levels Data before 2008 М1G category

## Slide 25: Statistics for internal noise levels Data from 2008 till 2013 М1G Category

## Slide 26: Conclusion
The admissible values for internal noise obligatory for application established by the Customs Union Technical regulation came into force from 01.01.2015 (Annex 3 paragraph 2)
GOST requirements are obligatory regarding testing methodology only (before the release of GOST ICS, GOST R 51616 as amended in 2009 is valid)

## Slide 27
Thank you for your attention!