## Slide 1: The trend of noise regulation in Japan
Ministry of Land, Infrastructure, Transport and Tourism
&
Japan Automobile Standards Internationalization Center
Transmitted by the expert from Japan
Informal document GRB-62-13-Rev.1
(62nd GRB, 1-3 September 2015,
agenda item 9)

## Slide 2: Measures for reducing vehicle noise
Flow of establishing vehicle noise regulation in Japan
Contents
Next vehicle noise regulation
    Vehicle noise regulation
    Tire noise regulation, etc.
Current vehicle noise regulation
Summary

## Slide 3: Flow of establishing vehicle noise regulation in Japan
ＷＴＯ
(World Trade Organization）
MOE
Permissible limit of automotive noise
The Announcement that Prescribes Details of Safety Regulations for Road Transport Vehicles
Report
Inform
Notice
Noise Regulation Act
Road Transport Vehicle Act
Enforcement of regulation
Comment
Consult
revision
revision
MLIT
CEC
CEC: Central Environment Council
MOE: Ministry of the Environment
MLIT: Ministry of Land, Infrastructure, Transport and Tourism

## Slide 4: Current vehicle noise regulation
3
Noise regulation value has been gradually strengthened.
Acceleration test
（ introduced in 1971）
Stationary test
（ introduced in 1986）
Transition of Acceleration noise regulation value on passenger cars
Constant speed test
（introduced in 1951）
* Constant speed test for motorcycles was abolished when UN-Regulation No.41 was introduced in Japan.
* Acceleration test for motorcycles was abolished and replaced by 'acceleration test' and 'ASEP ' when UN-Regulation No.41 was introduced in January 2014.
Chart: 
| 1971 | 1977 | 1979 | 1982 | 1998/1999
 | 84 | 82 | 81 | 78 | 76

## Slide 5: Next vehicle noise regulation
4
【 Outline of the Amendment 】
【Date of enforcement】
【 Scope 】
M and N category
● Constant speed test
● Acceleration test
( Full throttle acceleration)
● Stationary test
(Absolute value )
● Acceleration test
( Normal driving condition in urban traffic )
● Stationary test
* New Type Approval Vehicles : Measurement only
* In use car : Relative value
● Additional Sound Emission Provisions (ASEP)
Current regulations in Japan
Next regulation harmonizing with R51-03
 | Phase1 | Phase2
New Type Approval Vehicles （Except the import vehicle ） | ［1 October］ 2016 | ［1 September］ 2020 (N2 : 2022)
Other than above mentioned | Not applied | ［1 September］ 2022 (N2 : 2023)
● Compressed air noise（GVWR >2.8t）
※ “GVWR” means technically permissible maximum laden mass.
（● Constant speed test is not applied.）

## Slide 6: Next vehicle noise regulation
*2 GVWR ： Technically permissible maximum laden mass（t）
*3 Pn：Rated Maximum net power（kW）
【Regulation value】
Phase 3 has been designed in UNR51-03 on the assumption that review will be conducted if necessary.
（Same as UNR51-03)）
5
Japan will not adopt Phase 3 for the time being.
*1 PMR (Power to Mass Ratio) means following formula.
<Maximum output power (kw) / Mass of a vehicle in running order(kg))×1000>

## Slide 7: Next tire noise regulation
・Stud-less tires*
* Automobile which wear the following tires is out of scope.
M, N and O category
【 Scope 】
・Temporary use spare tires
・Tires designed for competitions
・Tires having a nominal rim diameter code ≦ 10 (or ≦ 254 mm) or ≧ 25 (or ≧ 635 mm)
・Tires with a speed rating less than 80 km/h
・Tires fitted with additional devices to improve traction properties (e.g. studded tires)
・Tires designed only to be fitted to vehicles registered for the first time before 1 October 1990.
・Professional off-road tires.
6
Category of vehicle | Date of enforcement | 
 | New Type Approval Vehicles (Except PHP Vehicle) | Other than above mentioned
M1 | 1 April 2018 | 1 April 2022
M2、N1、O1、O2 | 1 April 2019 | 1 April 2024
M3、N2、N3、O3、O4 | 1 April 2023 | 1 April 2026
【Date of enforcement】
・Tires intended to be fitted to road vehicles of categories other than M,N and O
・Tires conforming to Regulation No.75
*Japanese original tires which is designed to ensure the safety on both ice and snow

## Slide 8: Next tire noise regulation
Class of tire | MAX value(Stage 1) | MAX value(Stage 2)
C1 | 12.0 | 10.5
C2 | 10.5 | 9.0
C3 | 8.0 | 6.5
For "snow tire for use in severe snow conditions", the limits shall be increased by 1 N/kN. |  | 
Class of tire | Normal Section Width (mm) |  | Limit dB(Stage 2) | 
 |  |  | Other | Traction tires
C2 | Normal tire |  | 72 | 73
 |  | Snow tire | 72 | 73
 |  | Severe snow tire | 73 | 75
 | Special use tire |  | 74 | 75
C3 | Normal tire |  | 73 | 75
 |  | Snow tire | 73 | 75
 |  | Severe snow tire | 74 | 76
 | Special use tire |  | 75 | 77
Class of tire | Normal Section Width (mm) | Limit dB (Stage 2)
C1 | w≦185 | 70
 | 185＜w≦245 | 71
 | 245＜w≦275 | 72
 | 275＜w | 74
The above limits shall be increased by 1 dB(A) for "snow tyre for use in severe snow conditions", extra load tyres or reinforced tyres, or any combination of these classifications. |  | 
Tire noise
Rolling resistance
Unit: N/kN
（Same as UNR117）
（Same as UNR117）
Adopt the limit value of Stage 2
7
Adopt the limit value of Stage 2
【Regulation value】

## Slide 9: Next tire noise regulation
Wet grip
Category of use |  |  | Wet grip index(G) |  |  |  | 
 |  |  | C1 | C2（coming into force at October 2014） |  | C3（coming into force at October 2014） | 
 |  |  |  | Other | Traction tires | Other | Traction tires
Normal tire |  |  | ≧1.1 | ≧0.95 | ≧0.85 | ≧0.80 | ≧0.65
Snow tire |  |  | ≧1.1 | ≧0.95 | ≧0.85 | ≧0.65 | ≧0.65
 | Severe snow tire | with a speed symbol ("R" and above, including "H") indicating a maximum permissible speed greater than 160 km/h | ≧1.0 | ≧0.85 | ≧0.85 | ≧0.65 | ≧0.65
 |  | with a speed symbol ("Q" or below excluding "H") indicating a maximum permissible speed not greater than 160 km/h | ≧0.9 |  |  |  | 
Special use tire |  |  |  | ≧0.85 | ≧0.85 | ≧0.65 | ≧0.65
（ Same as UNR117）
8
【Regulation value】

## Slide 10: Summary
9
Schedule of enforcement of R117-02 in Japan
・Period of Public Comment: From 31 July 2015 to 4 September 2015
・Publication and Enforcement of the revision of the Safety Regulations for Road Transport Vehicles on the same day: 8 October 2015 (tbd)
Schedule of enforcement of R51-03 in Japan
・Period of Public Comment: December 2015 (tbd)
・Publication and Enforcement of the revision of the Safety Regulations for Road Transport Vehicles on the same day: March 2016 (tbd)
Japanese contribution to the GRB activities for the future
Japan will participate positively in the GRB activities as ever, considering the issues discussed in GRB such as the limit values for R51-03 Phase 3.

## Slide 11
Thanks for your attention !
Ministry of Land, Infrastructure, Transport and Tourism
&
Japan Automobile Standards Internationalization Center