## Slide 1: Proposal for amendments to UN R16: Mandatory fitting of safety-belt reminder
Informal document GRSP-57-24
(57th GRSP, 18-22 May 2015
Agenda item 7)
Submitted by the expert from EC, Japan and Korea
Notes: <number>

## Slide 2
Background
The safety-belt usage rate in Korea stands at about 85% for front seats,
but the rate is 19% for rear seats.
But, European countries are high. (IRTAD,2013)
IRTAD, 2013
Proposal 56th session of GRSP:
The mandatory installation of the Safety-belt Reminder is extended to the rear seat.
Generally, vehicle penetration rate in many Asia countries is lower than European countries,
and we presume that the occupancy rate of vehicle is higher than European countries.
Safety-belt usage rate is generally low in many countries of Asia and we need to improve the safety-belt
usage rate by the mandatory installation of the Safety-belt Reminder
Country | Belt wearing rate, front seats | Belt wearing rate, rear seats
France | 98% | 84%
Germany | 98% | 98%
UK | 95% | 89%
Korea | 85% | 19%
Notes: For your background information,
At the last GRSP in December, Korea proposed that the mandatory installation of the safety belt reminder be extended to the rear seats.
The basic logic was that unlike advanced European nations where the occupancy rate is low for rear seats and safety-belt usage rate is high, developing countries including Korea has very low safety-belt usage rate while more people are likely to occupy the rear seats in those countries.
And considering the role of setting the international standards which we hope that would be harmonized by countries around the world, we hope that the UN Regulation could reflect those needs.
And now with the support from my colleagues in Japan and European Commission, we propose to expand the coverage scope of SBR for rear seats as well as front seats.
<number>

## Slide 3
Occupancy rate of passenger car rear seat in Korea
Occupancy rate of passenger car seat (2015)
 | Front passenger seat | Rear passenger seats
Average | 30.9% | 14.8%
Week days | 25.5% | 11.1%
Weekend | 43.5% | 23.3%
Highways | 39.6% | 21.1%
Local roads | 25.1% | 10.6%
Rear seat occupancy rate is about 0.5 times to front passenger seat.
The occupancy rate of weekend and highways is higher.
Notes: According to a research done early this year, the average occupancy rate is 31% for front passenger seat and 15% for rear seats in Korea.
<number>

## Slide 4
Use rate of safety-belt in Korea
Usage rate of passenger car safety-belt (2015)
 | Driver seat | Front passenger seat | Rear seats
Average | 89.0% | 73.1% | 18.9%
Week days | 88.0% | 70.7% | 17.6%
Weekend | 91.1% | 76.4% | 20.4%
Highways | 93.1% | 75.7% | 16.2%
Local roads | 85.0% | 66.3% | 22.5%
Usage rate of rear seat safety-belt is about 0.2 times to front seat.
In highways, safety-belt usage rate for rear seat is the lowest while front safety-belt use is the highest.
Notes: It is also turned out that four out of five rear seat passengers do not wear safety-belts in Korea.
<number>

## Slide 5
 | The number of fatalities [people] | The number of the injured [people]
Front driver seats | 195 | 2,364
Front passenger seats | 57 (18%) | 2,266 (12%)
Rear passenger seats | 58 (19%) | 13,585 (75%)
Total | 310 | 18,215
Casualty of safety-belt non-users in Korea (2013)
Casualty of safety-belt non-use in Korea
The injured rate of safety-belt non-users on rear seat is 75% of total injured safety-belt non-users.
The fatality rate of safety-belt non-users on rear seat is 19% of total fatalities safety-belt non-users.
It is presumed that the injury rate of unbelted rear seat passenger is higher than the injury rate of unbelted
front driver and passenger.
Notes: The table at the top shows the number of fatalities and injuries of unfastened passengers for each type of seats.
The safety-belt non-users in rear seats accounted for 75% of injuries and 19% of fatalities of all safety-belt non-users.
This means that, after some adjustment of numbers, the injury rate of unbelted rear seat passenger is higher than the rate of unbelted front driver and passenger.
<number>

## Slide 6
Effectiveness of safety-belts in preventing injuries
 |  | belted | unbelted
Male (50%ile) on front passenger seat | Head injury risk (%) | 1.2% | 4.5%
 | Chest injury risk (%) | 5.4% | 97.7% (18 times)
Female (5%ile) on rear seat | Head injury risk (%) | 1.1% | 94.8% (86 times)
 | Chest injury risk (%) | 5.1% | 2.0%
Effectiveness of safety-belts in Korea
Test vehicle was a type of M2 (comprising12 seats in addition to the driver’s seat).
Test vehicle was crashed into road structures which made by concrete in velocity 80km/h.
Test was performed by KATRI on November, 2014.
The chest injury risk of unbelted male dummy on front passenger seat is about 18 times to belted dummy.
The head injury risk of unbelted female dummy on rear seat is about 86 times to belted dummy.
The combined injury risk of unbelted male dummy on front passenger seat is about 14 times to belted dummy.
The combined injury risk of unbelted female dummy on rear seat is about 16 times to belted dummy.
Notes: This slide shows the result of a test done in KATRI.
An M2 vehicle with passengers running at 80KPH were crashed with a concrete structure at an oblique angle.
The combined injury risk of front unbelted male increased to 14 times compared to belted dummy and the combined injury risk of unbelted female dummy on rear seat increased about 16 times the case of belted dummy.
<number>

## Slide 7
Cases of belted/unbelted passenger accident
18. April. 2015, Rollover accident
Middle school student drove his father’s car illegally.
This driver was only lightly injured thanks to safety-belt.
03. April. 2015, Rollover accident
School bus met with a rollover accident.
Among 12 children and 3 adults involved in the accident, nobody was seriously injured or dead thanks to safety-belt
28. April. 2015, Rear-end accident
There were a rear-end accident involving three buses.
22 belted passengers were only lightly injured thanks to safety-belt
Amongst 28 unbelted passengers, 1 person was dead and the others were injured seriously
03. Sep. 2014, Rollover accident
The safety-belted driver was injured, but two unbelted persons of accident car passengers were dead (one of them was ejected).
Effectiveness of safety-belts in Korea
Notes: These are accident cases that emphasize the importance of safety-belts.
At the left one at the bottom, the number of lightly injured belted casualties clearly contrasts with the fatality and serious injury of unbelted casualties.
<number>

## Slide 8
 | Use | Non use | Comparison
Front passenger seats | 0.15% | 2.97% | 19.8 times
Rear passenger seats | 0.13% | 0.58% | 4.5 times
 | Driver’s seats | Passenger seats | 
 |  | Front | Rear
Highways | 99.4% | 97.9% | 68.2%
Local roads | 98.0% | 93.9% | 35.1%
The number of deaths
The total number of deaths, sever injuries and injuries
*1 Fatality rates =
 | Non use | If they used seat belts… | 
Front passenger seats | 60 | 60 / 19.8 = | 3 (-57)
Rear passenger seats | 119 | 119 / 4.5 = | 26 (-93)
Seat belt use rates in Japan (2013)
2. Effects of seat-belt use to reduce fatalities
Fatality rates(*1) of seat belt users/non users in Japan (2013)
(2) The number of fatalities not using seat belts in Japan (2013)
57 + 93 = 150 people are annually expected to be saved
<number>
Effects resulted by mandatory implementation of seat belt reminder in Japan
Notes: This slide was provided by the courtesy of Japan.
The Safety-belt usage rate for rear seats was only 35% on local roads, much lower than 94% for the front passenger seats.
The table in the middle shows that the fatality rate of unbelted front passenger seats is almost 20 times the rate of belted front passenger, and the rate of unbelted rear seats is 4.5 times the rate of belted rear seats.
Taking into account of those numbers, the number of fatalities not using seat belts in Japan, which is 179, would have been reduced to 29 with 150 people staying alive if they had used safety belts.
<number>

## Slide 9
<number>
The cost benefit by mandatory implementation of seat belt reminder by EC
2. Monetised value and break-even costs per vehicle and per seat for EU28 casualties
influenced by action scenario (Mid estimate: 2015-2025)
※2 Assuming average number of seats is 30
Estimated number of EU28 casualties that would be influenced by action scenario
(Mid estimate: 2015-2025)
<number>
Notes: More systemic approach was done by the European Commission.
According to the cost benefic study of mandatory implementation of seat belt reminder, it was proved to be cost-effective for SBR for all seats except for the rear seat passenger in M1 vehicle.
<number>

## Slide 10
Proposal
 | M1 | M2 | M3 | N1 | N2 | N3
Driver's seat | Yes | Yes | Yes | Yes | Yes | Yes
Front passenger seat | Yes | Yes | Yes | Yes | Yes | Yes
Rear seat | Yes | － | － | Yes | － | －
Applicable categories
Requirements for safety-belt reminder
 | Driver’s seat | Front passenger seat | Rear seat
Not fastened with ignition on | Visual warning | Visual warning | Visual warning
Not fastened with the vehicle in motion | Visual and audible warning | Visual and audible warning | Visual and audible warning (only when any belt which was fastened before the vehicle started is unfastened)
Notes: This is the overall summary of our proposal.
We propose that driver and front passenger seats for all M and N vehicles and the rear seats of only M1 and N1 vehicles be fitted with SBR.
The first level of visual warning would be given when the safety belt is unlatched with ignition on. While the second level of visual and audible warning is given when the safety belt is unlatched or becomes unlatched with the vehicle in normal operation. For rear seats, the second level of warning only applies when any belt which was fastened before the vehicle started becomes unfastened.
<number>

## Slide 11
Test procedures
No safety-belt fastened in
any seat
Turn on ignition
Check visual warning for
every seat
(for [30s] on front seats,
for [60s] on rear seats)
Level 1 (Visual warning)
Level 2 (Visual and audible warning)
Drive the vehicle in accordance with the
driving conditions
(before 25km/h, 500m, 60s)
Safety-belt not fastened in the driver’s seat; Fasten safety-belts in seats other than the
driver’s seat
(1-1) Test for the driver’s seat
Safety-belt not fastened in the front
passenger seat; Fasten safety-belts in
seats other than the front passenger seat
Drive the vehicle in accordance with the driving conditions
(before 25km/h, 500m, 60s)
(2-1) Test for the front passenger seat
Drive the vehicle in accordance with the
driving conditions
(more than 25km/h, 500m, 60s)
Safety-belt fastened in the driver’s seat;
Fasten safety-belts in seats other than the
driver’s seat
(1-2) Test for the driver’s seat
Unbuckle driver‘s safety-belt
(2-2) Test for the front passenger seat
Drive the vehicle in accordance with the
driving conditions
(more than 25km/h, 500m, 60s)
Safety-belt fastened in the driver’s seat;
Fasten safety-belts in seats other than the
driver’s seat
Unbuckle front passenger’s safety-belt
Check visual and audible warning
for the driver’s seat
(warning interval [10s]
within a [60s] timeframe)
Check visual and audible warning
for the front passenger seat
(warning interval [10s]
within a [60s] timeframe)
Check visual and audible warning
for the front passenger seat
(warning interval [10s]
within a [60s] timeframe)
Check visual and audible warning
for the driver’s seat
(warning interval [10s]
within a [60s] timeframe)
Notes: This is the simplified test procedures for first and second level of SBR.
The left side shows the procedure for level 1, which applies to all seats. The right side is the test procedure for level 2 for driver and front passenger seats.
<number>

## Slide 12
Test procedures
Drive the vehicle in accordance with the
driving conditions
(more than 25km/h, 500m, 60s)
Check visual and audible warning
for the rear seats
(Visual and audible warning,
warning interval [10s]
within a [60s] timeframe )
Safety-belt fastened in the rear passenger
seats; Fasten safety-belts in seats other than
the rear passenger seats
Unbuckle each rear passenger’s
safety-belt
(3) Test for the rear seat (to be conducted for all rear seats)
Level 2 (Visual warning, or visual and audible warning)
Notes: And here it shows the level 2 test procedure for rear seats.
I would like to conclude my presentation, and pending your questions, our proposal to amendment to UN Regulation 16 would be followed by my Japanese colleagues.
<number>