## Slide 1: Toxicology and Flammability Requirements in Child Restraint Systems Regulations in UN R44 and UN R129
57th Session GRSP – Geneva 18 22/05/2015
Informal document GRSP-57-26
(57th GRSP, 18-22 May 2015
Agenda item 10)

## Slide 2: From Regulation No. 44 - Rev.3 - Child Restraint Systems (E/ECE/TRANS/505/Rev.1/Add.43/Rev.3)
6.1.5. The child restraint manufacturer has to declare in written form that the toxicity of materials used in the manufacture of restraint systems and accessible to the restrained child is in conformity with the relevant parts of EN 71:2009, part 3. Tests confirming the validity of the declaration may be carried out at the discretion of the test authority. This paragraph does not apply to restraint devices of groups II and III."
6.1.6. The child restraint manufacturer has to declare in written form that the flammability of materials used to manufacture the restraint system is in conformity with the relevant parts of EN 71:2009 part 2. Tests confirming the validity of the declaration may be carried out at the discretion of the test authority."
Session 1/2015, 24-25 February 2015
<number>
Toxicology
Flammability

## Slide 3: R129 provisions already adopted vs R44 Toxicology
6.1.5. The child restraint manufacturer has to declare in written form that the toxicity of materials used in the manufacture of restraint systems and accessible to the restrained child is in conformity with the relevant parts of EN 71:2009, part 3. Tests confirming the validity of the declaration may be carried out at the discretion of the test authority. This paragraph does not apply to restraint devices of groups II and III."
6.3.1.1. The Child Restraint System manufacturer shall declare in writing that the toxicity of materials used in the manufacture of restraint systems and accessible to the restrained child is in conformity with the relevant parts of EN 71-3:1994/A1:2000/AC. Tests confirming the validity of the declaration may be carried out at the discretion of the test authority..
Session 1/2015, 24-25 February 2015
<number>
Toxicology- R44
Toxicology – R129

## Slide 4: R129 provisions already adopted vs R44 Flammability
6.1.6. The child restraint manufacturer has to declare in written form that the flammability of materials used to manufacture the restraint system is in conformity with the relevant parts of EN 71:2009 part 2. Tests confirming the validity of the declaration may be carried out at the discretion of the test authority."
6.3.1.2. The Child Restraint System manufacturer shall declare in writing that the flammability of materials used to manufacture the restraint system is in conformity with the relevant paragraphs of EN 71-2:2011. Tests confirming the validity of the declaration may be carried out at the discretion of the Technical Service.
Session 1/2015, 24-25 February 2015
<number>
Flammability R44
Flammability R129

## Slide 5: RATIONALE
EN 71 2 and 3 contain various requirements for various materials
  Need to specify the most appropriate materials that will cover those utilised in CRSs
Need to define which of part of EN 71 -2 and 3 we are refering to ?
  Test Method
  Criteria
Chemical Substances – Other reg requirements & consumer testing
Clepa proposition derived from EN 71
Different references to EN 71-3 and EN 71-2 in R44 and R129 => Need to align !
<number>
Session 1/2015, 24-25 February 2015

## Slide 6: Defining The Appropriate Material EN 71-3: 2013
<number>

## Slide 7: EN 71-3 : 2013 – Migrations Limits for heavy metals & other materials
<number>

## Slide 8: REACH Regulation
<number>
Substances Of Very High Concern - 161 subtances
  Moving demands each year
 | Name | EC Number | CAS Number | Date of inclusion | Reason for inclusion | Decision number | IUCLID 5 Substance Dataset
1 | Bis (2-ethylhexyl)phthalate (DEHP) | 204-211-0 | 117-81-7 | 2014/12/17; 2008/10/28 | Equivalent level of concern having probable serious effects to the environment (Article 57 f); Toxic for reproduction (article 57c) | ED/108/2014 | 
 |  |  |  |  |  | ED/67/2008 | 
2 | 2-(2H-benzotriazol-2-yl)-4,6-ditertpentylphenol (UV-328) | 247-384-8 | 25973-55-1 | 17/12/2014 | PBT (Article 57 d); vPvB (Article 57 e) | ED/108/2014 | 
3 | 2-benzotriazol-2-yl-4,6-di-tert-butylphenol (UV-320) | 223-346-6 | 3846-71-7 | 17/12/2014 | PBT (Article 57 d); vPvB (Article 57 e) | ED/108/2014 | 
4 | 2-ethylhexyl 10-ethyl-4,4-dioctyl-7-oxo-8-oxa-3,5-dithia-4-stannatetradecanoate (DOTE) | 239-622-4 | 15571-58-1 | 17/12/2014 | Toxic for reproduction (Article 57 c) | ED/108/2014 | 
5 | Cadmium fluoride | 232-222-0 | 7790-79-6 | 17/12/2014 | Carcinogenic (Article 57 a); Mutagenic (Article 57 b); Toxic for reproduction (Article 57 c); Equivalent level of concern having probable serious effects to human health (Article 57 f) | ED/108/2014 | 

## Slide 9: Toxicity – 2015 EU Consumer Testing Protocol
<number>
PAH substances
Phthalate plasticisers
Organic tin and phenolic compounds
Formaldehyde
Flame retardants , phosphatic and brominated
Heavy metals

## Slide 10: How to deal with flammability
Add flame retardant to the material that is in contact with the child
But flame retardant may involve substances that
  are or will be judged dangerous to child safety
  That do not fulfil REACH requirements and or EN 71-2 requirements
  That do not fulfil consumer testing existing and new demands
<number>

## Slide 11: EN 71-3 : 2013 – Test Method
<number>

## Slide 12: EN 71-2:2011-09 Test Method
5.4 Test relating to flowing elements of toys to be worn on the head (except those covered
by 4.2.2 and 4.2.3), hoods, head-dresses, etc. and masks not covered by 4.2.4 which partially
or fully cover the head (e.g. fabric and cardboard masks, eye masks, face masks), toy
disguise costumes and toys intended to be entered or worn by a child (see A.9)

## Slide 13: EN 71-2:2011-09 Requirement
4.3 Toy disguise costumes and toys intended to be worn by a child in play (see A.5)
These include, for example, cowboy suits, nurses’ outfits and long flowing capes not attached to headwear
covered by 4.2.5.
When tested in accordance with 5.4, the rate of spread of flame of the test sample shall not exceed 30 mm/s
or the test sample shall self-extinguish.

## Slide 14
<number>
Session 1/2015, 24-25 February 2015
TRANS/WP29./78/REV 3
REFERING TO R 34 & R118
Clepa Proposition
Rate of flame : Moved From 200 mm/min to 100 mm/min in § 6.2.1.
Sample orientation : Horizontal
Rate of flame : Moved to 30 mm/s : 1800 mm/min
Sample orientation : 45°

## Slide 15: TRANS/WP29./78/REV 3 REFERING TO R 34 & R118
R118
  Scope :
    1.1. This Regulation applies to the burning behaviour (ignitibility, burning rate and melting behaviour) of interior materials used in vehicles of categories M3, Classes II and III 1/, carrying more than 22 passengers, not being designed for standing passengers and urban use (city buses).
Session 1/2015, 24-25 February 2015
5

## Slide 16: Clepa proposition ECE/TRANS/WP.29/GRSP/2015/6 Toxicity
"6.1.5. The child restraint manufacturer has to declare in written form that the toxicity of materials used in the manufacture of restraint systems and accessible to the restrained child is in conformity with the relevant parts of EN 71:2009, part 3. Tests confirming the validity of the declaration may be carried out at the discretion of the test authority. This paragraph does not apply to restraint devices of groups II and III.
6.1.5 The Child Restraint System manufacturer shall declare in writing that the toxicity of materials used in the manufacture of restraint systems and accessible to the restrained child is in conformity with the relevant parts of EN 71-3:2013 (paragraph 4.2., Table 2, Category III for specific requirements and paragraph 7.3.3. for test methodology). Tests confirming the validity of the declaration may be carried out at the discretion of the Technical Service. This paragraph does not apply to restraint devices of groups II and III."
<number>

## Slide 17: Clepa proposition ECE/TRANS/WP.29/GRSP/2015/6 Flammability
"6.1.6. The child restraint manufacturer has to declare in written form that the flammability of materials used to manufacture the restraint system is in conformity with the parts of EN 71:2009 part 2. Tests confirming the validity of the declaration may be carried out at the discretion of the test authority.
The Child Restraint System manufacturer shall declare in writing that the flammability of materials used to manufacture the Child Restraint System is in conformity with the method of section 5.4 of EN 71-2:2011+A1:2014 with a maximum rate of spread of flame of 30 mm/s. Tests confirming the validity of the declaration may be carried out at the discretion of the Technical Service. Where fabrics are assembled together, these shall be tested as a composite."
<number>

## Slide 18
Comparing R118 & Clepa Proposition
Using existings parts that in contact with the child
Various manufacturers have tested fabrics , energy absorbing elements , harness components includiing EPS , Polyester , , Polyamid, Coton , PU , and composite
Manufacturer | Sample | Flamme retardant | Regulation 118 |  | Test EN 71-2 2011 +A1: 04/2014 §5.4
 |  |  | Burning rate mm/min | Burning rate mm/sec | Burning rate mm/sec
A | 1 | No | 118 /Self Extinguishing | 2.0 Self Extinguishing | 2,2
A | 2 | yes | Do Not Ignite | Do Not Ignite | Do Not Ignite
A | 3 | yes | Self extinguishing | Self extinguishing | 29,9
A | 4 | no | 86,8 | 1,4 | 3,2
A | 5 | yes | Do Not Ignite | Do Not Ignite | 1,1
A | 6 | yes | Do Not Ignite | Do Not Ignite | 7,5
A | 7 | no | 54,4 | 0,9 | 19,0
A | 8 | yes | Do Not Ignite | Do Not Ignite | 6,5
B | 9 | No | 43 | 0,7 | 17,05
B | 10 | No | 140 | 2,3 | 13,74
B | 11 | Yes | 0 | 0,0 | ignited but extinguished
B | 12 | No | 78 | 1,3 | 11,42
B | 13 | No | 0 | 0,0 | 7,91
B | 14 | No | 180 | 3,0 | 11,72
B | 15 | No | 138,6 | 2,3 | 7,73
B | 16 | No | 152 | 2,5 | 9,43
C | 17 | Yes | 4,8 | 0,1 | 0
C | 18 | Yes | 8,9 | 0,1 | 90
Close
More demanding
Above limits

## Slide 19: CONCLUSIONS
For child safety need to balance flammability requirements with those related to toxicity
Important to refer to EN 71 regulation as it deals with intems in contact with child
Important also to define exactly which testing methods and corresponding criteria
Need to align both R129 and R44
Clepa is asking GRSP to consider its proposition in light of these explanatory notes