## Slide 1: Analysis of Glare given to oncoming vehicles by Motorcycles DRLs at Night - Based on Actual State of Motorcycles DRLs -
20 June 2016
National Traffic Safety and Environment Laboratory
Transmitted by the expert from Japan
Informal document No. GRE-76-03
(76th GRE, 25-28 October 2016
agenda item 7 (e))

## Slide 2
Analysis Background
Reevaluate effects concerning the glare at night caused by Motorcycles DRLs suitable for the actual state by numerical analysis.
* Japan proposed that headlamps of motorcycles equipped with optional daytime running lamps (DRLs) shall automatically be switched ON at night based on “Research on Daytime Running Lamps of Motorcycles (Informal Document No. GRE-75-09)” at the 75th session of GRE.
* The following comments were provided for our research by some experts in the last session.
- Installation height of motorcycle DRL is high, compared to the actual state.
- Luminous intensity of motorcycle DRL is high, compared to the actual state.

## Slide 3: A numerical analysis was performed to evaluate effects of motorcycle DRL glare to oncoming vehicle driver, depending on its lighting condition at night. Model formula of Schmidt-Clausen and Bindels (1), which is often used to calculate De Boer rating scale was used for this analysis. Glare evaluation rating W = 5.0  2logΣ (E/((1 + (Lh/Cpl)0.5) θ0.46Cpoo) ) (1) E: Illuminance at driver’s eyes (lx) Lh: Driver’s adaptation luminance (cd/m2) θ: Angle between driver’s line of sight and direction of the lamp Cpl: 4.0 × 10-2 (cd/m2) Cpoo: 3.0 × 10-3 (lx･min-0.46)
Analysis Method
If the glare evaluation rating “W” is below 4, it follows that the glare exceeding allowable limit is caused.

## Slide 4: * Sky illuminance: 0lx (Night) * Road luminance: 0.1 cd/m2 (equivalent to the road illumination of urban streets with a little traffic) * Driver’s line of sight: Direction of traveling * Vehicle positions: See the right figure. *Eye-point height of vehicle driver:1.2m *Lamps specifications : as the following table
Analysis Condition
The above condition for this numerical analysis was set based on “Research on Daytime Running Lamps of Motorcycles (Informal Document No. GRE-75-09)”.
 | DRL | Low Beam
Number of lamps | 2 | 1
Interval of lamps | 40cm | 
Installation height | 0.6m to 1.2m | 0.87m
Maximum luminous intensity | 600cd or 1,200cd | 9800cd
Light distribution patterns | Based on UN-R87 | Based on UN-R113
(assuming that vehicles pass each other on a two-way street)
In this analysis, “Maximum luminous intensity” and “Installation height” of the motorcycle DRL was varied.

## Slide 5: Figure: Effect of motorcycle DRL on the oncoming vehicle driver at night
Analysis Results
When DRLs are on at night, glare exceeding the allowable limit (glare evaluation rating < 4) occurs to the oncoming vehicle driver regardless of the DRL installation height.
Installation height of the DRL has little influence on glare evaluation ratings.
Glare evaluation rating of DRL ( DRL central luminous intensity : 1200 cd)
Distance (in the direction of travel) between motorcycle and oncoming vehicle (m)
Glare evaluation ratings
Imperceptible
Tolerable
Satisfactory
Disturbing
Intolerable
Distance (m)
Evaluation rating
Glare !
Installation height 0.6 m

## Slide 6: Figure: Effect of motorcycle DRL on the oncoming vehicle driver at night
Analysis Results
Even when the DRL central luminous intensity is 600 cd, glare exceeding the allowable limit (glare evaluation rating < 4) occurs to the oncoming vehicle driver.
Glare evaluation ratings
Distance (in the direction of travel) between motorcycle and oncoming vehicle (m)
Imperceptible
Satisfactory
Tolerable
Disturbing
Intolerable
Evaluation rating
Distance (m)
Installation height of the DRL has little influence on glare evaluation ratings.
Glare !
Glare evaluation rating of DRL ( DRL central luminous intensity : 600 cd)
Installation height 0.6 m

## Slide 7: Glare exceeding the allowable limit (glare evaluation rating < 4) occurs to the oncoming vehicle driver, even when the motorcycles DRLs is suitable for the actual state.
Conclusion
Motorcycles DRLs need to be securely switched to Low Beam at night.