## Slide 1: Night demonstration: H4 Halogen Reflector headlamp versus representative LED headlamp
Geneva, 26.10.2016
Dr. Rainer Neumann
GTB Document No.CE-5360
Transmitted by the expert from GTB | Informal Document No. GRE-76-25 (76th GRE, 25-28 October 2016, agenda item 7 (f))

## Slide 2: LED Headlamps : Advantages
Low energy consumption
Reduced CO2
Effective solutions also with small sized headlamps
Long life time
Flexibility in styling solutions keeping safe light output
Colour temperature leads to a well accepted light by consumers
GTB Document No.CE-5360

## Slide 3: Proposal for Future Halogen & LED Headlamps
Intention: Target to demand a good light pattern on the road rather than requiring a certain number of lumens emitted by the light source
Introduction of a performance based requirement alternatively to the exisiting 1000 lm objective luminous flux for LED and halogen light sources
Take into account the given state of the art globally
GTB Document No.CE-5360

## Slide 4: New Performance Proposal for LED Headlamps
-30 deg
-15 deg
+30 deg
+1 deg
-3.5 deg
Zone A >= 400lm
Zone B >= 200lm
GTB Document No.CE-5360

## Slide 5: Mounting Height (h), Inclination (alfa), distance (x)
Alfa
h
x
GTB Document No.CE-5360

## Slide 6
Headlamp mounting height [cm] | Ray inclination [deg] | Distance on the road [m]
85 | 0.57 | 85.4
 | 2.50 | 19.5
 | 3.50 | 13.9
 | 5.00 | 9.7
Headlamp mounting height [cm] | Ray inclination [deg] | Distance on the road [m]
65 | 0.57 | 65.3
 | 2.50 | 14.9
 | 3.50 | 10.6
 | 5.00 | 7.4
Page 6
GTB Document No.CE-5360

## Slide 7
Representative LED Headlamp (out of 60) , 513 lm total luminous flux
GTB Document No.CE-5360

## Slide 8: Reflector Headlamp H4 , 155mm diameter , 467 lm
GTB Document No.CE-5360

## Slide 9: Photometric Results
Representative LED Headlamp :
total luminous flux : 513 lm
Zone A : 511 lm
Zone B : 327 lm
Reflector H4 Headlamp, 155mm diameter :
total luminous flux: 467 lm
Zone A : 445 lm
Zone B : 206 lm
GTB Document No.CE-5360

## Slide 10: Reflector Headlamp H4 , 155mm diameter , 467 lm
GTB Document No.CE-5360

## Slide 11: Reflector Headlamp H4 , 155mm diameter, 400 lm
GTB Document No.CE-5360

## Slide 12: Reflector Headlamp H4 , 155mm diameter, 300 lm
GTB Document No.CE-5360

## Slide 13: Reflector Headlamp H4 , 155mm diameter, 200lm
GTB Document No.CE-5360

## Slide 14: Reflector Headlamp H4 , 155mm diameter, 100lm
GTB Document No.CE-5360

## Slide 15
Comparison: different 400lm light distributions
GTB Document No.CE-5360

## Slide 16
Comparison: different 400lm light distributions
GTB Document No.CE-5360

## Slide 17
Comparison: different 400lm light distributions
GTB Document No.CE-5360

## Slide 18
Comparison: different 400lm light distributions
GTB Document No.CE-5360

## Slide 19
Comparison: H4 light distributions
GTB Document No.CE-5360

## Slide 20
Comparison: balanced LED light distribution
GTB Document No.CE-5360

## Slide 21
Comparison: H4 light distributions
GTB Document No.CE-5360

## Slide 22
Comparison: balanced LED light distribution
GTB Document No.CE-5360