Proposal for Supplement 12 to the 04 series of amendments to Regulation No. 44 (Child Restraint Systems)

Submitted by the expert from Consumers International

The text reproduced below was prepared by the expert from Consumers International. It introduces an amendment to UN Regulation No. 44 (Child Restraint System (CRS)). It is based on informal documents GRSP-58-9 and GRSP-58-10 distributed at the fifty-eighth session of the Working Party on Passive Safety (GRSP) (ECE/TRANS/WP.29/GRSP/58 para. 35) and supersedes ECE/TRANS/WP.29/GRSP/2016/11. The modifications to the existing text of the UN Regulation are marked in bold for new or strikethrough for deleted characters.

I.	Proposal

Paragraph 6.1.3., amend to read:

"6.1.3.	According to the category which it belongs to, the child restraint shall be secured to the vehicle structure or to the seat structure.

# Possible configurations for approval

# Groups / categories table

| Group category | Universal (1) | Semi-universal (2) | Restricted | Specific vehicle |
| --- | --- | --- | --- | --- |
|  | CRS | ISOFIXCRS | CRS | ISOFIXCRS | CRS | ISOFIXCRS | CRS | ISOFIXCRS |
| 0 | Carry-cot | A | NA | A | A(3) | A | NA | A | A(3) |
|  | Rearward facing | A | NA | A | A (3) | A | NA | A | A(3) |
| 0+ | Rearward facing | A | NA | A | A(3) | A | NA | A | A(3) |
| I | Rearward facing | A | NA | A | A(3) | A | NA | A | A(3) |
|  | Forward facing (integral) | A | A (3) | A | A(3) | A | NA | A | A(3) |
|  | Forward facing (non-integral) | NA | NA | NA | NA | NA | NA | NA | NA |
|  | Forward facing (non-integral – see paragraph 6.1.12.) | A | NA | A | NA | A | NA | A | A(3) |
| II | Rearward facing | A | NA | A | NA | A | NA | A | A |
|  | Forward facing (integral) | A | NA | A | NA | A | NA | A | A |
|  | Forward facing (non integral) | A | NA | A | NA | A | NA | A | A |
| III | Rearward facing | A | NA | A | NA | A | NA | A | A |
|  | Forward facing (integral) | A | NA | A | NA | A | NA | A | A |
|  | Forward facing (non integral) | A | NA | A | NA | A | NA | A | A |
| With: CRS: Child restraint system A: Applicable NA: Not Applicable ______________________ (1) ISOFIX universal CRS means forward facing restraints for use in vehicles with positions equipped with ISOFIX anchorages system and a top tether anchorage. (2) ISOFIX semi universal CRS means: Forward facing restraints equipped with support leg or Rearward facing restraints equipped with a support leg or a top tether strap for use in vehicles with positions equipped with ISOFIX anchorages system and a top tether anchorage if needed Or rearward facing restraints, supported by the vehicle dashboard, for use in the front passenger seat equipped with ISOFIX anchorages system, Or lateral facing position restraint equipped if needed with an anti-rotation device for use in vehicles with positions equipped with ISOFIX anchorages system and top tether anchorage if needed. (3) New approvals and extensions will be granted in accordance with paragraphs 17.16 and 17.17. |

"

Insert new paragraphs 17.16. and 17.17., to read:

“17.16.  	As from [1 September 2017], no new approvals shall be granted under this Regulation to integral class child restraint systems of groups 0, 0+ and 1 that are equipped with ‘ISOFIX attachments’ (as specified in paragraph 6.3.2 of this regulation), unless they form part of a multi-group child restraint system that will also be approved for group 2 and above.

17.17. 	As from [1 September 2020], no extensions shall be granted under this Regulation to integral class child restraint systems of groups 0, 0+ and I that are equipped with ‘ISOFIX attachments’ (as specified in paragraph 6.3.2 of this Regulation), unless they form part of a multi-group child restraint system that is also approved for group II and above.

II.	Justification

1.	Phase 1 of UN Regulation No. 129 (integral Isofix CRS) entered into force on 9 July 2013.  At that stage the intention was to finalise Phase 2 (non-integral CRS) and phase 3 (belted CRS), and phase out UN Regulation No. 44 (no new type approvals) once all phases had entered into force (see also GRSP-52-17).

2.	The change of plans in 2015, involving a new approach for Phase 2 and leaving finalisation of Phase 3 (and maybe even a Phase 4) open-ended, permits the opportunity to approve new integral CRS with Isofix connections according to U Regulation No. 44 for an undefined period.

3.	CI considers undesirable that CRS manufacturers are still allowed to start developing new products according to UN Regulation No. 44 for an undefined period, resulting in:

(a)	Two categories of products offering two levels of protection that can be introduced on the market (UN Regulation No. 44: no side impact required, forward facing installation allowed as of 9kg);

(b)	Confusion amongst consumers (mass based vs stature based);

(c)	Less encouragement for manufacturers to develop products to the latest standard.

4.	Until today 43 Contracting Parties to the 1958 Agreement have signed UN Regulations Nos. 44 and 52 to UN Regulation No. 129. There are no Contracting Parties that signed only UN Regulation No. 44 without signing UN Regulation No. 129. So there is no risk that newly developed Isofix integral CRS be withheld from certain markets.

5.	Therefore CI proposes that no new UN Regulation No. 44 approvals will be granted to Isofix integral CRS as of [16 November 2016], and that transitional provisions will be amended accordingly.