## Slide 1
Pedestrian Safety Research
in Japan
59th GRSP
9th-13th May 2016
MLIT / NTSEL
Informal document GRSP59-21
(59th GRSP May 9-13, 2016,
Agenda item 22(a))
Submitted by the expert from Japan

## Slide 2
Macro Traffic Accident Study
Traffic accident fatalities by mode
Effects of the pedestrian safety standard
Accident data
Macro accident data from 2012 to 2013
Fatal pedestrian accidents
M1 category vehicles
Compliant/non-compliant with the pedestrian safety standard
Pedestrians accounted for the largest proportion of traffic accident fatalities.
Pedestrian safety standard is effective in reducing the fatalities by traffic accidents .
*From a document of the 3rd vehicle safety meeting for FY2014 conducted by MLIT
4,373 persons in 2013
32.4%
1,415
6.7%
295
13.7%
600
10.6%
465
36.2%
1,584
Vehicle
Motorcycle
Small motorcycle
Bicycle
Pedestrian
Others
(From a document published by the National Police Agency in 2013)
0.0%
0.5%
1.0%
1.5%
2.0%
2.5%
3.0%
3.5%
Fatality rate
Compliant
Non-compliant
Accident data
Macro accident data for 2013
Fatal accidents

## Slide 3
Macro Traffic Accident Study
42% of pedestrian fatal accidents occurred at 40 km/h or below.
Of the fatal accidents that occurred at under 40km/h , 51% accounted for the cases that the head/face were the most injured body regions.
In 55% of the above said fatal accidents, the head/face were hit by vehicle externals.
Travel speed of the vehicle
Most injured
body region
Accident data
Macro accident data for 2008-2012
Pedestrian fatal accidents
Passenger cars (mini vehicles, sedans, mini vans) compliant with the pedestrian safety standard
There is a potential to reduce pedestrian fatalities by further improving vehicles’ pedestrian safety.
What struck head/face

## Slide 4
Micro Traffic Accident Study
Adult headform test area in R127
O：Striking area of the vehicle in accidents with AIS2+ head injury in the micro accident survey
Outside of the test area in R127
*From a report on results of detailed traffic accident research and analysis through medicine-engineering collaboration for vehicle safety in 2013 conducted by MLIT
Accident data
Micro accident data from 1993 to 2012
Pedestrian accidents with AIS2+ head injury
Passenger cars and trucks with bonnet
Accidents excluding children aged 10 or younger /below 140 cm in height
Striking area | No. of cases | Proportion
Hood | 15 | 21 %
A-pillar periphery | 23 | 32 %
Lower wind shield glass frame periphery | 24 | 34 %
Upper wind shield glass frame periphery | 2 | 6 %
Wind shield glass | 6 | 9 %
Fender | 1 | 1 %
Total | 71 | 100 %
Lower wind shield glass frame and A-pillar peripheries are the major areas that struck head in pedestrian accidents with AIS 2+ head injury.
-> Many were outside of the test areas in pedestrian safety standard.
Child headform test area in R127

## Slide 5
Pedestrian Head Protection Tests
We conducted the pedestrian head protection tests in which the impactor was hit at the center of the A-pillar (worst-case condition).
We conducted the tests according to the R127 specifications except for the test area.
The tested vehicle was compliant with the pedestrian safety standard.
Several tests were conducted with the same vehicle (results from the second , third, and all subsequent trials might have been affected by the preceding tests).

## Slide 6
Test Results
HIC was above the threshold in all A-pillar tests
In J-NCAP test result of the same vehicle, HIC was below the threshold in all test areas.
A-pillar lower
A-pillar center
A-pillar upper
0
1000
2000
3000
4000
5000
6000
7000
8000
9000
Center right
Upper right
Lower right
Center left
Upper left
Lower left
HIC
0
1000
2000
3000
4000
5000
6000
7000
8000
9000
Test
1
Test
2
Test
3
Test
4
Test
5
Test
6
Test
7
Test
8

## Slide 7
Pedestrian Head Protection Tests
We conducted the pedestrian head protection tests in which the impactor was hit at the center of the A-pillar (worst-case condition).
We conducted the tests according to the R127 specifications except for the test area.
The vehicle was equipped with a pedestrian airbag.
Tests were conducted with/without the airbag.
The pedestrian airbag was forcibly deployed at the timing when its performance was sufficient.

## Slide 8
With the pedestrian airbag, HIC was far below the threshold.
Without the airbag, HIC was far above the threshold.
->The pedestrian airbag is effective in protecting the pedestrian’s head in a collision, potentially reducing the number of fatal pedestrian accidents.
Effects of Pedestrian Airbag
With pedestrian airbag
Without pedestrian airbag
0
1000
2000
3000
4000
5000
6000
7000
8000
9000
With airbag
Without airbag
HIC 15
Pedestrian protection standard threshold

## Slide 9
Summary
In recent fatal traffic accidents in Japan, pedestrians account for the largest proportion.
According to the macro accident study from 2012 to 2013 in Japan, fatality rate of pedestrian accidents with vehicles compliant with the pedestrian safety standard was lower than that with non-compliant vehicles.
According to the macro accident study from 2008 to 2012 in Japan , among pedestrian accidents involving passenger cars such as sedans, minivans, and mini vehicles compliant with the pedestrian safety standard, 42% of pedestrian fatal accidents occurred at 40 km/h or below. Of the fatal accidents that occurred at under 40km/h , 51% accounted for the cases that the head/face were the most injured body regions. In 55% of the above said fatal accidents, the head/face were hit by vehicle externals.

## Slide 10
Summary
According to the micro accident study from 1993 to 2012 in Japan, in the traffic accidents between an adult pedestrian and a vehicle with bonnet resulting in AIS2+ head injury, 66% were cases in which the pedestrian’s head was impacted by the A-pillar or the lower front wind shield glass frame peripheries, which were both outside of the test area in R127.
In the pedestrian head impact test cases using the one vehicle model compliant with the pedestrian safety standard, HIC of the tests impacted at the A-pillar was higher than those at the test area in R127.
In the pedestrian head impact test case using the one vehicle model equipped with a pedestrian airbag, the pedestrian airbag was effective in reducing the head injury when the head was impacted with the A-pillar.