## Slide 1
Reporting on new technologies and the way forward
© AC.nl
Directorate-General for Internal Market, Industry, Entrepreneurship and SMEs
Automotive and Mobility Industries Unit
Status of the review of the General Safety and Pedestrian Safety Regulations
60th session of GRSP – 14/12/2017
Submitted by expert from EC | Informal document GRSP-60-21 (60th GRSP, 13-16 December 2016, agenda item 27(a))

## Slide 2: Regulation (EC) No 661/2009
Main type-approval requirements for the General Safety of motor vehicles, trailers, components and separate technical units.
Contains detailed implementing measures that are EU or UNECE Regulations for defined vehicle categories
Phase-in mostly completed since 11/2014.
  Electrical Safety, Electronic Stability Control, Advanced Emergency Braking on trucks and buses, Tyre Pressure Monitoring, Driver Safety-Belt Reminder, ISOFIX, …

## Slide 3: Regulation (EC) No 78/2009
Pedestrian Safety Requirements, child/adult headform impacts on bonnet, as well as legform impact on front bumper.
Based on old Directive 2003/102/EC, but with more stringent requirements and mandatory Brake Assist System (BAS).
Still being phased in, specifically for heavy M1 passenger cars (SUVs) and N1 light commercial vehicles (vans) since 2011 to 2019.

## Slide 4: Reporting obligations on safety
General Safety and Pedestrian Safety Regulations require to report to the European Parliament and the Council on progress in the safety field.
Including monitoring and assessment of new advanced safety features, their cost effectiveness and feasibility for possible inclusion in a future revision of the regulations on general vehicle safety and on the protection of pedestrians and other vulnerable road users.

## Slide 5: What we have done for the reporting
Commission has undertaken a preliminary study with TRL (published March 2015):
  Review of possible considerations for legislation.
  New safety features that meet CARS 2020 criteria and the Road Safety 2011-2020 policy orientations.
  Indicative cost-benefits analysis of 55 possible measures that could be introduced in the EU
Outcome was 'short list' for GSR and PSR reporting and thus the way forward in the EU.

## Slide 6: General Safety Regulation Reporting on the Way Forward
Instead of identifying safety problem in the field and working towards a solution, list of available and feasible measures was assessed.
List of measures has been limited to those that are most likely to be cost effective.
In depth cost effectiveness and impact on competitiveness is being checked at this moment, as the basis for Impact Assessment.
Stakeholder engagements, public consultations.

## Slide 7: Stakeholders that have been consulted (from 2014 onwards)
ACEA / OICA (car industry)
CLEPA (supplier industry)
FIA (motorist interests)
ETSC (transport safety)
Euro NCAP (consumer testing)
Transport & Environment
Transport for London
…
Member States / Contracting Parties

## Slide 8: 19 Measures included in the Report
Autonomous Emergency Braking
Emergency Braking Display
Intelligent Speed Adaptation
Lane Keeping Assist
Driver Distraction/Drowsiness Monitoring
Safety-Belt Reminder (all seats)
Frontal Impact Crash Updates
Side Impact Crash Updates
Rear Impact Crash Introduction
Alcohol Interlock Device Installation
Crash Event Data Recorder
Tyre Pressure Monitoring
Truck Front End Design Program
Truck Rear Underrun Protection
Truck Lateral Protection
Bus Fire Safety Program
Pedestrian/Cyclist Detection
Head impact on A-pillar/windscreen
Reversing Detection

## Slide 9: Combined Key Active Safety Measures – 1/9/2020
Automatic Emergency Braking System
  M1, N1
Lane Keep Assistance
  M1, N1
Driver Drowsiness and Distraction Monitoring
  M, N
Intelligent Speed Adaptation
  M, N
For new vehicles: Plus 2-year period

## Slide 10: Focus on AEBS
Automatic Emergency Braking System
For new types of vehicle:
1/9/2020 moving obstacle
1/9/2022 stationary obstacle
1/9/2024 pedestrian detection
1/9/2026 cyclist detection
For new vehicles: Plus 2-year period
N1 (non M1 derived) vehicles: 2-year offset

## Slide 11: Further Focus on Pedestrian Safety
Automatic Emergency Braking System
For new types of vehicle:
1/9/2024 pedestrian detection
1/9/2026 cyclist detection
For new vehicles: Plus 2-year period
N1 (non M1 derived) vehicles: 2-year offset

## Slide 12: General Safety Measures – 1/9/2020
Safety Belt Reminders
  M1, N1 – on all seats / M2, M3, N2, N3 – front seats only
Emergency Braking Display
  M, N
Alcohol Interlock Devices Interface
  M, N
Crash Event Data Recorder
  M1, N1
Tyre Pressure Monitoring
  M, N, O3, O4
For new vehicles: Plus 2-year period

## Slide 13: General Safety Measures – 1/9/2020
Frontal Crash Program Update
  M1, N1
Side Crash Program Update
  M1, N1
Rear Crash Testing Introduction
  M1, N1
For new vehicles: Plus 2-year period

## Slide 14: Truck, trailer and Bus specific – 1/9/2020
Front End Blind Spot Cameras and Detection
  M2, M3, N2, N3
Upgrading Lateral Protection (elimination of exemptions)
  N2, N3, O3, O4
Upgrading Rear Underrun Protection
  N2, N3, O3, O4
Upgrading Front Underrun Protection
  N2, N3
Fire Safety for Buses
  M2, M3
For new vehicles: Plus 2-year period

## Slide 15: Pedestrian Safety – 1/9/2020
Reversing camera/detection
  M, N, O3, O4
For new vehicles: Plus 2-year period

## Slide 16: Pedestrian Safety M1, N1 – 1/9/2024
Automatic Emergency Braking System
  Pedestrian detection
  Cyclist detection (note: from 1/9/2026)
A-Pillar and Windscreen Head Impact Test
For new vehicles: Plus 2-year period
N1 (non M1 derived): 2-year offset

## Slide 17: Truck and Bus Front End Design – 1/9/2028
Direct Vision Requirements
  M2, M3, N2, N3
Facilitation through DG MOVE's Maximum Authorised Weights and Dimensions Directive (EU) 2015/719 amending 96/53/EC
For new types of vehicle only

## Slide 18: General Safety Regulation Revision Future Commission Proposal
Proposal for revision is to follow mid-2017.
To contain the measures identified to be cost effective.
Process to be started once implications of the Impact Assessment are clear.
Again, stakeholder engagements, public consultations, etc.
After Commission adoption, to be discussed in the European Parliament and the Council.

## Slide 19: Way forward of the General Safety and Pedestrian Safety Regulations
Currently carrying out an in depth cost and effectiveness analysis, forming the basis for Impact Assessment for Commission Proposal to amend GSR and PSR, expected mid-2017.
Looking at combining/bundling technologies (while not double counting costs and benefits).
Assessing the impact on competitiveness.
Stakeholder consultations are ongoing (event was 28-29/11 in London, now individually).

## Slide 20: Status of the Commission Report
Saving Lives: Boosting Car Safety in the EU
Reporting on the monitoring and assessment of advanced vehicle safety features, their cost effectiveness and feasibility for the review of the regulations on general vehicle safety and on the protection of pedestrians and other vulnerable road users
Adopted by the European Commission on 12/12/2017.
http://ec.europa.eu/growth/tools-databases/newsroom/cf/itemdetail.cfm?item_id=9029

## Slide 21: For further information
http://ec.europa.eu/growth/sectors/automotive
Status of EU legislation, links to Regulations and other useful information.
https://circabc.europa.eu/w/browse/b2bc6bdb-7e39-48cd-9f16-079703cd82e6
Studies carried out by the Automotive and Mobility industries unit of DG GROW

## Slide 22: European Commission Directorate-General for Internal Market, Industry, Entrepreneurship and SMEs Automotive and Mobility Industries Unit
Thanks for your attention