## Slide 1: Overview of CATC Development
MIIT, China
2017.06
Informal document WP.29-172-21 172nd WP.29, 20-23 June 2017
Agenda item 6
Notes: <number>

## Slide 2: Background
With the rapid increasing of automotive industry and vehicle parc, the transportation status changed significantly in China.
NEDC, the currently-used type approval cycle, is inconsistence with the characteristics of the actual driving condition in China, and the fuel consumption gaps between lab/real are becoming larger.
Current regulations can’t accurately evaluate the new techs, i.e. the technologies for new energy vehicles.
<number>
Notes: 中国逐渐成为汽车大国，但是目前能耗和排放的相关法规试用的都是欧洲的NEDC工况，这与我国实际行驶特征不符，而且差异越来越大。基于该工况得到的测试评价结果，与车辆在实际使用中的性能，也是有较大偏差的。与此同时，国六排放标准的制定以及新能源车等新技术的评价，都需要使用更合适的工况。中国汽车工业由大到强，开发中国工况的呼声也越来越高。
In China, the driving cycle in current standard is inconsistence with the characteristics of the actual driving condition in China and the differences become larger and larger. And the current regulations can’t accurately evaluate new technology, such like technologies for new energy vehicle. Meanwhile, CHINA 6 is under development and which test cycle should be applied is also under discussion. There are increasingly loud calls for developing China test driving cycle.
Based on these backgrounds, CATC was issued by Ministry of Industry and Information Technology and co-managed by Ministry of Industry and Information Technology, Ministry of Finance, Ministry of Environmental Protection, Standardization Administration and Chinese Academy of Engineering. China Automobile Technology & Research Center was entrusted to organize specialists for a three-year deep research.
<number>

## Slide 3: Targets
China Automotive Testing Cycle (CATC) program was lauched by MIIT and other related ministries of China. CATARC led the this 3-year program with hundreds of researchers from 50+ Univ./Ins./OEM.
Main Targets:
  Develop the testing cycle for fuel consumption/emission
    National/regional CLTC (light-duty) and CHTC (heavy-duty), including new energy vehicles
  Research and evaluate the test procedure
<number>
Notes: 基于这样的行业共识，在多年的筹划和准备之后，于2015年3月份，由工信部下达，联合财政部、国标委、环保部和中国工程院共同管理，启动了该中国工况的项目。并委托中国汽车技术研究中心牵头，组织行业专家，展开为期三年的深入研究和开发。项目包括两大研究目标，一是开发能耗/排放法规检测工况，包括全国的以及典型城市和典型区域的轻型、中重型汽车工况。也包括新技术的评价工况的开发。第二个目标是修订基于新工况的汽车能耗/排放测试标准。
There are two project targets. The first is to develop the test driving cycle for energy consumption and emission testing standard. The driving cycle for light and heavy duty vehicle, national and typical city should be developed. The second target is to develop and revise the energy consumption and emission test standard based on the new developed driving cycle.
<number>

## Slide 4
Development Roadmap
In-use driving behaviour data
low-frequency traffic volumes data
Data
acquisition
Develop the
reference database
CATC building
Compare short trip combination and the reference database
Weighting factor matrix development and data classification
Notes: 轻重型车的工况构建过程基于欧洲WLTC工况开发的研究基础，但车辆类型和采集规模更大，并且引入了基于地理信息技术的城市低频出行大数据，用以进行城市权重和速度区间权重的设定。工况开发总的来说包括四个步骤：试验规划、数据采集、工况构建和工况验证。通过科学的试验规划，能够保证数据采集工作可以覆盖到各种典型的城市、道路、时段、车辆和驾驶员的类型，确保工况能够代表中国的统一情况。工况曲线开发出来，通过工况验证去调整和修改，并最终完成定型。
The development of test cycle includes four steps: test planning, data collection, cycle development and cycle validation.
In test planning, the selection schemes of cities, route, periods of time, vehicle and drivers are confirmed by survey. Based on those schemes, data collection is carried out. Through scientific planning, it is ensured that data collected can represent the united situation of China.
Data collection includes two parts: the one is the collection of vehicle operating data. This is realized through collecting real-time data by data acquisition equipment on vehicles. However, due to the limit of objective condition, the areas in collection have certain individuality. So the other one is to collect the traffic characteristics and obtain vehicle flow distribution in different areas. Thus, it can be converted to weight factors of areas. Then in the process of developing cycle, the contribution percentage of different data is adjusted by those weight factors.
In cycle developing, first we will preprocess the driving data, such as deleting the mistake data, filtering and so on, and code every piece of data according to the area, the types of automobiles and the driving time. Than the data will be divided into short-trips and idle sections. Then the statistical and distribution characteristics of short-trips and idle sections will be calculated. In order to construct driving cycle including the features of different speed ranges, the short-trips will be divided into 3 classes: low speed, medium speed and high speed. The method of PCA ( principal component analysis ) and cluster analysis is used for this classification. The characteristic database will be weighing calculated with the regional weighing factors, and then the unified speed-acceleration distribution can be obtained. After this, we can determine the quantity and the duration of the segments in the cycle by a certain rule. And the suitable segments will be selected to make all possible combinations. By comparing the chi-squared value between the distribution of segments and the unified distribution, the combination with the smallest chi-squared value will be chosen as the cycle.
After the cycle validation, we can finally obtain the CATC.
<number>

## Slide 5
Vehicle Selection
<number>
Notes: 这是轻型车的具体选择方案。
These are the detail plan of light-duty vehicle selection.
<number>

## Slide 6
Vehicle Selection (cont’d)
<number>
Notes: 这是重型车的具体选择方案。
These are the detail plan of heavy-duty vehicle selection.
<number>

## Slide 7
3900 vehicles, 27 million km
Data Collection
<number>
3082(LD total) and 1059 (NEV, 34%)
908(HD total) and 110 (NEV, 12%)
Notes: 截至2017年5月，累计收集了623个不同轻型、重型车型、3900余辆常规车辆、新能源车辆，总里程达2700万公里，包含22个参数，如车辆速度、油耗、电耗、发动机动力总成、新能源车电池电机、环境信息等数据，这也是迄今为止全球的规模最大的、范围最广、参数最多的工况开发数据库。
里程比例方面，轻型车行驶了约1500万公里，重型车900万公里，新能源车180万公里。
<number>

## Slide 8
Idle Ratio
Average Speed
Feature Analysis
<number>
Notes: <number>

## Slide 9
Speed distribution (LS)
Speed distribution (MS)
Speed distribution (HS)
Feature Analysis (Cont’d)
Speed distribution (total)
<number>
LS: ≦60
MS:60-80
HS:≧80
Notes: <number>

## Slide 10
Big traffic data collection (every 5 mins in 41 cities) from GIS
Split into 3 speed phases: low/mid/high
LS
MS
HS
LS
MS
HS
Total
Total
City
Weight Factor
<number>
Notes: <number>

## Slide 11
Compare CATC data characteristic with other big traffic data, i.e. Didi, AMAP and Baidu.
The speed of CATC is in line with China's reality.
Average speed of different data base
Average speed in different cities
Data Validation
<number>
Notes: 为了说明CATC采集数据的合理性和有效性，以平均车速这一主要交通特征为例，与网络交通大数据（滴滴出行、高德交通）和百度GIS交通量大数据（GIS）进行对比。结果显示，无论是在各城市的平均车速比较，还是在全国综合平均车速比较，CATC与它们都较为接近且居中，反映了CATC符合中国实际！
<number>

## Slide 12
CATC Curve
<number>
Notes: 项目组采用了改进了的工况构建方法，完成工况曲线绘制。轻型车工况曲线已基本完成定型，主要包括乘用车和轻型商用车，其中核心的乘用车工况已完成3.1版的定型，工况分为低速、中速和高速区间，分别对应城市、城郊和高速运行。总时长1800秒，最大速度114km/h，平均速度29.0 km/h。
<number>

## Slide 13
Speed distribution
Index | Collected data采集数据 | Collected data weighted by GIS results GIS加权后 | NEDC | FTP75 | WLTC | CLTC
Ave. speed 平均速度(km/h) | 26.47 | 29.88 | 33.6 | 33.9 | 46.4 | 28.97
 |  |  | 43.5 | 40.9 | 53.2 | 37.19
Ave. acc.平均加速度（m/s2） | 0.48 | 0.48 | 0.53 | 0.62 | 0.53 | 0.45
Ave. dec.平均减速度（m/s2） | -0.53 | -0.53 | -0.75 | -0.71 | -0.58 | -0.5
RPA相对正加速度（m/s2） | 0.18 | 0.17 | 0.11 | 0.17 | 0.15 | 0.17
Acc. Ratio 加速比例(%) | 27.74 | 29.14 | 23.2 | 31.1 | 30.9 | 28.67
Dec. ratio 减速比例(%) | 25.53 | 26.40 | 16.6 | 27.1 | 28.6 | 26.39
Cruise ratio匀速比例(%) | 21.35 | 22.41 | 37.5 | 24.7 | 27.8 | 22.83
Idling ratio怠速比例(%) | 25.38 | 22.05 | 22.6 | 17.2 | 12.7 | 22.11
Cycle Comparison of CLTC(P)
<number>
Notes: 中国工况采集的数据符合实际，基于实采数据开发的CATC相比于其他的工况，也更加符合实际。从工况技术特征比较的一些典型结果看，
在平均速度方面，CATC轻型车工况与实际采集数据吻合度最高，其它法规工况的车速明显高于中国实际车速。
在加速度、减速、匀速和怠速比例分布方面，CATC轻型车工况与实际采集数据吻合度最高，NEDC、FTP75和WLTC工况与实际偏差度较大。这样的差异，将直接反映到油耗和排放测试结果中，对法规工况结果与实际结果的差异产生关键影响。
<number>

## Slide 14
Cycle Validation
Operability Validation
1# ICEV
2# BEV
Turbo
charged
>3.0L
Impact of Cycle:
Tests among CATC/WLTC/NEDC
<number>
Notes: <number>

## Slide 15
Validation and final design of CATC
Impacts of the fuel consumption limits and policies in terms of the new CATC
Discussion of the CATC application in both fuel consumption and emission standards
Future Plan
<number>
Notes: <number>

## Slide 16
Thanks!
<number>
Notes: <number>