## Slide 1
Reversing Alarm
KOTSA (Korea Transportation Safety Authority)
KATRI (Korea Automobile Testing & Research Institute)
Park Jinwoo, Chief Researcher
(truehelp@ts2020.kr)
Transmitted by the expert from the Republic of Korea
Informal document GRB-65-19
(65th GRB, 15-17 February 2017,
agenda item 2)

## Slide 2
Accidents due to reversing
Accident video

## Slide 3
Accidents due to reversing (2010~2012)
Chart: Age
| 65 years or older | under 65 years old
 | 0.744 | 0.256
Chart: fatalities
| Pedestrian | Vehicle
 | 0.787 | 0.213
Who was involved in the accident and dead?

## Slide 4
Which vehicles involved in accidents
Accidents due to reversing (2010~2012)
Chart: Fatalities in all traffic accident
| M1 | N | M2&3 | others
 | 0.5 | 0.22 | 0.08 | 0.2
Chart: Fatalities by reversing
| M1 | N | M2&M3 | others
 | 0.3 | 0.56 | 0.06 | 0.08

## Slide 5
Place of accident due to reversing
Chart: Accident subject
Chart: Place of accident caused by reversing
| Residential area | shared road | Backward moving | Others
 | 0.241 | 0.241 | 0.103 | 0.415
Accidents due to reversing (2010~2012)
General fatal accidents occurred mainly in the evening but the deaths by reversing accidents occurred mainly during daytime rather than night time.

## Slide 6
Reversing alarm in KMVSS
The vehicles(N3, Van, Box truck, school bus) shall have rear view camera or rear detecting sensor(Alarm signal for driver) or reversing alarm device when it move to backward.
Reversing alarm regulation in Korea
N3 & Van
Box type
School bus

## Slide 7
Conclusion
Proposal
Scope : Include N2, M2, School bus, Box-type truck besides N3 and M3.(If it is possible, include N1 also)
Pause switch : prohibited.
In case of school-bus, the vehicle should have both rear view camera and reversing alarm for preventing accident of children.
Microphone height : One point(ex : 1.2m)
  Reversing alarm sound is beep sound not continuous sound, so it is not easy to find the maximum or minimum sound between 0.5m and 1.5m.

## Slide 8
Thank you!