## Slide 1: 74th UNECE GRPE session
PMP IWG Progress Report
UNITED NATIONS
Informal document GRPE-74-17
74th GRPE, 9-13 January 2017
Agenda item 7

## Slide 2: PMP meetings in 2016
13th January 2016 (Geneva) : 38th PMP meeting
9th-10th March 2016 (Brussels) : 39th PMP meeting
27th April – 3rd May (Web/phone conference): 40th meeting
31st May (Web/phone conference)
12th-13th October (JRC-Ispra) : 41st meeting
NEXT MEETING: 15th – 16th March 2017
(Meeting rooms booked in Ispra)

## Slide 3: EXHAUST PARTICLE EMISSIONS

## Slide 4: Main open points
Round Robin Sub-23nm
Raw exhaust sampling
Round Robin PNC (Particle Number Counter)
Horizon 2020 projects

## Slide 5
Key messages
        Sub-23 nm exhaust particles:
          There are particles <23nm - Sometimes they are an artifact
          Particle not counted with the current PMP method: GDIs 30-40%, motorcycles (2-s engines)up to >200%, PFIs 50-100%, DPFs 5%.
          High emitters are still detected by PMP23nm - Thus not critical yet for current engine technologies to which the PN limit is applicable
          Measuring particles down to 10 nm appears possible with “limited” changes to the existing methodology

## Slide 6
New mandate / ToR
        The PMP groups has submitted to GRPE in June 2016 an updated draft version of the ToR and request a new mandate with a new specific concrete objective:
        Sub 23 nm exhaust particles:
          Demonstrate the feasibility to measure sub23nm particles with the existing PMP methodology with appropriate modifications and assess measurement differences/uncertainties by means of a round robin (RR)
        The objectives of the proposed RR have been further discussed in the October meeting considering also new available information on new research projects
        A new document describing the RR scope and objectives has been prepared and it will be uploaded on the PMP website
        The details of the RR will be discussed during the next face-to-face meeting

## Slide 7: Scope of the Round Robin
Development of a sub23nm (cut-off size: 10 nm) particle number measurement procedure based on the existing PMP methodology conveniently adapted.
Main purpose: Monitoring particle emissions of new engine/after-treatment technologies.
Assessment of the repeatability/reproducibility of the proposed particle counting methodology by means of a “round robin”.
Demonstrate feasibility to measure sub23nm
Examine the need of a catalytic stripper (CS)
Confirm the draft requirements and calibration procedures of sub23nm protocol
Evaluate measurement differences/uncertainties
Evaluate sub23nm fraction of modern engines

## Slide 8: Objectives of the Round Robin
1. Identify the modifications to the existing measurement equipment
Expected Result: The main objective is to identify the modifications to the equipment/procedure needed to measure from 10 nm and to determine whether existing systems can (or cannot) be adjusted during an annual maintenance with a relatively low cost.
2. Assess the need of a catalytic stripper (CS)
3. Evaluate sub23nm fraction of modern engines
Expected result: The fraction (percentage) of sub-23 nm particles from latest engines will be reported.

## Slide 9: Objectives of the Round Robin
4. Evaluate measurement differences/ uncertainties. Confirm the specification of the modified systems
Expected result: The measurement uncertainty will be reported based on the RR-10 and it will be related to the technical specifications of the systems that will circulate. The need of better systems (or not) will be discussed.
5. Calibration procedures of sub23nm protocol.
6. NEW: Check measurement uncertainty of existing PMP-23nm systems.
7. NEW: Check differences between tailpipe and CVS
Expected result: The uncertainty of the ‘location’ will be quantified, especially for 10 nm systems.

## Slide 10: Investigation of sub23nm protocol
One system with CS and 10nm CPC to circulate
Each lab PMP system plus a 10nm CPC (to circulate?)
One golden vehicle
Different labs will test different engine technologies

## Slide 11: PN Counting from Raw Exhaust via Fixed Dilution
        Interest in this approach confirmed by some engine manufacturers and some instrument manufacturers
        01 Series of amendments to Reg. 132 already includes such possibility but the procedure is not defined
        First analysis of potential benefits/issues presented during the last meetings
        Correlation with other methods (CVS and partial flow system) and advantages/disadvantages to be checked – Additional data required

## Slide 12: Raw exhaust (tailpipe) sampling
Experimental program
  Primary dilution
  Losses
  Volatile removal efficiency
  Pressure effects
  Time alignment
JRC will wait for experimental data
Limited number of tests carried out at JRC in the context of PN-PEMS for HD program

## Slide 13: Experimental setup (JRC)
Not engine test bed
Euro VI vehicles
Low (thermophoretic) losses due to position of PMP_TP
EFM uncertainty <5%

## Slide 14: Raw exhaust sampling
Preliminary results show 20% differences
Input from others is necessary
Theoretical investigation of uncertainty
(According to recent information industry will try to generate some more data)

## Slide 15: PNC Calibration Round Robin
Confirm that the k factor can be included in the final counting efficiencies
Investigate the possibility to change the calibration material
Applicability to PN-PEMS procedures
Investigate the possibility to calibrate at 10 nm

## Slide 16: Participants presentations during 41st PMP meeting
BMW – AVL – VW
Available on the PMP website
Final results could be available for the next face-to-face meeting

## Slide 17: HORIZON 2020
Participants presentations
  DownToTen
  PEMS4nano
  SUREAL-23

## Slide 18: HORIZON 2020 projects
Topic | DownToTen | PEMS4nano | SUREAL-23
Objective | Instrumentation | Fuel efficient G-DI engine | Instrumentation + vehicle testing
Size [nm] | >5-10 | >10 | >1
Technology | tbd | CPC | tbd
Prototype | 2018 | 2019 Jan | 2018 start
Testing | many | Single cylinder and other | Super Low Emission Vehicles
 |  | Validation of instrument | Prototype limited availability to others
PMP link | Important | Medium | Important

## Slide 19: NON-EXHAUST PARTICLE EMISSIONS Steps for Building a Common Method for Measuring Brake Wear Particles

## Slide 20
Step 1 - Selection/development of a braking test cycle
WLTP Database Analysis (Concluded – Report published by JRC)
Comparison of WLTP data with Existing Industrial Cycles (Concluded – Results presented at the 41st PMP meeting)
Development of a first version of a New Braking Cycle (Deadline: June 2017 – On-going work by a dedicated Task Force)
Task Force is coordinated by JRC but includes the main experts from industry – phone conferences are regularly held (4 so far) – progress report to be presented at the next meeting
Testing and Validation of the New Cycle - Possible round robin (January 2018)

## Slide 21
Step 2 - Selection of the most suitable sampling method
Comparison of existing systems/test rig configurations (Deadline: June 2017 – On-going work by the group)
Selection of Functional Parameters (Deadline: June 2017 – On-going work by the group)
Selection of Testing Parameters (Deadline: January 2018)
Testing and Validation of the Selected Configuration (Deadline: To be defined depending on the progress)

## Slide 22
Step 3 - Selection of the most suitable methodology for BW Particles Measurement and Characterization
Comparison of Existing Methodologies (Deadline: June 2017 – Work postponed due to prioritization of steps 1 and 2)
Selection of the most suitable methodologies based on the selected sampling configuration (Deadline: June 2018)
Testing and Validation of the Selected Methodologies (Deadline: To be defined depending on the progress)
Data processing method (Deadline: To be defined)

## Slide 23: Stay in touch
JRC Science Hub: ec.europa.eu/jrc
Twitter and Facebook:
@EU_ScienceHub
LinkedIn:
european-commission-joint-research-centre
YouTube:
JRC Audiovisuals
Vimeo:
Science@EC