## Slide 1: Informal Working Group ACSF ACSF of Category C
www.bmvi.de
Informal document GRRF-85-06
85th GRRF, 11 December 2017
Agenda item 2

## Slide 2: Activities of the IWG ACSF
3 meetings for ACSF of category C since the 84th session of GRRF
24th Oct. 2017 Meeting in Solihull, UK
(only Contracting Parties)
17th Nov. 2017 Webex Conference
22nd – 24th Nov. 2017 IWG ACSF Meeting in Bonn, GER

## Slide 3: Activities of the IWG ACSF
Following major issues have been solved within the IWG ACSF:
reaction time value
  minimum distance (Srear)
  minimum operation speed (Vsmin)
  critical situation (Scritical)
Test target (L3e vehicle)
Type approval test requirements

## Slide 4: a) reaction time value
www.bmvi.de

## Slide 5: a) reaction time value - State of discussion
Already in 84th session of GRRF the IWG had a fundamental consensus regarding the principles of
  minimum distance (Srear)
  minimum operation speed (Vsmin)
  critical situation (Scritical)
The remaining discussion points were:
  When will the reaction of the driver in the rear vehicle start
  (somewhere between activation of the direction indicators and
  the start of the lane change manoeuvre)?
  Which reaction time component value shall be take into the calculation (0.4 or 1.2 s after start of the lane change manoeuvre)?

## Slide 6: a) reaction time value - Simulation on test track done by BASt
Braking starts 0.4 s after start of LCM with 3 m/s²
Remaining safety gap = 1 s
VACSF = 80 km/h
Vrear = 130 km/h
S ~ 60m (Scritical)

## Slide 7: a) reaction time value - continuous lateral movement
The driver in the rear vehicle can see the flashing direction indicators of the ACSF car at least 3 s before the start of the lane change manoeuvre
The IWG ACSF came to the conclusion, that the lateral movement of the ACSF car to the lane marking in combination with the flashing direction indicators is a clear signal to the driver in the rear vehicle that the ACSF vehicle will change the lane
To have a clear visible lateral movement it is important, that the ACSF vehicle is not already driving closed to the lane marking at the beginning of the lane change procedure
Therefore requirements for a continuous lateral movement and lane centering were added

## Slide 8: a) reaction time value - continuous lateral movement
new § 5.6.4.6.4.
The lateral movement of the vehicle towards the intended lane shall not start earlier
than 1 s after the start of the lane change procedure. Additionally the lateral movement
to approach the lane marking and the lateral movement necessary to complete the lane
change manoeuvre, shall be completed as one continuous movement.
new § 5.6.4.1.2.
When the ACSF of Cat. C is activated (stand by) the system shall aim to center the
vehicle in the lane. […]
max. 5 s
min. 1 s
3 - 5 s
One continuous movement,
lateral acceleration max. 1 m/s²,

## Slide 9: a) reaction time value - continuous lateral movement
appr.1 – 2 s
total reaction time
0.4 s
The mandatory continuous lateral movement achieves that we have a total reaction time of at least 1.4 s, which is comparable to the AEBS reaction time (approximately 1 – 2 s before LCM + 0.4 s after LCM).

## Slide 10: a) reaction time value - conclusion
In summary the IWG ACSF came to the conclusion that due to the mandatory continuous lateral movement a value of 0.4 s as the reaction time component after the lane change manoeuvre has started is a reasonable value.
0.4 s shall be used in the formula as tB

## Slide 11: b) Test target (L3e vehicle)
www.bmvi.de

## Slide 12: b) Test target (L3e vehicle) - continuous lateral movement
Sensor performance shall be tested at the worst case scenario, which is a motorcycle (L3e) coming from the rear
Unfortunately no standardized test target for L3e vehicle is available
IWG ACSF agreed to following solution:
new Annex 8, § 3.5.5.1
For the approaching vehicle in the test a type approved high volume
series production L3 motorcycle with an engine capacity not
exceeding 600 ccm without front fairing nor windscreen shall be
used.
(until a standardized test target is defined)
Source: StVO § 39

## Slide 13: c) Type approval test requirements
www.bmvi.de

## Slide 14: c) Type approval test requirements - Test overview (7 tests)
  Lane change functional test
  Minimum activation speed test Vsmin
  Overriding test
  Lane change procedure suppression test
  Sensor performance test
  Sensor blindness test
  Engine start/ run cycle test

## Slide 15: c) Type approval test requirements - General test requirements
  Straight test track with
    at least two lanes,
    same direction of travel,
    road markings on each side of the lanes
  Vehicle test speed defined in each test as Vtest
    Based on minimum specified speed Vsmin
    Assumed max. speed of approaching vehicle Vapp = 130 km/h (*)
  Test requirements must be fulfilled in whole speed range
    Demonstration to satisfaction of technical service (appropriate documentation)
(*) If not otherwise specified in test

## Slide 16: c) Type approval test requirements - (1) Lane change functional test
Objective
Verification lane change procedure
  Activation ACSF of Category C (standby mode) by driver
  Approaching vehicle passes vehicle under test entirely
  Lane change procedure initiated by driver (indicator)
Recording lateral acceleration & lateral jerk
Repetition of test: 2x
Test procedure

## Slide 17: c) Type approval test requirements - (1) Lane change functional test
Automatic resumption ACSF of Cat. B1
Max. 5 s (*)
One continuous movement,
lateral acceleration max. 1 m/s²,
lateral jerk max. 5 m/s³
Objective
Verification lane change procedure
Min. 1 s
3 - 5 s
(*) Max. 5 s for M1, N1 and max. 10 s for M2, M3, N2, N3
Information provided to driver indicating LCP on-going
!
Max. 0.5 s
Test fulfilled:

## Slide 18: c) Type approval test requirements - (2) Minimum activation speed test Vsmin
Objective
Verification no system activation below specified minimum speed
  Activation ACSF of Cat. C (standby mode) by driver
  Approaching vehicle passes vehicle under test entirely
  Lane change procedure initiated by driver (indicator)
Test procedure
Test fulfilled
  Lane change manoeuvre is not performed.

## Slide 19: c) Type approval test requirements - (2) Minimum activation speed test Vsmin
Objective
Verification no system activation below specified minimum speed
Test procedure
In case Vsmin is calculated based on country specific general maximum speed other than 130 km/h:
In addition test procedure with
Test fulfilled: Lane change procedure is not performed.
In addition test procedure with
Test fulfilled: Lane change procedure is performed.
Additional testing
Simulation country of operation allowed.
Detection country of operation and knowledge of country specific general maximum speed limit shall be demonstrated to technical service.

## Slide 20: c) Type approval test requirements - (3) Overriding test
Objective
Verification overriding force needed by driver
Test procedure
Driver firmly maintains steering control in straight direction
Measurement force applied by driver on steering control
Repetition of test: 2x
  Measured overriding force ≤ 50 N
Test fulfilled:

## Slide 21: c) Type approval test requirements - (4) Lane change procedure suppression test
Objective
Verification conditions to suppress lane change procedure
Test procedure
Test repeated for following conditions, which shall occur before lane change manoeuvre has started:
Driver’s actions:
  removed hands from steering control and hands-off warning initiated
  manual deactivation direction indicator lamps
  overrides system
  switches system off
Vehicle speed reduced to
Begin lane change manoeuvre ≥ 5 s
  Suppression lane change procedure in each test case above
Test fulfilled:

## Slide 22: c) Type approval test requirements - (5) Sensor performance test
Objective
Verification of minimum distance Srear declared by manufacturer
Test procedure
Approaching vehicle
Type approved high volume series production L3 motorcylce
Engine capacity ≤ 600 cm³
w/o front fairing nor windscreen
Shall aim to drive middle of lane
Source: StVO § 39

## Slide 23: c) Type approval test requirements - (5) Sensor performance test
Objective
Verification of minimum distance Srear declared by manufacturer
Test procedure
Distance rear end test vehicle and front end of approaching vehicle measured (e.g. differential GPS)
Value the system detects approaching vehicle noted
Distance measured
  System detects approaching vehicle latest at distance declared by manufacturer Srear
Test fulfilled:

## Slide 24: c) Type approval test requirements - (6) Sensor blindness test
Objective
Verification system detection sensor blindness
Test procedure
Making rear sensor(s) blind
Means agreed between vehicle manufacturer and technical service (documented in report)
Standstill (no new engine start/ run cycle!)
Continued test procedure
Vehicle speed
Initiation lane change procedure

## Slide 25: c) Type approval test requirements - (6) Sensor blindness test
Objective
Verification system detection sensor blindness
Test fulfilled
System detects sensor blindness
System provides warning to driver
Lane change manoeuvre is not performed
Vehicle manufacturer demonstrates to satisfaction of technical service requirements also fulfilled under different driving scenarios. May be achieved by documentation.
Additionally
!

## Slide 26: c) Type approval test requirements - (7) Engine start/ run cycle test – Phase I
Objective
Verification default-off status
Test procedure
Engine start/ run cycle
  Approaching vehicle passes vehicle under test entirely
  Lane change procedure initiated by driver (indicator)
  No activation ACSF of Cat. C (off mode) by driver
Test fulfilled
  Lane change manoeuvre is not performed.

## Slide 27: c) Type approval test requirements - (7) Engine start/ run cycle test – Phase II
Objective
Verification required object detection for system activation
Test procedure
Engine start/ run cycle
  No approaching vehicle!
  Lane change procedure initiated by driver (indicator)
  Activation ACSF of Cat. C (standby mode) by driver
Test fulfilled
  Lane change manoeuvre is not performed.

## Slide 28: c) Type approval test requirements - (7) Engine start/ run cycle test – Phase III
Objective
Verification lane change enabling conditions
Test procedure
Approaching vehicle
Type approved high volume series production vehicle
Source: StVO § 39

## Slide 29: c) Type approval test requirements - Engine start/ run cycle test – Phase III
Objective
Verification lane change enabling conditions
Test procedure
Distance rear end test vehicle and front end of approaching vehicle measured (e.g. differential GPS)
Value the system detects approaching vehicle noted
Distance measured
  System detects approaching vehicle latest at distance declared by manufacturer Srear
Test fulfilled:

## Slide 30: Thank you for your attention!
Federal Ministry of Transport
and Digital Infrastructure
Invalidenstraße 44
D-10115 Berlin
www.bmvi.de