## Slide 1
Amendment to regulation UN 117
Introduction of worn tyre performances
69th GRB January 2019
Informal document GRB-69-08
(69th GRB, 22-25 January 2019,
agenda items 7 (c))

## Slide 2: Why to approve worn tyre?
New EU regulation on type-approval requirements:
(19) The Union should continue to promote the development of technical requirements for tyre noise, rolling resistance and wet grip performance of tyres at the United Nations level. This is because UN Regulation No 117 now contains these detailed provisions. The process of adapting the requirements on tyres to take account of technical progress should continue at United Nations level, in particular to ensure that tyre performance is also assessed at the end of a tyre's life in its worn state and to promote the idea that tyres should meet the requirements throughout their life and not be replaced prematurely. Existing requirements in Regulation (EC) No 661/2009 relating to tyre performance should be replaced by equivalent UN Regulations.
Worn state tire shall be tested
69th GRB January 2019

## Slide 3: Not be replaced prematurely:
69th GRB January 2019
depletion of resources (deforestation),
waste (+25%),
greenhouse gas emissions
50% of the Tyres are removed before 3 mm tread depth!!
+6,6 Mt CO2 eq
(*)
Current value of tread wear indicator (<= 2,2mm) shall be kept
Current removing practice :
Current regulation (e.g. UN 30 for passenger cars) and consensus :
Depth of the sculpture : 1,6 mm -0/+0,6
      Due to the over-production of tyres:
Effects on environment:
      Due to the over-consumption of the vehicle:
greenhouse gas emissions
(*) Ernst & Young study:
Planned obsolescence is not inevitable - June 2017

## Slide 4: Worn Tyre Performances: Noise?, Rolling Resistance? Wet Grip?
69th GRB January 2019
Noise Performances :
    On average, noise decreases by 1 dB between the new and the worn tyre state.
Rolling Resistance Performances:
    Rolling resistance decreases by about 20% between the new and the worn tyre state.
Wet Grip Performances :
    Wet grip deteriorates systematically between the new and the worn tyre state.
Chart: Braking distance 80-20 kph on wet surface
| Worn Tire | New Tire
 | 40 | 27.7
Only wet grip performances shall be taken into account
New
Worn

## Slide 5: Does it exist a relationship between the wet grip performances at new tyre state and worn tyre state?
69th GRB January 2019
The both configurations shall be tested
Wet braking distance (15 tyres)
Tyre performance at new state
doesn’t give an indication of the
tyre performance at worn state

## Slide 6: How to approve the tires in both configurations (new and worn state)?
If possible by using a method based on the same principle (avoid to create a burden for the tire manufacturers and the technical services)
Current regulatory methods described in UN 117 regulation.
Trailer method
Vehicle method
Or
New tyre to be approved in comparison to the new reference tyre (SRTT)
Wet grip indexnew : GN
Worn tyre to be appoved in comparison to the worn reference tyre (SRTT)
Wet grip indexworn : GW
69th GRB January 2019

## Slide 7: Which level of performance can we require?
*: depending on the speed symbol
The same limits of wet grip index (G) than those defined in the regulation UN 117
without severisation for the worn state
Normal tyre | Snow tyre | Snow tyre for use in severe snow conditions | Special use tyre
≥ 1.1 | ≥ 1.1 | ≥ 1.0 or ≥ 0.9* | Not defined
Same relative performance for the worn tyres
69th GRB January 2019

## Slide 8: How to obtain the worn tyre state?
69th GRB January 2019
By using a standardized method: ASTM F1046-01(2015)
The wear is obtained artificially through a buffing of the tread pattern
New state
X% Reduction
-X %
2 mm +/-0,2

## Slide 9: Is this method representative of a natural wear?
The buffed tyre performance is very close to the naturally worn tyre
Loss of braking performance of worn tire (buffed or naturally worn) versus new tire (%)
69th GRB January 2019

## Slide 10: Conditions of tests: Are they representative of the mechanisms involved in the contact area?
Main mechanism in R117 for the new state : pure grip (full contact patch)
Worn tyre : balance of two mechanisms (grip + hydroplaning)
Test conditions are relevant for the worn tyre testing , in terms of mechanisms balance
69th GRB January 2019
Braking
Grip
aera
Hydroplaning
area
80 km/h
20 km/h
40 km/h

## Slide 11: Conditions of tests: Are they relevant also for worn tyre testing ?
Height of water: 1mm +/-0.5 (value in regulation UN 117)
82%
< 1%
17 %
0.5 mm
1 mm
Test Speeds: 80 Km/h (Vehicle) or 65 km/h (Trailer) in regulation UN R117
Water depth distribution when road is wet
< 65 km/h | < 80 km/h
81.9% | 89.1%
Percentage of cases where the initial speeds were before the accidents
Water height and speeds are relevant to measure grip performance and hydro performance in the worn state.
69th GRB January 2019

## Slide 12: When could we apply the new amendment of regulation UN 117?
69th GRB January 2019
From the date of entry into force of the new amendment:
Voluntary application (upon the wish of the tire manufacturer):
[71 th GRB (2020)]
Adoption
[Entry into force ( 2021)]
[WP29 (June 2020)]
Vote
Mandatory date for new type of tyre upon the request of CP’s :
[ 1st September 2026]
Mandatory date for new tyre upon the request of CP’s :
[ 1st September 2029]
69th GRB (2019)

## Slide 13: Conclusions
69th GRB January 2019
The assessment of the wet grip performance on tyres in worn state is relevant.
The UN 117 method used to evaluate the wet grip performance of new tyres can also be used for worn tyres.
The addition to the existing method is limited to a preparation of the tread of the tyres (candidate and SRTT).
The same limits in term of level of relative performance can be used both new and worn tyres.
The mandatory dates are proposed to apply this new amendment.

## Slide 14: THANK YOU FOR YOUR ATTENTION
69th GRB January 2019