## Slide 1
<number>
A preliminary study on test methods of UN regulation No. 51-03 based on CATC
Informal document GRB-69-18
(69th GRB, 22-25 January 2019,
agenda item 4(a), 6 and 19)
China Automotive Technology and Research Center Co., Ltd.
Notes: <number>

## Slide 2: Introduction
<number>
China will publish the GB 1495 standard soon in [2019], whose test methods are similar to UN Regulation No.51-03 (without ASEP) and ISO 362-1.
Research on relationships between environmental noise problems, test cycles, test methods, limit values and environmental influences of new systems was carried out in China.
With the data collection and analysis of China Automotive Test Cycles (CATC), more proofs show that the test methods of UN Regulation No.51-03 need to
be re-searched.

## Slide 3: Contents
<number>
China Automotive Test Cycles
The possibility of using CATC in the noise test methods
Test methods design
Example 1
Example 2
Example 3
Conclusions

## Slide 4: China Automotive Test Cycles
<number>
From 2015 to 2018, 5048 vehicles real driving behaviors were collected in 41 cities of China on time, for purpose of setting proper test methods for fuel consumption, emission and also development of EV.

## Slide 5: Using CATC in the noise test methods
<number>
CATC has collected more than 20 parameters for each vehicles, including the vehicle speed, vehicle acceleration, engine speed, and gears distribution……
We realized in the year 2017, that all the data can be used to design the noise test methods like ISO 362-1.
Several cases study on noise problems, driving behaviors, test methods design and proof tests were carried out from the summer of 2017.
*Figure from: ASEP-04-11 (China) Road conditions and conclusion of China on ASEP test method.

## Slide 6: Test method design
<number>
Low, middle speed range
（30, 50, 70 km/h）
Wot test
High speed range
(80, 100, 120 km/h)
Cruise test
Starting
Running
Test methods
New tests created
Starting noise
Wot noise at fixed gears and fixed speed
Cruise noise at high speed
Tyre noise (OICA)
Engine noise (OICA)
Partial load noise (OICA)
Other traditional tests
Method B of R51-03
ASEP of R51-03

## Slide 7: Example 1
<number>
 | Acceleration procedure during summer |  |  | Acceleration procedure during winter |  | 
 | 25~35km/h | 45~55km/h | 65~75km/h | 25~35km/h | 45~55km/h | 65~75km/h
1st gear | 0.01% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
2nd gear | 1.89% | 0.00% | 0.00% | 0.69% | 0.00% | 0.00%
3rd gear | 41.88% | 0.97% | 0.02% | 31.10% | 0.39% | 0.00%
4th gear | 44.68% | 32.28% | 3.32% | 54.50% | 22.16% | 1.76%
5th gear | 11.22% | 66.52% | 96.59% | 13.04% | 77.42% | 98.18%
Test Gear designed for 30km/h: (1+X/2)/2; for 50km/h: X/2; for 70km/h: (X/2+X)/2
(“X” means the total gears number)
Engine speed percentile | Summer time |  |  | Winter time |  | 
 | 25~35km/h | 45~55km/h | 65~75km/h | 25~35km/h | 45~55km/h | 65~75km/h
50% | 1571 | 1935 | 2544 | 1481 | 1886 | 2545
90% | 2126 | 2348 | 2714 | 1990 | 2257 | 2703
95% | 2268 | 2442 | 2764 | 2140 | 2380 | 2731
99% | 2688 | 2762 | 3121 | 2418 | 2552 | 3024
Method B：3rd gear, engine speed 3450 r/min.
ASEP: 2nd and 3rd gears, speed range 20-80km/h
Conclusion: method B is already 99% percentile for this vehicle.

## Slide 8: Example 2
<number>
 | Acceleration procedure |  | 
 | 25~35km/h | 45~55km/h | 65~75km/h
1st gear | 0.00% | 0.00% | 0.00%
2nd gear | 2.22% | 0.00% | 0.00%
3rd gear | 48.81% | 0.32% | 0.00%
4th gear | 43.30% | 16.22% | 0.26%
5th gear | 4.02% | 47.26% | 3.89%
6th gear | 0.15% | 36.11% | 95.85%
Test Gear designed for 30km/h: (1+X/2)/2; for 50km/h: X/2; for 70km/h: (X/2+X)/2
(“X” means the total gears number)
Engine speed percentile | All time |  | 
 | 25~35km/h | 45~55km/h | 65~75km/h
50% | 1288 | 1502 | 1781
90% | 1604 | 1771 | 1919
95% | 1672 | 1859 | 1945
99% | 2018 | 2018 | 2224
Method B：3rd gear, engine speed 2760 r/min.
ASEP: 2nd and 3rd gears, speed range 20-80km/h
Conclusion: method B is already 99% percentile for this vehicle.

## Slide 9: Example 3
<number>
 | Acceleration procedure |  | 
 | 25~35km/h | 45~55km/h | 65~75km/h
1st gear | 0.01% | 0.00% | 0.01%
2nd gear | 2.74% | 0.01% | 0.02%
3rd gear | 76.20% | 0.77% | 0.01%
4th gear | 20.59% | 26.18% | 1.29%
5th gear | 0.33% | 65.44% | 25.57%
6th gear | 0.00% | 7.60% | 56.67%
7th gear | 0.00% | 0.00% | 13.12%
Test Gear designed for 30km/h: (1+X/2)/2; for 50km/h: X/2; for 70km/h: (X/2+X)/2
(“X” means the total gears number)
Engine speed percentile | All time |  | 
 | 25~35km/h | 45~55km/h | 65~75km/h
50% | 1386 | 1424 | 1515
90% | 1631 | 1757 | 1921
95% | 1689 | 1848 | 1988
99% | 2086 | 1978 | 2359
Method B: not carried out
Conclusion: good performance vehicles have very low engine speed during real driving. What is the difference between the vehicles can be loudly and the vehicles are loudly? How to check?

## Slide 10: Conclusions
<number>
What is the purpose of method B? The real driving conditions or extreme conditions? If it is extreme conditions, what is the “additional” of ASEP means? What is the real traffic noise problems?
For low and normal performance vehicles, this test conditions of method B is not easy.
The ASEP test methods now seem to make no sense for at least normal vehicles, it is a test at wrong gears, an engine noise regulation are suggested if the noise at different engine speed are interested.
China wants to analyze CATC and re-search the test methods of GB 1495 and R51-03 method B and ASEP, combined with the real traffic noise problems.
More vehicles are needed to be analyzed like the high performance vehicles.

## Slide 11
Web site：www.catarc.org.cn
<number>
Thanks for your attention
National Automotive Standardization Technical Committee