## Slide 1
Harmonization of Crash Regulations in Korea
14-18 May 2018
Republic of Korea
Informal document GRSP-63-21
(63rd GRSP, 14 - 18 May 2018,
agenda item 26 (a))
Submitted by the expert from Republic of Korea

## Slide 2
Purpose
Harmonization with UN GTR and/or UN Regulations
  Occupant Protection
    KMVSS article 102 is harmonized with UN Regulations (R94, R95, R135 and R137)
  Fuel System Integrity
    KMVSS article 91 is harmonized with UN Regulations (UN R94, 95, 134, 135 and 137) about passenger vehicles
    Side impact test, rear moving barrier test, and static rollover test are maintained

## Slide 3
Timeline
Notice for Proposed of Rule Making
  26 April 2018 – 25 June 2018
Implementation of the Amended Regulations
  New types: 1 September 2020
  All new vehicles: [31 December 2021]

## Slide 4
Protection of Occupants (article 102)
Full Width Frontal Collision Test
 | Current | NPRM
Scope | Passenger vehicle | Passenger vehicle not exceeding 3.5 ton
Test Procedure | Fixed rigid barrier Speed: 48 km/h Dummies: Driver & Passenger (H3 50%ile M) | Fixed rigid barrier Speed: 50 km/h Dummies: Driver (H3 50%ile M), Passenger (H3 5%ile F)
Requirements | Injury criteria | Injury criteria, steering wheel displacement, door opening during/after impact, fuel leakage → Harmonized with UN R 137

## Slide 5
Protection of Occupants (article 102)
Offset Frontal Collision Test
 | Current | NPRM
Scope | None | Passenger vehicle not exceeding 2.5 ton
Test Procedure | None | Deformable barrier(40% offset) Speed: 56 km/h Dummies: Driver & Passenger (50%ile H3 M)
Requirements | None | Injury criteria, steering wheel displacement, door opening during/after impact, fuel leakage → Harmonized with UN R 94

## Slide 6
Protection of Occupants (article 102)
Side Impact Test
 | Current | NPRM
Scope | Passenger vehicle | Passenger vehicle and truck not exceeding 3.5 ton
Test Procedure | Moving deformable barrier (MDB, 950kg) Speed: 50 km/h Dummy: Driver (ES2) | Moving deformable barrier (MDB, 950kg) Speed: 50 km/h Dummy: Driver (ES2)
Requirements | Injury criteria, door opening during/after impact, fuel leakage | Injury criteria, door opening during/after impact, fuel leakage → Harmonized with UN R 95

## Slide 7
Protection of Occupants (article 102)
Pole Side Impact Test
 | Current | NPRM
Scope | None | Passenger vehicle and truck not exceeding 3.5 ton
Test Procedure | None | Fixed rigid pole Speed: 32 km/h (75 degree angle) Dummies: Driver (WorldSID 50%ile M)
Requirements | None | Injury criteria, door opening during/after impact, fuel leakage → Harmonized with GTR 14 and UN R 135

## Slide 8
Fuel System Integrity (article 91)
Liquid Fuel Vehicle
 | Current | NPRM
Scope | Passenger vehicle and bus not exceeding 4.5 ton | Passenger vehicle (Bus not exceeding 4.5 ton: Maintain current requirements)
Test Procedure | Full width frontal collision test (48 km/h) with article 91 | Revised tests: Harmonized 3 type crash tests with UN Regulations - Full width frontal collision test - Offset frontal collision test - Pole side impact test
 | Side impact test (50 km/h, 950 kg) with article 102 Rear moving barrier impact test (48 km/h, 1,805 kg) with article 91 Static rollover test with article 91 | Maintain current tests: Side impact test, rear moving barrier test, and static rollover test

## Slide 9
Fuel System Integrity (article 91)
Hydrogen and Fuel Cell Vehicle
 | Current | NPRM
Scope | Passenger vehicle and bus not exceeding 4.5 ton | Passenger vehicle (Bus not exceeding 4.5 ton: Maintain current requirements)
Test Procedure | Full width frontal collision test (48 km/h) with article 91 | Revised tests: Harmonized 2 type crash tests with UN Regulations - Offset frontal collision test - Pole side impact test
 | Side impact test (50 km/h, 950 kg) with article 102 Rear moving barrier impact test (48 km/h, 1,805kg) with article 91 | Maintain current tests: Side impact test, rear moving barrier test

## Slide 10
Fuel System Integrity (article 91)
Electric Vehicle
 | Current | NPRM
Scope | Passenger vehicle and bus not exceeding 4.5 ton | Passenger vehicle (Bus not exceeding 4.5 ton: Maintain current requirements)
Test Procedure | Full width frontal collision test (48km/h) with article 91 | Revised tests: Harmonized 2 type crash tests with UN Regulations - Full width frontal collision test - Offset frontal collision test
 | Side impact test with article 102 Rear moving barrier impact test (48km/h, 1,805kg) with article 91 Static rollover test with article 91 | Maintain current tests: Side impact test, rear moving barrier test, and static rollover test