## Slide 1: Transposition of GTR15 (WLTP) and GTR19 (Evap) into UN Regulations Update for GRPE from WLTP Transposition Task Force January 2019
Informal document GRPE-78-14- Rev.1
78th GRPE, 8-11 January 2019
Agenda item 3(b)

## Slide 2: Post-77th GRPE Update
Task Force and WLTP IWG Meetings held:
25/06/18 (WebEx); 06/08/18 (WebEx); 20-21/09/18 (Tokyo); 05/11/18 (WebEx); 23/11/18 (Paris); 17/12/18 (WebEx); and 7-8/01/19 (Geneva)
Discussions on transposition also held at 28th Session of IWVTA (09/11/18, Geneva) (see IWVTA-28-08-rev.1 WLTP Transposition)
  25th June – 9th November 2018
  Worked on structure and content of draft text
  Approach 3 (one series of amendments to cover L1a, L1b & L2) reconsidered
    Discussed at 28th IWVTA Session - Mixed support/objection for Approach 3
  Worked on structure and content of draft texts
  Inclusion/Exclusion of EU specific procedures (e.g. ATCT) re-discussed
  Different EU and JPN positions on durability → Task Force put ‘on hold’
  Discussions on the ‘need for’/’purpose of’ Levels 1a & 1b

## Slide 3: Post-77th GRPE Update
23rd November 2018, OICA, Paris – face to face/WebEx
  Discussions on a potential new concept to avoid dis-harmonisation in UNR WLTP by including Level 1a (Europe) in UNR 83 08 series (see schematic on next slide)
  Matrix concept developed
    Issue - Plug-in hybrids don’t fit within the 3 phase (L1b)/4 phase (L1a) concept
  European Commission proposal to extend timeline
    More time needed for finalising the L2/L1 concept and for developing harmonised Conformity of Production and Durability requirements
    Proposal to extend timeline by one GRPE session (i.e. Informal Documents for 79th GRPE and Working Documents for 80th GRPE)

## Slide 4: ‘Alternative concept discussed at 23rd Nov 2018 meeting
UNR WLTP - 01
Type 1 GTR15
Type 5 GTR15
Type 4 GTR19
UNR83 07
UNR83 08
UNR83 09
UNR WLTP - 00
Level 1
Phases | CO | HC | NOx | PM
1-2 |  |  |  | 
1-2-3 | xxx | xxx | xxx | xxx
1-2-3-4 |  |  |  | 
Level 2
Phases | CO | HC | NOx | PM
1-2 |  |  |  | 
1-2-3 | xxx | xxx | xxx | xxx
1-2-3-4 | xxx | xxx | xxx | xxx
4 phase
3 phase for OVC
3&4 phase for OVC
Note
Under this concept, UNR83 08 series would be a complete ‘copy and paste’ of (EU) 2017/1151.
UNR 83 09 series would only include the (EU) 2017/1151 requirements which are not included in UNR-WLTP (e.g. Type 6, ISC, OBD, RDE etc.).
Note
The Type 5 test was not included in the diagram developed during the meeting. However if a harmonised Type 5 test is developed to the timetable then it would also be included in UNR 83 08 series.
Notes
UNR WLTP 00 and 01 would use a harmonised test procedure – with some potential non-harmonised options in 00 (e.g. single-axis dyno).
00 and 01 series would both include a harmonised Type 5 test if developed in time.
Under this concept the Level 1 elements (UN 83 08 and UNR WLTP 00) would not be applicable until Level 2 was in force

## Slide 5: Post-77th GRPE Update
17th December 2018 - WebEx
  Japan supported the extension to the timeline
  Japan strongly objected to including WLTP in UNR 83 – reasons:
  Having regional regulations in separate UNR (EU: R83, JPN: R-WLTP), “harmonisation” scheme will be collapsed. Therefore, UNR for WLTP based on GTRs should go to one single UNR.
    Same requirement with separate UNR is against the concept of 1958 agreement.
    The approach EC and Japan agreed before (= Approach 2) is not yet denied. There is no need to change scheme from the original to “discussion starter idea”

## Slide 6: WLTP Transposition: Open issues
Different cycles (EU L-M-H-ExH), (Japan L-M-H)
  Solutions exist for pure combustion engined vehicles and pure electric vehicles but OVC-HEV are still problematic as they require two separate tests (one for 4 phases, one for 3 phases)
Reference Fuels
Number of tests to demonstrate CO2
Limits for Drive Trace Indices (RMSSE: Japan 0.8 km/h; Europe 1.3 km/h
Usage of Daytime Running Lights
Testing of 4WD vehicles
Conformity of Production
Utility Factors
EU unique items (ATCT, Normalisation, Vehicle Type, ….)
Adapted from IWVTA-28-08.

## Slide 7: Post-77th GRPE Update
25th WLTP IWG – 7th/8th January 2019
Further discussion on approach and concept for transposition
  Japan reconfirmed their position – to proceed with Approach 2.
Discussed options within GTR15 and GTR19 and how to proceed
Discussed the importance of developing the UNR within the timetable covered by the mandate for Phase 2 of IWG
Introduction of initial report on gasoline reference fuel study
Update on Conformity of Production Task Force
  Timeline aligned with UNR WLTP
Update on Durability Task Force
  Proposal on way forward for Durability by European Commission

## Slide 8: Revised Work plan
Developing Level 2 is top priority for Task Force
  This will help to further highlight the main issues requiring resolution
Obtain consensus on both the approach and the concept
Continue to develop UNR WLTP and UNR 83 08 series regulatory texts
Further discussion/agreement on Contracting Party options
Proposal for a harmonised gasoline reference fuel
Meetings
  Dates for face to face and WebEx meetings to be decided
Informal UNR WLTP and UNR 83 08 series for 79th GRPE, May 2019
Working Documents for 80th GRPE, January 2020

## Slide 9
Contact information
Rob Gardner, TRL Ltd on behalf of the European Commission (Task Force Leader)
rgardner@trl.co.uk