## Slide 1: DATA STORAGE SYSTEM FOR AUTOMATED DRIVING (DSSAD)
Submitted by experts from OICA
Informal document GRVA-02-20 2nd GRVA, 28 January – 1 February 2019
Provisional agenda item 5 (a)
Transmitted by the expert from:

## Slide 2
DSSAD : Purpose of the Data Storage System for Automated Driving
Definition :
The Data Storage System for Automated Driving is a device or a function that :
records and stores a set of data (“timestamped flags”) during the automated driving sequences
Definition :
The Data Storage System for Automated Driving is a device or a function that :
records and stores a set of data (“timestamped flags”) during the automated driving sequences
of any vehicle equipped with Level 3 / Level 4 / Level 5 Automated Driving Systems (ADS),
Definition :
The Data Storage System for Automated Driving is a device or a function that :
records and stores a set of data (“timestamped flags”) during the automated driving sequences
of any vehicle equipped with Level 3 / Level 4 / Level 5 Automated Driving Systems (ADS),
in order that whenever a significant safety related event occurs, it can provide
Definition :
The Data Storage System for Automated Driving is a device or a function that :
records and stores a set of data (“timestamped flags”) during the automated driving sequences
of any vehicle equipped with Level 3 / Level 4 / Level 5 Automated Driving Systems (ADS),
in order that whenever a significant safety related event occurs, it can provide
a clear picture of the interactions between the driver and the system,
before and after (whenever possible) the event, in order to establish :
Definition :
The Data Storage System for Automated Driving is a device or a function that :
records and stores a set of data (“timestamped flags”) during the automated driving sequences
of any vehicle equipped with Level 3 / Level 4 / Level 5 Automated Driving Systems (ADS),
in order that whenever a significant safety related event occurs, it can provide
a clear picture of the interactions between the driver and the system,
before and after (whenever possible) the event, in order to establish :
- if the driver or the system was requested to be in control of the driving task, and
- who was actually performing the driving task.

## Slide 3
STATUS/MODE OF THE SYSTEM
Several status and/or modes will potentially exist :
=> OFF (“disengaged”), STAND-BY, ACTIVE, FAILURE, LIMITED, TRANSITION,…
DSSAD : Set of data to be stored
STATUS/MODE OF THE SYSTEM
Several status and/or modes will potentially exist :
=> OFF (“disengaged”), STAND-BY, ACTIVE, FAILURE, LIMITED, TRANSITION,…
TRANSITION DEMAND (TD) :
  Several Transition Demand types will potentially exist, depending from the context :
  A-Type for “comfortable/planned” situations, like end of the Use-Case, and B-Type for other “unplanned” situations, C-Type ?...
  The “warning cascade” could vary from TDA and TDB depending on the needs and requirements and each component of the TD cascade, may be stored independently, because released through different channels, like “visual”, “audible”, “haptic” for example.
  => Each Transition Demand may be stored as a cascade of several signals :
  TDA = TDA1 + TDA2 + TDA3 TDB = TDB1 + TDB2 …etc…
STATUS/MODE OF THE SYSTEM
Several status and/or modes will potentially exist :
=> OFF (“disengaged”), STAND-BY, ACTIVE, FAILURE, LIMITED, TRANSITION,…
TRANSITION DEMAND (TD) :
  Several Transition Demand types will potentially exist, depending from the context :
  A-Type for “comfortable/planned” situations, like end of the Use-Case, and B-Type for other “unplanned” situations, C-Type ?...
  The “warning cascade” could vary from TDA and TDB depending on the needs and requirements and each component of the TD cascade, may be stored independently, because released through different channels, like “visual”, “audible”, “haptic” for example.
  => Each Transition Demand may be stored as a cascade of several signals :
  TDA = TDA1 + TDA2 + TDA3 TDB = TDB1 + TDB2 …etc…
MINIMAL RISK MANOEUVER (MRM) :
Several MRM types (A-Type, B-Type,…) will potentially exist, depending from the context :
=> Each MRMA, MRMB… may be differentiated.
STATUS/MODE OF THE SYSTEM
Several status and/or modes will potentially exist :
=> OFF (“disengaged”), STAND-BY, ACTIVE, FAILURE, LIMITED, TRANSITION,…
TRANSITION DEMAND (TD) :
  Several Transition Demand types will potentially exist, depending from the context :
  A-Type for “comfortable/planned” situations, like end of the Use-Case, and B-Type for other “unplanned” situations, C-Type ?...
  The “warning cascade” could vary from TDA and TDB depending on the needs and requirements and each component of the TD cascade, may be stored independently, because released through different channels, like “visual”, “audible”, “haptic” for example.
  => Each Transition Demand may be stored as a cascade of several signals :
  TDA = TDA1 + TDA2 + TDA3 TDB = TDB1 + TDB2 …etc…
MINIMAL RISK MANOEUVER (MRM) :
Several MRM types (A-Type, B-Type,…) will potentially exist, depending from the context :
=> Each MRMA, MRMB… may be differentiated.
OVERRIDE & TAKE-OVER (OR & TO) :
Several OR and/or TO types (A-Type, B-Type, etc…) will potentially exist.:
=> Each ORA / ORB / TOA / TOB / TOC… may be differentiated.

## Slide 4
AD system data
In the case of an accident with inflation of at least one airbag, the complementary Event Data Recorder (EDR) system will provide many additional information with its usual possibilities and limitations :
With trigger : ADS data and Detailed EDR data (record @ trigger event)
  Trigger: Airbag deployment & strong deceleration (Δv > 8 km/h within 150 ms as in US part 563 EDR)
Without trigger : ADS data only ( including timestamp / continuous [3] month storage)
ON / OFF
TD
TO
MRM
ADS is active
No TD
No MRM
Incident/accident without EDR trigger
Case of an Accident with EDR trigger
Additionnal
data
5s before crash
Detailed EDR data
[3 month] storage of ADS data
WHO WAS DRIVING
ACCIDENT RECONSTRUCTION
DSSAD : complementary & independent to EDR
« Different data storage systems for different purposes »

## Slide 5
« US » EDR
speed, accelerations, restraint systems deployment,… trigger time stamped
DSSAD
System status/mode, Transition Demands from system HMI, Driver’s Override & Take Over, MRM activations
REGULATED
OPTIONAL
(NO TECHNICAL REGULATION)
All Vehicles
equipped with
Lev 3, 4 or 5 AUTOMATED
DRIVING SYSTEMS
Accident Emergency Call System
(GPS/Galileo/Glonass position, GMT time stamped, retention system status, VIN…
« other data »
Video scene recording, insurrance system data, fleet management tool data, other personnal data (depending on regional privacy laws)…
Data Storage context :
Only DSSAD applies to AD only
Light Vehicles M1/N1
WHO WAS DRIVING
ACCIDENT RECONSTRUCTION
  “It might be important to collect data in retrieval format about who was in control and of what throughout the operation in case of an unexpected event that could impact road traffic safety.”
  (WP1 – IGEAD – 07-04 – Guidance for Automated Vehicles – discussion paper)

## Slide 6
CONCLUSION : a strategy for DSSAD
 | EDR (M1/N1) | DSSAD (All vehicles with ADS)
Purpose | Supporting crash analysis and reconstruction | Support legal information needs on vehicle control (Driver/System)
How | Record data when triggered (momentaneous) | Store data over a longer period
What data | Data relevant to crash analysis Vehicle speed Vehicle Speed reduction Engine throttle Service brake Ignition Airbag deployment .. | Data relevant to vehicle control: AD system ON/OFF Transition Demand Take Over Minimum Risk Manoeuver Repective data timestamps
Reference | FMVSS 49 CFR Part 563 | To be discussed (OICA proposal available)
Application |  | 
“conventional vehicle” | Applicable | No need
“vehicle with Automated Driving function” (LEV3, 4 & 5) | Applicable | Applicable
Proposed strategy for Automated Driving functionalities:
            Implement the concept of DSSAD in ACSF B2 Level 3 – highway application (short term) & in “horizontal regulation on Automated Driving” (mid term)

## Slide 7
ANNEXES
DATA STORAGE FOR AUTOMATED DRIVING

## Slide 8
Data : data to be displayed or utilized by some CPUs of the vehicle (e.g. « speed of vehicle » is the information that is displayed to the driver through the speedometer, with tolerance as given by UNECE R39. It is not the absolute speed of the car)
recording data : keeping the instant value of several continuous information or an instant message (both available in the vehicle’s CAN or ECUs) in a volatil memory. These data may be recorded and overwitten continuously : they are not available after a while, if not stored.
Storing data : keeping the recorded data in a non-volatil memory for future retrieval or « read only » access.
Trigger : parameter or signal, which threshold is achieved or exceeded when a significant safety related event occurs.
DSSAD : Data Storage System for Automated Driving, which aims at making clear « who was driving before (and possibly after) a significant safety related event » and « who was requested to drive » (it can be different, especially during transition driving sequences.
EDR : Event Data Recorder, which aims at a better understanding of the retention system action and vehicle conditions durong a severe crash.
EDR is described in North American CFR Part 563.
AECS : Accident Emergency Call System, which aims at providing a Public Safety Answering Point with a set of data concerning a severe crash that just occured. AECS are described in European e-Call regulation, Russian ERA-Glonass regulation, and will be in UNECE Reg.
Significant safety related event : Event that can put human beings in danger. Some of these may be subject to retention system deployment, some others not. Some of these may be subject to emergency manoeuver before impact and some others may not. Minimal Risk Manoeuver should be performed without emergency manoeuver, and without impact, but it is however considered as a significant safety related event.
Minimal risk manoeuvre : procedure aimed at minimizing risks in traffic, which is automatically performed by the system (e.g. when the driver does not respond to a “transition demand”).
Emergency Manoeuvre : manoeuvre performed by the system in case of a sudden unexpected event in which the vehicle is in imminent danger to collide with another object, with the purpose to avoid or mitigate a collision.
DSSAD : Glossary of terms

## Slide 9
As it is proposed to be stored and available for [3 months] or [25.000] flags (the first achieved of both), the DSSAD can always bring the answer to the question “who was driving ?” to the authorized person or administration.
Determination of “who is allowed to access the data” may vary from a country to another.
It should remain under the responsibility of the OEM to decide the right technical solution in order to restrict access to the authorized person/administration only, and to guaranty that the Read Only Data cannot be corrupted.
Maximum number of elementary events to be stored by the system remains to be decided. ( 25.000 ? )
(considering an average number of 5 elementary events per sequence of use : 25.000 = 50 sequences (of an average 5 events) / day , during 100 days)
ANNEX 2 : Detailed principle of the DSSAD

## Slide 10
ANNEX 2 : Detailed principle of the DSSAD
These data are not available any longer because they were stored but storage is now too old
ON/OFF STATUS
When the MRM is finished, the system turns OFF
From [3 months] ago, all information is always available, with time stamp
TAKE-OVER
TRANSITION DEMAND
MRM
ON
OFF
ON
OFF
When the driver Takes Over after being requested, the system turns OFF
When the driver does not respond to TD, the system proceeds to a MRM
Who was requested to drive ?
Who was actually driving ?
SYSTEM
DRIVER
SYSTEM
SYSTEM
DRIVER
ON/OFF STATUS
When the driver decides to Take Over it, the system turns OFF
TAKE-OVER
TRANSITION DEMAND
MRM
ON
When the MRM is engaged, the system turns OFF as soon as the driver Takes Over.
When there is a traffic violation, it is possible to determine who was driving at that time…
Who was requested to drive ?
Who was actually driving ?
SYSTEM
DRIVER
SYSTEM
DRIVER
Unknown if older than [3 months] ago
ON
DRIVER
SYSTEM
ON
DRIVER
DRIVER
ON
ON
…even if the traffic violation occured 2 or 3 months ago…
A-Type
B-Type
B-Type
A-Type
OFF
OFF
OFF
OFF
OFF
Use the Powerpoint version
With animations for better understanding of the concept.

## Slide 11
The previous slide illustrates the concept of DSSAD, as proposed by the cluster n°2.
For simplification of the drawing, some hypothesis were considered, which do not necessarily reflect the future conclusions and detailed requirements that will be established regarding SAE Lv3 & above systems.
Simplifications considered in this slide are :
1- the system only has 2 possible status : ON (active) and OFF (disengaged),
2- the Transition Demand (TD) is only “one shot” and A-type or B-type only,
3- the driver directly Takes Over (TO) the system, without any preliminary Over-Ride and/or Transition Sequence
4- the system automatically switches to OFF as soon as the driver takes over or the MRM is finished,
5- there is only one MRM type that is engaged [X] seconds after the TD in the case there was no TO by the driver
Reality will be a little bit more complicated, but it does not change the concept itself.
The detail of the set of data to be stored will be possible to establish only after the requirements regarding the principles to be followed by these systems are given by the future dedicated regulation.
NB : All the potential STATUS/MODES OF THE SYSTEM, and definitions of OVERRIDE & TAKE-OVER, that are given in the glossary of terms, were inspired by the ACSF draft for E-systems, as it exists today. As so, they are only indicative, and modifications could be introduced by future regulation on these systems.
DSSAD : Important considerations
regarding previous slide