## Slide 1
Overview of the recommendations on cyber security
Submitted by the Chair of the Task Force on Cybersecurity and OTA (software updates)
Informal document GRVA-03-02 3rd GRVA, 3-4 June 2019 Agenda item 4(a)

## Slide 2
        Content
Background
Cyber Security
Ongoing work - the test phase

## Slide 3
The remit of the group was to produce
  a recommendation addressing cyber security issues
  develop outputs for use as a regulation or resolution
How the recommendations were developed
  The group contained experts from Contracting Parties and NGO‘s (CITA, FIA, ITU, OICA, CLEPA, ISO and others)
  Thirteen meetings were held to agree the proposed recommendations plus twenty-one ad-hoc meetings
Work started on 21 December 2016
Background

## Slide 4
2. The Cyber Security recommendation

## Slide 5
        The group developed a split approach for the cyber security assessment:
        Assessment of relevant vehicle manufacturer management system
        Assessment and certification of vehicles
New approach: Certification of OEM‘s organization & processes
Cyber Security Management System Requirements
Vehicle Requirements
Organizational structure & processes
Design of the vehicle architecture, risk assessment and implementation of mitigations
Notes: Note: assurance can be in the form of self-certification or type approval.

## Slide 6
Cyber Security Regulatory Proposal (Annex A)
Cyber Security Guidance (chapters 1-6, Annex B and Annex C)
Sets out what good cyber security looks like through 10 principles
Requirements for vehicle manufacturers “cyber security management system“
Requirements for vehicle assurance for cyber security certification
        Structure of the Recommendation on Cyber Security
Describes possible controls that could be used to mitigate risks
Describes a range of threats that should be considered in the design of a vehicle
Processes cover all phases of a vehicle life until scrappage
Processes required include: organisational structure; risk management processes; design processes; verification processes; monitoring; and response
Includes processes for managing suppliers
Vehicle architecture and connectivity needs to be described
Assurance provided based on a manufacturer‘s risk assessement, what controls have been implemented to reduce risks, and other evidence provided to demonstrate that the requirements are met

## Slide 7
        The picture below represents the interaction of a vehicle with external systems and what could be assessed during vehicle certification.
Scope of the cyber security proposal – confined to the vehicle!
GNSS
V2V
V2I
Diagnostic/ Maintenance Tools
Gateway
ECUs
Body ECUs
P/T
ECUs
Chassis
ECUs
OEM Server
Supplier Server
„Neutral“ Server
Communication
channels
Infotainment
Black Box
„Internet of
Things“
WWW
Backend Servers
SD
@
e.g. CAN, Ethernet, ...
OBD II
e.g. Over the air
Updates, performance
data, eCall...
e.g. 3G, WiFi, ...
e.g. Battery status,
Vehicle functionalities, ...
Grid connection, incl. smart charging
External storage devices / Nomadic devices
Camera
Radar, ...
GNSS – Global Navigation Satelite System , V2V – Vehice-to-Vehicle , V2I – Vehicle-to-Infrastructure , P/T – Powertrain , ECU – Electronic Control Unit , OBD – On Board Diagnostic
        Note: the picture is not a representation of a required vehicle architecture

## Slide 8
Are there detailed technical measures mandated?
No.
The proposal was drafted in a technology neutral way. This should give some flexibility to vehicle manufacturers to decide how to ensure the cyber security of their vehicles.
A rigid definition of technical measures could be counterproductive, since the cyber security environment is a very dynamic one. The risk is that any detailed technologies which are mandated could become outdated/vulnerable and may block alternative, innovative, approaches and therefore limit or counter the possibilities to ensure cyber security. There is also a risk that a given solution may not be applicable to all vehicle designs. Thus the proposal might force unsuitable technologies on vechicles.
Noting that guidance may be valuable in this area, the proposal and annexes do include principles and mitigation measures which could be used. These are still at a low level of detail.
Scope of the cyber security proposal – level of detail

## Slide 9
Step 1: Certification of the OEM‘s organization and processes - implementation and assessment of the Cyber Security Management System (CSMS)
How to obtain Cyber Security certification
OEM implements a CSMS
Organization & processes implemented to ensure cyber security over the development, production and post-production phase and to cover the entire supply chain
It includes e.g. processes to identify, assess and categorize risks, processes used for testing the security, for monitoring, detection and response and processed used to keep cyber security current
The CSMS may be based on ISO/SAE 21434 „Cyber security engineering“
Assessment of the OEM‘s CSMS
National or Regional Authority assesses the CSMS of the vehicle manufacturer and whether it is compliant to requirements
Issuance of a CSMS Certificate of Compliance
The CSMS Certificate of Compliance is the prerequisite to obtain a cyber security certification, linked to vehicle architectures
The CSMS Certificate of Compliance has a max. validity of 3 years
National or Regional Authority may at any time verify its continued validity and act appropriately if the requirements are no longer met.

## Slide 10
Step 2: Vehicle certification- Development and Production to be in accordance with the CSMS
How to obtain Cyber Security certification
OEM develops the vehicle architecture
During the development and production the vehicle manufacturer has to employ the CSMS processes to ensure cyber security
Risk assessment to be conducted
Security/protection measures to be implemented
The effectiveness of security measures implemented needs to be tested and verified
Assessment of the vehicle
National or Regional Authority assesses the vehicle and whether it is compliant to the requirements
Issuance of certification
Requirements are established to ensure conformity of vehicles being produced

## Slide 11
        Cyber security shall be ensured over the lifetime of the vehicle. This implies e.g. that cyber security measures will have to be updated while the vehicle is in use.
        Things to note:
        New approach, not yet implemented in UN Regulations or GTR’s
        Different to “durability requirements” where requirements have to be met after 160000 km of use
        It is technically and economically challenging to predict changing environment over time and the future resource needed. For example at a certain point of time more than software updates may be required to ensure cyber security.
How to maintain compliance in the post-production phase?
Development
Production
Post- Production
010110010

## Slide 12
The vehicle manufacturer has to ensure that the processes of the CSMS, based on the requirements, are executed. The key requirements are monitoring for potential cyber attacks, detection of them and having a well exercised response plan.
Within the response plan the manufacturer may define a range of reponse options to pre-defined situations and trigger points for them. Implementation of some options (such as reducing vehicle functionility) may need discussion with regulatory bodies.
How to maintain compliance in the post-production phase?
Monitoring
Response
Detection

## Slide 13
What the proposal does:
    Provides a global baseline for vehicle cyber security
    Ensures best practice is incorporated into the design of vehicles
    Requires vehicle manufacturers to provide a reasoned argument as to why their vehicles are cyber secure (and the structure by which this should be done)
    Ensures there is ongoing support for vehicles post-production
What the proposal does not do:
    “Gold plate” by specifying specific vehicle designs or technologies
    Ensure vehicles cannot be hacked. No measure will be able to do this. The approach suggested will ensure the risk is minimised.
    Secure systems that interact with a vehicle but are outside of the vehicle manufacturer’s control (such as telecom networks or dongles)
    Specify how long monitoring and response procedures should be in place or what they should be
    List all possible risks and mitigations
Summary of the proposal

## Slide 14
How is the post-production phase covered?
Assurance assessment of a vehicle is not used for assessing post-production support as it is a test of a given configuration at a given point in time. It is therefore unsuitable for assessing ongoing processes. Instead the Cyber Security Management System (CSMS) is used.
Post production is addressed by the requirements for the CSMS
Vehicle manufacturers have to show the processes they implement to ensure cyber security during the development, production and post-production phase.
Requirement 7.2. of Annex A specifies, that the manufacturer has to implement processes to monitor for, detect and respond to cyber attacks.
This includes demonstrating how they will monitor for, and react to, new and evolving cyber threats.
Consequence of non-compliance If a vehicle manufacturer fails to maintain their CSMS, or serious deficienes are noted in it (for instance they are unable to detect or respond to a cyber attack) the national or regional authority may take appropriate action. This may include withdrawing the certificate.
Without a valid CSMS Certificate of Compliance the manufacturer would no longer able to apply for a new vehicle certification for Cyber Security. Continued production of existing certified vehicles may also be affected.
Questions & Answers

## Slide 15
2. Why is there not a fixed length of time for how long vehicles should be supported?
There are a number of reasons, including:
What needs to be supported to maintain cyber security may vary depending on the vehicle architecture/design.
Such a requirement cannot be adequately assured at the point of certification for a given vehicle, especially for an extended period of time e.g. 25 years (manufacturers may struggle to demonstrate that they and their supply base would exist for such a period).
Cyber security certification may not be relevant for vehicles no longer in production (=> production definitely discontinued).
Some methods of support, such as indefinite software support, may be impractical.
Some existing national/regional laws may supercede any stated UN requriement. This is comparable to serviceability, e.g. how long spare parts have to be provided. There are legal obligations are dealt with on national/regional basis. Examples of legislation which may be applicable include:
EU legislation on product liability (10 years)
National legislation on recalls (can be indefinite)
Recommendation: The issue, if of interest, will have to be addressed by the national/regional jurisdictions or UNECE may decide to develop a harmonized framework on this topic.
Questions & Answers

## Slide 16
3. What if a vehicle manufacturer is unable to maintain the support for a given vehicle?
The regulations do not address this. The issue is comparable to recalls due to safety/non-complaince issues. Such legal obligations are today dealt with on national/ regional basis.
A lack of support will not automatically make a vehicle unsafe/not secure and vice versa. For all vehicles there is a risk that there is a vulnerability which may be exploited. The risk will depend on possibility of an exploit, the ability/willingness of people to use it, and its outcome. A vehicle will only definitively become unsafe if there is a vulnerability found which has been exploited to affect its safety. A vehicle will be at risk of such exploitation until the vulnerability is fixed. The fix will depend on the vulnerability and its exploitation. Support should reduce the chance of a vulnerability being found and exploited but will not negate such risks. Under existing legal frameworks, it is up to an authority to decide whether a security issue requires the decommissioning of a vehicle, under which circumstances, with all it‘s consequences. This could be achieved on a case-by-case decision, dependent on the severity of the issue, number of vehicles affected, etc.
Recommendation: The issue, if of interest, will have to be addressed by the national/regional jurisdictions or UNECE may decide to develop a harmonized framework on this topic.
Questions & Answers

## Slide 17
4. Are there detailed test procedures specified for checking the cyber security of a vehicle?
No. Without knowing the system being submitted it is difficult to define detailed test procedures suitable for an assessment, especially due to the high complexity of vehicle systems.
An alternative approach was adopted. This is that the vehicle manufacturer shall provide a reasoned argument regarding the sufficiency of their measures and testing. This provides an appropriate method to certify a Cyber Security Management System and the ability to check which measures the vehicle manufacturer has implemented to ensure cyber security for a given vehicle.
An interpretation guidance document is being written during a test phase to help provide a consistent approach to assessments.
The recommendation section and annexes do include principles and mitigation measures which could be used for reference for during assessments.
Questions & Answers

## Slide 18
5. How will the risks and mitigations listed in Chapters 4 and 5 and their corresponding Annexes B and C be maintained?
Both sections note that they are not definitive and vehicle manufacturers should consider other sources to maintain an up to date appreciation of all possible risks and mitigations.
The maintenance of these sections could be achieved through a number of options, including:
Standards bodies (or other suitable bodies) could maintain the lists
WP29 could re-convene the working group periodically to update the lists if others are not adequately doing so
Recommendation: The issue, if of interest, should be considered in line with the recommendations in chapter 7 of the Recommendation.
Questions & Answers

## Slide 19
3. Overview on the test phase

## Slide 20
Aim of the „test phase“
=> Provide guidance on how to assess the requirements and documentation required
=> Verify the effectiveness/robustness of the requirements
=> Verify that certification authorities are able to reach the same conclusions based on identical OEM documentation
Next step – testing the proposal
Aim is to assure the proposal and not to test the products!

## Slide 21
Outputs of the „test phase“
=> Interpretation guideline
=> If necessary, proposals for clarifying the proposal
=> Report of the test phase to cover: - conclusions on the effectiveness /robustness of the proposal - verification that certification authorities/ are able to reach the same conclusions
Overview

## Slide 22
TFCS-14 Paris
04-05 Dec. 2018
GRVA-03 Geneva
24-27 Sep. 2019
Prep Report on TP
Identification of participants (latest feedback)
18 Jan. 2019
Preparation Phase
Proposed timeline for the test phase
Coordination Meeting 2
Jun/Jul 2019
Start Preparation Phase
Feb. 2019
Assessment Phase
Start Assessment Phase
May/June 2019
GRVA-02 Geneva
28 Jan. - 01 Feb. 2019
TFCS-16 TBC
Sept. 2019
TFCS-15
July 2019
Final Evaluation
Aug 2019
Coordination Meeting 1
Feb. 2019
Prep Final Interpret Doc V1.0
Reg. amendments
TFCS
Web
meeting
March 2019
TFCS
Web
meeting
June 2019