## Slide 1: Truck – Trailer data transmission for UN R79 Assistance functions, ISO 11992 standard
GRVA-04
September 2019
Informal document GRVA-04-34
4th GRVA, 24-27 September 2019 Agenda item 6(d)

## Slide 2: Motivation
Current situation
The trailer restricts the rear vision from the truck.
The truck does not beneficiate of sensors installed on the trailer
Proposal
With a standardized interface between truck and trailer, the truck would beneficiate of the sensors of the trailer, e.g. side sensor (short range), rear vision sensors (mid or long range), depending on the application (e.g. ACSF C, blind spot detection)
Note: the proposal applies to both truck/trailer combination and tractor/semi-trailer combination

## Slide 3: Principles
Principle of the proposed amendments to UN R79:
Reference to ISO 11992-1 (physical layer) and to ISO 11992-3:2020 (application layer)
Use of ISO 12098 15 pole connector
Implementation of similar requirements and technical Annexes as in UN R13

## Slide 4: Necessary Amendments
Concept of proposed amendments to UN R79-03
Amend Chapter 2: New definitions for the interface and data communication
Amend Chapter 5: New requirements specifying the interface
Amend Annex 8: Add new tests for towing vehicle and trailer individually
New Annex 9*
„Compatibility between towing vehicles and
trailers with regard to data transmission
according to ISO 11992 for environmental
monitoring“
New Annex10*
„Test method for evaluating the functional
compatibility of vehicles with electrical control
cables“
* similar to UN-R13/11

## Slide 5: Necessary Amendments
Concept of proposed amendments to UN R79-03
New Annex 9
„Compatibility between towing vehicles and trailers with regard to data transmission according to ISO 11992 for environmental monitoring“
General requirements
Messages from ISO 11992-03 for towing vehicle and Trailer, including the direction of the messages (source and destination)
1. General requirements
2. Content for the communication document
3. Towing vehicle
  requirements for the trailer simulation
  test methods
  Definition of the messages and error warnings to be checked
  possibly additional tests
4. Trailer
  requirements for the truck simulation
  test methods
  Definition of the messages and error warnings to be checked
  possibly additional tests
New Annex10
„Test method for evaluating the functional compatibility of vehicles with electrical
control cables“

## Slide 6: Next steps
Collect comments and questions by end of November 2019
Prepare necessary amendments to R79-03, in order to present a text proposal at next GRVA-05 of February 2020.