## Slide 1: Status of the Informal Working Group on ACSF
Summary of ACSF IWG Meetings – 22nd and 23rd Session
Informal document GRVA-04-36 4th GRVA session, 24. Sep – 27. Sep. 2019, Agenda item 4(c)
Submitted by the Chair of the IWG on ACSF
1

## Slide 2: Schedule of IWG on ACSF
22nd meeting was held from 9th to 11th April 2019 (Brussels, Belgium)
Small Drafting Group was held from 28th to 29th May 2019 (Berlin, Germany)
23rd meeting was held from 30th July to 1st August 2019 (Brussels, Belgium)
  IWG ACSF would like to present the current situation
  of discussions
<number>

## Slide 3
<number>
Overview of the discussion topics on requirements for Automated Lane Keep System on highways
    Scope
    General Requirements
    Activation, Deactivation and Driver Input
    Dynamic Driving Task, and Sensing Capabilities
    Driver Availability Recognition System
    Transition Demand and System Operation during Transition
    Minimum Risk Manouevre
    Emergency Mananouvre

## Slide 4
<number>
    Scope
The following set of requirements applies to “Automated Lane Keeping System (ALKS) for low speed application”, a system which is initiated/activated by the driver and which keeps the vehicle within its lane by influencing the lateral movement of the vehicle and controls the longitudinal movement of the vehicle for extended periods without further driver command/confirmation at the speed of [60] km/h or below.
This system applies to vehicles of categories M1.
Agreed principle

## Slide 5
<number>
    General Requirements
The activated system shall cope with all dynamic driving tasks and situations including failures.
If determined necessary, the activated system shall issue a transition demand with sufficient lead time.
The activated system shall comply with all relevant road traffic regulations in the country of operation.
Agreed principle

## Slide 6
<number>
    Activation, Deactivation and Driver Input
The system shall become active only upon a deliberate action by the driver and
all the following condition are met:
- The driver is in the driver seat and the driver’s safety belt is fastened,
- the driver is available to take over control of the dynamic driving task,
- no failure affecting the safe operation or the functionality of the ALKS
is present,
- DSSAD is operational,
- the environmental and infrastructural conditions allow the operation
and
- the vehicle is on roads where pedestrians and cyclists are prohibited
and which, by design, are equipped with a physical separation that
divides the traffic moving in opposite directions.
Agreed principle

## Slide 7
<number>
    Activation, Deactivation and Driver Input
It shall be possible to manually deactivate (off-mode) the system by an intentional action of the driver using the same means as to activate the system.
The means of deactivating shall provide protection against unintentional manual deactivation.
Driver override by steering, accelerating or braking shall be permissible
It shall be ensured the driver is in control of the vehicle at the time of the deactivation
How to confirm that ‘the driver is in control of the vehicle’ before deactivating the system
When the driver is responding to the transition demand, is it enough to confirm the driver is holding the steering control, or is it necessary to check additional criteria to confirm ‘the driver is in control of the vehicle’?
Discussion points
Agreed principle

## Slide 8
<number>
    Activation, Deactivation and Driver Input
What status should the driver assistance systems be after the ALKS deactivation?
Discussion point
<Option 1>
Return to the status which was at right before the ALKS activation (e.g. if the ACSF category B1 and ACC were ON, it is possible to return to the B1 and ACC mode)
<Option 2>
It is not permissive to shift to the functions which allow the driver remove his/her hands/foot off from the steering/accelerator/braking control (because the driver should become in charge of the steering/accelerator/braking control after the system deactivation to avoid his/her mode confusion)

## Slide 9
<number>
    Dynamic Driving Task, and Sensing Capabilities
The minimum following distance shall be calculated using the formula:
dmin = vALKS* tfront
Where:
dmin = the minimum following distance
vALKS = the actual speed of the ALKS vehicle in [m/s];
tfront = minimum time gap in seconds between the ALKS vehicle and a leading vehicle in front as per the table below:
Discussion point

## Slide 10
<number>
    Driver Availability Recognition
Driver presence:
        Check use of the seat belt
        Check driver’s presence in the seat
      It is desirable to establish detailed criteria for driver availability recognition, but on the other hand establishing standardized criteria can be difficult since it is still a technologically premature area and it may also lead to restricting future technological development.
Discussion point
Agreed principle

## Slide 11
<number>
    Transition Demand
System shall detect its limits and always issue a transition demand before/upon reaching the limits, System shall work properly during the whole transition phase
Transition phase shall be long enough for human drivers (not sleeping; no medical issues) to take over manual control again.
Warning during transition phase shall be escalating and demanding to encourage the driver to take over the control manually as soon as possible.
Vehicle is not allowed to be brought to standstill by the system during the transition phase except when the traffic situation requires it.
System shall be deactivated automatically after a transition phase except a MRM is started.
a minimum risk manoeuvre shall be started automatically, earliest [10 s] after the start of the transition demand
Agreed principle

## Slide 12
<number>
    Minimum Risk Manoeuvre
  Only starts after a transition demand if the driver has not taken over manual control.
  System shall be deactivated automatically after MRM.
  In case of severe vehicle failure or severe ALKS failure, it is permissible to directly initiate MRM without issuing transition demand
  If the system [is designed to / intends to] perform lane change manoeuvres during the MRM, should Lane change maneuver during MRM be allowed for the low speed ALKS?
  If lane change manoeuvres are to be allowed, it is necessary to discuss/develop additional requirements and test procedure but it may be difficult to complete within the timeframe of the current mandate.
Agreed principle
Guidance point

## Slide 13
<number>
    Emergency Manoeuvre (EM)
  Only allowed if traffic situation requires to prevent / mitigate
  imminent collision.
  Full deceleration capabilities of the vehicle and evasive manoeuvre
  in the lane allowed.
  No transition demand required; EM works in parallel with ongoing transition phase/MRM with higher priority for EM.
  After an Emergency Manoeuvre the system shall [continue to operate/initiate a transition demand].
  If the system is capable of confirming and has confirmed that no critical situation, should crossing the lane marking during the evasive manoeuvre be allowed for the low speed ALKS ?
  If crossing the lane marking during the evasive manoeuvre is to be permitted, it is necessary to discuss/develop additional requirements and test procedure but it may be difficult to complete within the timeframe of the current mandate.
Agreed principle
Guidance point
Discussion point

## Slide 14: Summary
IWG ACSF discussion is proceeding in conformity with the principles and the guidelines of the framework document.
IWG ACSF has made progress in defining core technical requirements for ALKS on highways, with many in-depth discussions about these very complex issues.
IWG ACSF focuses on only the low speed system in order to finalize the draft proposal for submission to 5th GRVA.
Work Plan until 5th GRVA:
Two IWG ACSF meetings (November in Barcelona, January TBD)
and several web-ex meetings are planned.
<number>