## Slide 1: Status of the Informal Working Group on ACSF
Summary of ACSF IWG Meetings – 24th and 25th Session
Submitted by the Chair of the IWG on ACSF
1
Informal document GRVA-05-25 5th GRVA session, 10 – 14 February 2020 Provisional agenda item 4(a)

## Slide 2: Schedule of IWG on ACSF
24th meeting was held from 18th to 20th November 2019 (Barcelona, Spain)
25th meeting was held from 21st to 24th January 2020 (Tokyo, Japan)
  IWG ACSF would like to present the draft regulation for ALKS and the last points for discussions
<number>

## Slide 3
<number>
Overview of the Draft UN Regulation No. [X]
    Scope and Purpose
    Definitions
    Applicatin of Approval
    Approval
    System Safety and Fail-safe Response
    Human Machine Interface / Operator Information
    Object Event Detection and Response
    Data Storage for Automated Systems – to be provided by EDR/DSSAD IWG
    Cybersecurity and Software Update – to be reviewed by CS/OTA TF
    Modification of Vehicle Type and Extention of Approval
    Conformity of Production
    Production Definitively Discontinued
    Names and Addressed of Technical Services Responsible for Conducting Approval Tests and of Typpe Approval Authorities
Uniform Provisions concerning the Approval of Vehicles with regard to Automated Lane Keeping System
    Annexes
    Communicatoin
    Arrangements of Approval Marks
    System Informatio Data
    Special Requirements to be Applied to the Safety Aspects of Electronic Control System [and Audit] - to be provided by VMAD IWG
    Test Specifications for ALKS

## Slide 4
<number>
    Scope & Definitions
This Regulation applies to vehicles of Category M1.
“Automated Lane Keeping System (ALKS)” for low speed application is a system which is activated by the driver and which keeps the vehicle within its lane at the speed of 60 km/h by influencing the lateral movement of the vehicle and controls the longitudinal movement of the vehicle for extended periods without further driver command.

## Slide 5
<number>
    System Safety and Fail-safe Response
    General Requirements
Perform all dynamic driving task, manage all situations including failures, and shall not endanger safety of vehicle occupants & other road users
Not cause any ‘rationally foreseeable and preventable’ collisions
Comply with traffic rules relating to the dynamic driving task in the country of operation
Exercise control over systems to maximize driver controllability (e.g. demist, windscreen, wipers and lights)
Continuously perform self-check
Implement measures to avoid reasonably foreseeable misuse/tampering
No activation of the system when the system can no longer meet the requirements of this Regulation
Implement process to manage the safety and continued compliance of the ALKS system over lifetime

## Slide 6
<number>
    Dynamic Driving Task
Keep the vehicle inside the lane in a stable lateral position
Detect a vehicle driving beside and adjust speed/lateral position
Maximum speed system is allowed to operate is 60 km/h
Adjust the distance to the vehicle in front
Bring the vehicle to a complete stop behind a stationary vehicle/road user/blocked lane of travel
Detect the risk of an imminent collision and perform EM
Avoid a collision with a leading vehicle decelerating up to full braking
Avoid a collision with a cut-in vehicle up the blow threshold:
Avoid a collision with pedestrian – UN R152 requirement to be satisfied
Present speed of the ALKS vehicle |  | Minimum time gap | Minimum following distance
km/h | m/s | s | m
7,2 | 2,0 | 1,0 | 2,0
10 | 2,78 | 1,1 | 3,1
20 | 5,56 | 1,2 | 6,7
30 | 8,33 | 1,3 | 10,8
40 | 11,11 | 1,4 | 15,6
50 | 13,89 | 1,5 | 20,8
60 | 16,67 | 1,6 | 26,7
The minimum following distance shall be calculated using the formula:
dmin = vALKS* tfront
𝑇𝑇𝐶𝐿𝑎𝑛𝑒𝐼𝑛𝑡𝑟𝑢𝑠𝑖𝑜𝑛 > 𝑣𝑟𝑒𝑙/(2∙6m/s²)+[0.35𝑠*]
*Parameters defining a manoeuvre that shall be avoided have to be reviewed.

## Slide 7
<number>
    EM
Carried out in case of an imminent collision risk
Longitudinal deceleration > 5.0 m/s² be considered to be an EM
Full braking performance a/o evasive manoeuvre in lane*
EM shall not be terminated unless the imminent collision risk disappeared or the driver deactivated the system
After EM is terminated the system shall continue to operate
If the EM results in the vehicle being standstill the signal to activate the hazard warning lights shall be generated
* Possibility of lane change is expected once appropriate technical requirements for such a function is established.

## Slide 8
<number>
    TD
    System shall detect its limits and always issue a transition demand with sufficient lead time
    System shall continue to operate work properly during the whole transition phase
    TD terminated when the system is deactivated or MRM has started
    a minimum risk manoeuvre shall be started automatically, earliest 10 s after the start of the transition demand
    Vehicle shall not be brought to standstill during TD (except required by the traffic situation (then hazard warning light within 5s)
    In case of severe ALKS or severe vehicle failure MRM may be initiated immediately
planned event: sufficiently before the event
unplanned event/failure: immediately upon detection

## Slide 9
<number>
    MRM
    During MRM the vehicle shall be slowed down inside the lane* or remain on an appropriate trajectory
    Aim of achieving a deceleration demand not greater than 4.0 m/s²
    The hazard warning lights shall be activated with the start of MRM (until deactivated manually)
    MRM shall only be terminated once the system is deactivated or the system has brought the vehicle to a standstill.
    The system shall be deactivated at the end of MRM
* Possibility of lane change is expected once appropriate technical requirements for such a function is established.

## Slide 10
<number>
    Driver Availability Recognition System
    Driver presence:
        Check driver’s presence in the seat (1 s)
        Check use of the seat belt
      When driver presence not confirmed, TD to be initiated
    Driver Availability:
      At least two individual criteria need to be met (rational of the criteria to be explained to TS) in the 30 sec interval
      When Driver Availability not confirmed, warning is provided until appropriate driver’s action detected or transition demand is initiated (15 s after warning)
Human Machine Interface/Operator Information

## Slide 11
<number>
    Activation, Deactivation and Driver Input
Dedicated means shall be provided for activation and deactivation
System shall be default off
Activation Conditions:
Deactivation Conditions:
During EM deactivation may be delayed
On deactivation of the system, there shall not be an automatic transition to any function which provides continuous longitudinal and/or lateral movement of the vehicle (e.g. ACSF-B1 System).
Driver Present,
Driver Available,
no failure affecting the safe operation/functionality of the ALKS is present,
DSSAD is operational,
the environmental and infrastructural conditions allow the operation,
positive confirmation of system self-check, and
the vehicle is on roads where pedestrians and cyclists are prohibited and which, by design, are equipped with a physical separation that divides the traffic moving in opposite directions and prevent traffic from cutting across the path of the vehicle
Dedicated means,
Driver override by steering (thresholds),
Driver override by braking + hands on steering, acceleration + hands on steering, or
TD/MRM + hands on steering + attentive

## Slide 12
<number>
    System Override
Thresholds need to be defined to avoid unintentional override/input
Driver Attentiveness shall be confirmed by following criteria:
Driver input to steering control (when the input exceeds a reasonable threshold): override the lateral control function of the system
Driver input to the braking control (resulting in a higher deceleration than that induced by the system or maintaining the vehicle in standstill by any braking system): override the longitudinal control function of the system
Driver input to the accelerator control (within fulfilling requirements): override the longitudinal control function of the system
Any driver input to the accelerator or brake control shall immediately initiate a TD
Driver gaze direction (road ahead),
Driver gaze direction (the rear view mirrors), or
Driver head movement,

## Slide 13
<number>
    Information to the driver
    - The following information shall be provided to the driver:
    Object Event Detection and Response
Forward detection range: min. 46 m
Lateral detecting range: to be sufficient to cover the full width of the lane immediately to the left/right
Declared detection range to be verified by TS
Manufacturer shall provide evidence that effect of wear and aging does not reduce sensing system performance below minimum detection range
System status: unavailability, display when activated, change to deactivation
Any failure affecting the operation of the system: optical
TD: optical + acoustic or haptic, and
after 4 s, escalation (of package of warning), haptic warning mandatory
MRM: optical + acoustic or haptic
EM: optical
Activation: dedicated optical signal (tell-tale and something more)
Deactivation: acoustic (unless deactivation after TD)

## Slide 14
<number>
Para | Description | No Object | Passenger Car |  |  | Powered Two Wheeler |  |  | Pedestrian |  |  | Obstacle |  | 
 |  | RM | RM | EM | NAS | RM | EM | NAS | RM | EM | NAS | RM | EM | NAS
4.1 Lane Keeping |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Lane Keeping and stability | X |  |  |  |  |  |  |  |  |  |  |  | 
 | Parallel vehicle drifting towards ego vehicle |  | X |  |  | X |  |  |  |  |  |  |  | 
4.2 Avoid a collision with a road user or object blocking the lane |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Stationary vehicle |  |  |  |  | X |  |  |  |  |  |  |  | 
 | Stationary adult pedestrian |  |  |  |  |  |  |  | X |  |  |  |  | 
 | Adult pedestrian crossing the lane |  |  |  |  |  |  |  | X | [X] |  |  |  | 
 | Object representing a blocked lane |  |  |  |  |  |  |  |  |  |  | X |  | 
 | Object partially blocking the lane |  |  |  |  |  |  |  |  |  |  | X |  | 
 | Multiple obstacles in the lane |  |  |  |  | X |  |  |  |  |  |  |  | 
4.3 | Following a lead vehicle |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Following Distance Test |  | X | X |  | [X] | [X] |  |  |  |  |  |  | 
 | [Following Stability Test (lateral offset)] |  | X |  |  | [X] |  |  |  |  |  |  |  | 
4.4 | Lane Change of another vehicle into the lane |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Cut in Tests with an accelerating cut in vehicle |  | X |  |  | [X] |  |  |  |  |  |  |  | 
 | Cut in Tests with a constant speed cut in vehicle |  | X | X |  | [X] | [X] |  |  |  |  |  |  | 
 | Cut in Tests with a decelerating cut in vehicle |  | X | X | X | [X] | [X] |  |  |  |  |  |  | 
4.5 | Stationary obstacle after lane change of the lead vehicle |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Cut out Tests |  | X | X |  | X | X |  | X | X |  | X | X | 
4.6. | Field of view |  |  |  |  |  |  |  |  |  |  |  |  | 
 | [Dynamic Field of View Tests (Forward)] |  |  |  |  | [X] |  |  | [X] |  |  |  |  | 
 | [Dynamic Field of View Test (Lateral)] |  |  |  |  | [X] |  |  |  |  |  |  |  | 
Annex 5 Test Specifications for ALKS
RM | Regular Manoeuvre.
EM | Emergency Manoeuvre.
NAS | Non-Avoidable Situation.
 | Potential test area that can be selected by the technical service in addition to the mandatory testing. Note pass/fail criteria for NAS tests does not apply, mitigation strategy will be assessed by the technical service.
X | Mandatory test area to be tested by the technical service. Each ‘X’ indicates that a mandatory single test is to be carried out. Additional testing may be carried out in this area at the request of the technical service with varied parameters compared to the testing already performed.
X | Mandatory test area to be tested by the technical service. Each ‘X’ indicates that a mandatory single test is to be carried out. Additional testing may be carried out in this area at the request of the technical service with varied parameters compared to the testing already performed. Pass/fail criteria detailed within this regulation does not apply. However, the ALKS mitigation strategy will be assessed by the technical service.
Detail to be further reviewed

## Slide 15: Summary
IWG ACSF discussion is almost finished.
IWG ACSF focused only on the low speed system in order to finalize the draft proposal for submission to 5th GRVA.
Work Plan until 6th GRVA:
The last discussion points are to be discussed/finalized among the expert members
<number>