## Slide 1: Motivation of Cut-In Requirements
Additional explanation to paragraph 5.2.5.2.
of the draft UN Regulation for ALKS (GRVA-05-07)
Submitted by expert from Germany
Informal document GRVA-05-36
5th GRVA, 10-14 February 2020
Agenda item 4(a)

## Slide 2: Cut-In Requirements: Model for ADS Behavior
ALKS Vehicle
Intruding Vehicle
ALKS Vehicle
Intruding Vehicle
ALKS Vehicle
Intruding Vehicle
30 cm
No intervention required
Intervention assumed for original proposal
Intervention assumed for new proposal

## Slide 3: Cut-In Requirements: Intervention Concept
Monitor other traffic (continuously)
Decide Brake Intervention (instantanuously)
Transmission delay
Increase brake force
Full braking phase
Unpreventable: Avoidance not required. Do not switch strategy!
Preventable: Avoidance required
Decision too late TTC<TTCmin
Decision in time TTCTTCmin
1st Parameter: Ass. decision strategy
2nd Parameter: typical delay
3rd Parameter: typical jerk
4th Parameter: available deceleration

## Slide 4: Cut-In Requirements: Intervention Model
Start of Intervention
0
0
deceleration
relative speed
ALKS Vehicle
Intruding Vehicle
30 cm
ALKS decides intervention: other traffic enters lane by > 30 cm
ALKS monitors other traffic

## Slide 5: Cut-In Requirements: Intervention Model (2)
Start of Intervention
0
0
tdelay
tincrease, deceleration
deceleration
relative speed (avoidance case)
ALKS Vehicle
Intruding Vehicle
30 cm
ALKS decides intervention: other traffic enters lane by > 30 cm
ALKS monitors other traffic
decelmax
Decision in time TTCTTCmin

## Slide 6: Cut-In Requirements: Intervention Model (3)
Start of Intervention
0
0
tdelay
tincrease, deceleration
deceleration
ALKS Vehicle
Intruding Vehicle
30 cm
relative speed (mitigation case)
ALKS decides intervention: other traffic enters lane by > 30 cm
ALKS monitors other traffic
decelmax
Decision too late TTC<TTCmin

## Slide 7: Mathematical Model for Edge TTC
TTC for brake start to avoid collision with deceleration d:
Approximation (avoiding numeric integration) for jerk influence:
Take „dead time“ delay (command transmission etc) into accout:
=

## Slide 8: Parameter Derivation
1st Parameter: Ass. decision strategy
2nd Parameter: typical delay
3rd Parameter: typical jerk
4th Parameter: available deceleration
Assume an intrusion of 30 cm into lane can be considered critical (intrusion continuously monitored!)
Transmission in bus system, overcome actuator friction, …
100 ms (confirmed by manuf.)
Typical (own measurement): 0.4 – 0.6 s from 0 to 10 m/s²
New brake systems (own measurement): 0.15 s from 0 to 10 m/s² Assumed (conservative!) in DE/FR prop.: 0.5 s from 0 to 6 m/s²
Typical value from field data: 6 m/s² availabe also on wet roads.

## Slide 9
3rd Parameter: typical jerk
0.48 s from 0 to 9.9 m/s²
Parameter

## Slide 10
4th Parameter: available deceleration
Parameter

## Slide 11: Summary
DE/FR model assumes a continuous monitoring of traffic in adjacent lanes
DE/FR model assumes a critical condition and consequently a brake intervention when other traffic enters > 30 cm into ego lane
DE/FR model assumes a plausible delay (transmission, actuator friction) of 0.1 s
DE/FR model assumes a brake intervention with 6 m/s² reached in 0.5 seconds
These values have been shown to be realistic
DE/FR position: Automated vehicles should not be required to have a weaker perfomance than current ADAS-equipped vehicles

## Slide 12: Comparison of JP and DE/FR DTC values
Vrel (km/h) VLateral (m/s) | 0 | 10 | 20 | 30 | 40 | 50
0 | N/A | N/A | N/A | N/A | N/A | N/A
0.5 | 5.0 | 9.6 3.28 | 19.8 7.85 | 31.0 13.7 | 45.0 20.84 | N/A 29.27
1.0 | 5.0 | 6.6 2.45 | 13.7 6.18 | 22.0 11.20 | 32.3 17.51 | N/A 25.1
1.5 | 5.0 | 5.6 2.17 | 11.6 5.63 | 18.4 10.37 | 26.4 16.40 | N/A 23.71
1.8 | N/A | N/A 2.08 | N/A 5.44 | N/A 10.09 | N/A 16.03 | N/A 23.25