## Slide 1: Alternative Approach to UN R13 Type-IIA for Battery Electric Vehicles
GRVA-05
10-14 February 2020
Informal document GRVA-05-38-Rev.1 5th GRVA. 10-14 February 2020 Agenda item 8(c)

## Slide 2: Background
At the 2nd session of GRVA in January 2019, OICA and CLEPA were given the opportunity to present the document GRVA-01-27.
At the 4th session of September 2019, OICA presented document GRVA-04-30. The document invited the Contracting Parties to provide their comments to OICA by 31st of October 2019. OICA offered to address them with relevant proposals and justifications, in a proposal for the 5th session of GRVA.
The technical issue is that a Battery Electric Vehicle (BEV) is not able to pass the type IIA test with a fully loaded battery (the worst case for the test), unless the vehicle would be equipped with specific technical solutions like e.g. resistors with high-temp cooling system, extra batteries.
Such solutions would negatively impact the vehicle weight and autonomy, packaging (vehicle architecture) and cost, reducing the environmental and economic interest of BEVs.
The issue has been brought up to the table of GRVA in September 2018, OICA is now eager to make progress. What is at stake is to define a regulatory frame to enable the development of electric solutions for heavy vehicles.

## Slide 3: Rationales
The main challenge is to ensure the availability of sufficient free capacity in the batteries, to be able to pass the type IIA without using the brakes.
This can of course be done by always keeping a free capacity equivalent to the energy of a type-IIA, which would only be used manually by the driver (e.g. using a dedicated control). The major issue with that simplistic approach is that this permanently free capacity cannot be used for traction.
The interest of the proposed alternatives approach is to permit some smart charging strategies (e.g. based on route planning) to optimize the use of the installed battery capacity for the purpose of traction, while ensuring the driver is informed of the available endurance braking capacity and/or being warned if the service brake performance falls below a given threshold.
As an alternative to such smart charging strategies, a type-II test with increased performance is also proposed.

## Slide 4: Rationales
Our experience of BEVs on different type of usages (based on customers experience or simulations) shows the battery charge is in the vast majority of cases at a level providing sufficient performance for ensuring safety and users satisfaction, at a similar level as with current vehicles.
The worst case which is considered in the regulation to pass type-IIA test (fully charged battery) is something very seldom that the drivers should almost never experience. The proposals we are making now are aiming at ensuring this worst case preserves the safety level of BEVs.

## Slide 5
Current
(Requirements)
M3 class II, III & B + N3 ADR + N3 towing O4 trailers
Type-IIA
6km at 30kph
Slope 7%
(height -420m)
Don’t use service brakes !
Type-II
6km at 30kph
Slope 6%
(height -360m)
Hot-stop
3.3 m/s² (N3)
3.75m/s² (M3)
Other vehicles
BEV & Hybrid vehicles **
** Vehicles equipped with an ERB system of cat A or B

## Slide 6
M3 class II, III & B + N3 ADR + N3 towing O4 trailers
Possible Technical solutions to fulfill current Type-IIA
Add an Endurance Brake (e.g. a cooled resistor)
BEV & Hybrid vehicles **
** Vehicles equipped with an ERB system of cat A or B
Type-IIA
6km at 30kph
Slope 7%
(height -420m)
Don’t use service brakes !
X
kWh
Secure X kWh in the batteries
( X kWh = Type-IIA energy )
X kWh
These solutions limit the development of BEVs (increased weight, reduced autonomy, cost...)
Secure “less than X kWh” in the batteries and use a supplementary retardation means (e.g. a “small” cooled resistor)
Type-II
6km at 30kph
Slope 6%
(height -360m)
Hot-stop
3.3 m/s² (N3)
3.75m/s² (M3)
Other vehicles
Current
(Possible solutions)

## Slide 7
BEV & Hybrid vehicles **
** Vehicles equipped with an ERB system of cat A or B
+
Brake estimator
Warn the driver if performance is below:
3.3 m/s² (N3) 3.75m/s² (M3)
Type-IIA
+
Type-IV
Alternative to Type-IIA
Other vehicles
Type-II *
* Type-II with increased
Performance
Slope 7%
Hot-stop 5 m/s²
Secure free battery capacity to be able to stabilize speed in the forthcoming (predicted) downhill on the route of the vehicle (the system shall be able to secure at least the energy of a type-II)
+
Inform driver about the free battery capacity (i.e. the available retardation capacity)
OR
Type-IIA
6km at 30kph
Slope 7%
(height -420m)
Don’t use service brakes !
Type-II
6km at 30kph
Slope 6%
(height -360m)
Hot-stop
3.3 m/s² (N3)
3.75m/s² (M3)
Proposal
M3 class II, III & B + N3 ADR + N3 towing O4 trailers

## Slide 8
Thanks for your attention

## Slide 9
Backup slides (reminder)

## Slide 10: Technical background UN R13 - Type-II and IIA tests
Type-II
Downhill Behaviour Test
Type-IIA
Endurance Braking Performance Test
Scope
  M3 and N3
  Except vehicles submitted to Type-IIA
Service brake: no restriction
Pass criteria: Hot-stop performance after Type-II
  N3: 3.3 m/s²
  M3: 3.75m/s²
Scope
  M3 class II, III & B
  N3 ADR and/or authorized to tow cat. O4
Service brake: prohibited
  Pass criteria: Average speed of 30km/h (+/- 5 km/h)
6%
30km/h
6 km
7%
30km/h
6 km

## Slide 11: Technical background UN R13 – Definition of SoC *
2.21.4. “Electrical state of charge” means the instantaneous ratio of electric quantity of energy stored in the traction battery relative to the maximum quantity of electric energy which could be stored in this battery;
+
_
0%
+
_
50%
SoC
+
_
100%
* State of charge

## Slide 12: Technical background Description of the issue
BEV
7%
30km/h
6 km
General:
UN R13 Type-IIA test is not adapted to Battery Electric vehicles (BEV) technology.
Technical issue:
Technical Services requires Type-IIA to be conducted with a fully charged traction battery (i.e. the worst case).
In these conditions:
  The kinetic energy of the vehicle cannot be converted and stored in the traction battery,
  No endurance braking is available.
  Type-IIA cannot be passed without complex technical solutions highly impacting weight, packaging and cost, e.g. resistors and high-temp cooling system, extra batteries.  Such solutions kill the economical interest of BEV technology.
Type-IIA not feasible
An alternative approach is needed for BEVs

## Slide 13: Alternative to Type IIA Principles
BEV & Hybrid vehicles *
* M3 class II, III & B + N3 ADR and/or authorized to tow cat. O4, equipped with an ERB system of cat A or B
Type-II
Type-IIA
Type-IIA
Current way
Alternative approach
No change for vehicles not equipped with an ERB system
Brake estimator
Warn the driver if performance is below Type-II hot-stop requirements:
N3 = 3.3 m/s²
M3 = 3.75m/s²
30 +/-5km/h
30 +/-5km/h
hot-stop requirements:
N3 = 3.3 m/s²
M3 = 3.75m/s²
+
+