## Slide 1: Necessity of the traffic critical scenarios drafting at the SG1a group of VMAD IWG
Submitted by the IWG on VMAD
Informal document GRVA-05-62 5th GRVA, 10-14 February 2020
Agenda item 4(a)

## Slide 2
Basic structure of the DRAFT UN Regulation for ALKS
Regulation
Introduction
1. Scope and purpose
2. Definitions
3. Application for approval
4. Approval
5. System Safety and Fail-safe Response
6. Human Machine Interface / Operator
Information
7. Object Event Detection and Response
8. Data Storage for Automated Systems
9. Cybersecurity and Software-Updates
Modification of vehicle type and extension
of approval
11. Conformity of production
12. Penalties for non-conformity of production
13. Production definitively discontinued
Names and addresses of Technical Services
responsible for conducting approval tests
and of Type Approval Authorities
Annexes to the Reg.
1 Communication
2 Arrangements of approval marks
3 System information data
4 Special requirements to be applied to the safety aspects of electronic control systems [and Audit] (Informal doc. GRVA05-18,19)
New validation/test method drafted by VMAD IWG
Test Specifications for ALKS
Conventional test method drafted by ACSF IWG
(Annex DSSAD (Informal doc.GRVA05-31))
Drafted by DSSAD/EDR IWG
New Reg. for CS/SU (Informal doc.GRVA05-05-06)
Drafted by CS/OTA TF
Requirement
Validation

## Slide 3
Necessity of boundary of preventable/unpreventable for audit/assessment
Regulation
5. System Safety and Fail-safe Response
6. Human Machine Interface / Operator
Information
7. Object Event Detection and Response
5. System Safety and Fail-safe Response (Excerpt)
5.1. General Requirements
5.1.1. The activated system shall perform the dynamic driving tasks, manage all situations including failures, and shall not endanger the safety of the vehicle occupants or any other road users.
The activated system shall not cause any collisions that are reasonably foreseeable and preventable. If a collision can be safely avoided without causing another one, it shall be avoided. When the vehicle is involved in a detectable collision, the vehicle shall be brought to a standstill.
To inspect conformity of the vehicle with ALKS to this provision according to Annex 4, boundary of Preventable and unpreventable should be determined.
Requirement

## Slide 4
Annexes to the Reg.
1 Communication
2 Arrangements of approval marks
3 System information data
4 Special requirements to be applied to the safety aspects of electronic control systems [and Audit] (Informal doc. GRVA05-19)
New test method drafted by VMAD IWG
Test Specifications for ALKS
Conventional test method drafted by ACSF IWG
(Annex DSSAD?(Informal doc.GRVA05-?))
Drafted by DSSAD/EDR IWG
New Reg.for CS/SU (Informal doc.GRVA05-?)
Drafted by CS/OTA TF
Basic structure of DRAFT Annex 4(audit/assessment) ①
Annex 4
Special requirements to be applied to the functional and operational safety aspects of automated driving systems
1. General
2. Definitions
3. Documentation
3.1. Requirements
3.2. Description of the functions of "The System" including
control strategies
3.3. System layout and schematics
3.4. Safety concept of the manufacturer
3.5. Safety management system (Process Audit)
4. Verification and tests
5. Reporting by
6. Communication to the other type –approval authorities
(See appendix 3- Could also be annexed to the
Communication form)
7. Competence of the auditors/assessors
Appendix 1: Model assessment form for automated driving
systems
Appendix 2: Information document form for Automated Driving
System to be provided by the manufacturer for the
approval
(Appendix 3: Communication form?)
(Appendix 4: Traffic critical scenarios)

## Slide 5
Annex 4
Special requirements to be applied to the functional and operational safety aspects of automated driving systems
1. General
2. Definitions
3. Documentation
3.1. Requirements
3.2. Description of the functions of "The System" including
control strategies
3.3. System layout and schematics
3.4. Safety concept of the manufacturer
3.5. Safety management system (Process Audit)
4. Verification and tests
5. Reporting by
6. Communication to the other type –approval authorities
(See appendix 3- Could also be annexed to the
Communication form)
7. Competence of the auditors/assessors
Appendix 1: Model assessment form for automated driving
systems
Appendix 2: Information document form for Automated Driving
System to be provided by the manufacturer for the
approval
(Appendix 3: Communication form?)
(Appendix 4: Traffic critical scenarios )
Basic structure of DRAFT Annex 4(audit/assessment)②
(Excerpt)
3.4.4. The documentation shall be supported, by an analysis which shows, in overall terms, how the system will behave to mitigate or avoid hazards which can have a bearing on the safety of the driver, passengers and other road users.
The chosen analytical approach (es) shall be established and maintained by the Manufacturer and shall be made open for inspection by the Type-approval authority at the time of the type approval.
The Type-approval authority shall perform an assessment of the application of the analytical approach (es):
(a) Inspection of the safety approach at the concept (vehicle) level.
This approach shall be based on a Hazard / Risk analysis appropriate to system safety.
(b) Inspection of the safety approach at the system level including a top down (from possible hazard to design) and bottom up approach (from design to possible hazards). The safety approach may be based on a Failure Mode and Effect Analysis (FMEA), a Fault Tree Analysis (FTA) and a system-theoretic process analysis (STPA) or any similar process appropriate to system functional and operational safety.
(c) Inspection of the validation/verification plans and results including appropriate acceptance criteria. This shall include validation testing appropriate for validation, for example, Hardware in the Loop (HIL) testing, vehicle on-road operational testing, or any other testing appropriate for validation/verification.
The inspection shall confirm that each of the following items is covered where applicable under (a)-(c):
(i)-(iii) (omitted)
(iv) Identification of the relevant scenarios (including traffic critical scenarios defined in Appendix4) within the ODD and management method used to select scenarios and validation tool chosen

## Slide 6
Appendix 4: Traffic critical scenarios for ALKS①（Under discussion)
This Appendix defines traffic critical scenarios for Annex 4 of the regulation which needs to be divided into preventable and unpreventable, according to the requirement in the regulation which stipulates “The activated system shall not cause any collisions that are reasonably foreseeable and preventable.”
Preventable scenarios are those where the validation should prove that ALKS does not result in an accident.
Unpreventable scenarios are those where the validation should prove that collision mitigation strategy of ALKS should be implemented in an accident.
1. Traffic critical scenarios
Following three are traffic critical scenarios:
・Cut-in: the ‘other vehicle’ merges in front of the ‘ego vehicle’
・Cut-out: the ‘other vehicle’ exits the lane of the ‘ego vehicle’
・Deceleration: the ‘other vehicle’ decelerates in front of the ‘ego vehicle’
Each of these traffic critical scenarios can be created using the following parameters/elements:
・Road geometry
・Ego vehicle’s behavior/ manoeuvre
・Other vehicle‘s behavior/ manoeuvre
2. Performance model of ALKS
Traffic critical scenarios of ALKS are divided into preventable and unpreventable scenarios.
They are determined based on the performance model of the ALKS shown below;
〇 Human driver with ADAS model
In low-speed ALKS scenario, the avoidance capability required for the driver model is
braking control only. As a result, this driver model is separated into the following three
segments: “Risk perceive situation(Risk evaluation time)”; “Delay in time(Time duration from having
finished perception until starting deceleration)”; and, “Deceleration degree(Jerking time to full
deceleration) and Max. G-force(Full Deceleration)”.

## Slide 7
Appendix 4: Traffic critical scenarios for ALKS②（Under discussion)
〇 Performance model
To determine whether traffic scenarios are collision preventable or collision unpreventable, performance model factors [Risk perception points, risk evaluation time, Time duration seconds from having finished perception until starting deceleration, jerking time to full deceleration and full deceleration] shown below can be used as the performance model of ALKS considering attentive human behavior .
Merit of this model is that parameters can be set flexibly which is needed for audit/assessment.
[0.4sec]
Risk evaluation time
ds on
Risk perception point
・Performance model factors for vehicles (Under discussion)
 |  | Factors
・Risk perception point | lane change (cutting in, cutting out) | Deviation of the center of a vehicle over 0.375m from the center of the driving lane (Derived from research by Japan)
 | deceleration | Deceleration ratio of preceding vehicle and following distance of ego vehicle
・ Risk evaluation time |  | 0.4 seconds (Derived from research by Japan)
・Time duration from having finished perception until starting deceleration, |  | 0.75 seconds (Common data in Japan)
・Jerking time to full deceleration |  | 0.6 seconds (Derived from experiments by NHTSA and Japan)
・Full deceleration |  | 0.774G (Derived from experiments by NHTSA and Japan)