## Slide 1: Digital Tachograph : Information Day
Geneva, 27/10/2003
Digitac

## Slide 2: PRESENTATION Introduction 1. Type approval 2. How to put a digital tachograph into service? 3. Issuing of tachograph cards and Tachonet 4. Use of the digital tachograph and of tachograph cards 5. Maintenance of the digital tachograph
Agenda

## Slide 3: INTRODUCTION
Leo HUBERTS – EC

## Slide 4
Background and latest developments
Leo Huberts, European Commission,
Directorate for Energy and Transport
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 5
Short historical overview
1992: Commission launches Tachosmart
Digital tachograph with paper disks (Type 1A)
1994: first Commission proposal
Type 1A
1995: modified Commission proposal
Digital tachograph with smart cards (Type 1B)
1998: Council Regulation 2135/98
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 6
Objectives:
Improve enforcement
Enhance fair competition
Increase road safety
Maintain satisfactory social standards
“Whereas blatant infringements and fraud present a road safety hazard and
are unacceptable for reasons of competition for the individual driver who does
respect the rules”
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 7
Council Regulation (EC) No 2135/98:
Introduces basic provisions for a new type of digital recording equipment with mass memory (VU) and smart cards
Amends Council Regulation 3821/85 on recording equipment in road transport
Mandates Commission to define technical specifications for digital tachograph, assisted by MS committee
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 8
Technical specifications:
1998-2001: Discussions in the Tachograph Committee (CATP)
Nov. 2001: Proposal for a Council Regulation
(Annex 1B – requirements for construction, testing, installation and inspection)
Aug. 2002: Commission Regulation (EC) No 1360/2002 of 13 June 2002 adapting for the seventh time to technical progress Council Regulation (EEC) No 3821/85 on recording equipment in road transport (Annex 1B)
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 9
Annex 1B:
Definitions
General characteristics/functions for VU and cards
Construction and functional requirements for VU and cards
Installation of recording equipment
Checks: inspections and repairs
Card issuing
Type approval
Technical appendices
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 10: INTRODUCTION OF THE DIGITAL TACHOGRAPH
Implementation of the digital tachograph:
In order to help Member States implementing the digital tachograph, the Commission is supporting three projects:
Card Issuing Working Group, initiated and managed by URBA 2000 in cooperation with the French Ministry of Transport
Implementation of the Digital Tachograph, initiated and managed by the Swedish National Road Administration and Granturco & Partners
Tachonet project, managed by Getronics, in cooperation with the Card Issuing Working Group

## Slide 11
Time schedule for the implementation of the digital tachograph:
Article 2 of Regulation (EC) n° 2135/98
24 months from the date of publication of Annex 1B vehicles put into
service for the first time must be fitted with digital tachograph
21 months from the date of publication of Annex 1B Member States shall
take measures to ensure that they are able to issue driver cards
In the event that 12 months after the date of publication of Annex 1B EC
type approval has not been granted to any item of recording equipment
(VU’s + cards), the Commission shall propose to the Council (and the EP)
an extension of the 24 and 21months deadlines
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 12
Consequences of the time schedule:
Annex 1B has been published on 5/8/02
Digital tachographs must be fitted in new trucks by 5/8/04
Member States must be able to issue tachograph cards by 5/5/04
VU’s and cards should have been type approved by 5/8/03
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 13
Where are we now?
On the basis of statements, issued by certain tachograph manufacturers in January 2003, it became clear that there would be no type approved
equipment by 5/8/03
However, one tachograph manufacturer assured the Commission that he would be able to get type approval by the end of this year
Based on this statement the Commission decided not to propose an
extension of the implementation deadlines for the time being.
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 14
Latest developments:
At an informal meeting on 12 September the tachograph and vehicle manufacturers issued the following statements:
First type approved VU’s and cards expected in March/April 2004
Type approved VU’s need to be tested before they can be fitted in new vehicles
Vehicle tests are expected to start in January 2004 and end in January
2005
After performance of the tests vehicle manufacturers need approx. 6
months to start up mass production and user adaptation
Fitment of the digital tachograph: probably summer 2005
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 15
Next steps:
Given the latest developments the Commission will have to re-assess
the situation (Oct./Nov.)
Decision taken by the Commission will be communicated to all the
stakeholders
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 16
Position AETR countries:
EU legislation on digital tachograph will be incorporated in AETR
agreement.
At latest 4 years after entry into force of the relevant amendments the
digital tachograph will become mandatory in AETR countries (approx. 2008/2009)
Before digital tachograph becomes mandatory in AETR countries, they
will be faced with EU trucks equipped with digital tachograph and with
AETR based companies that will use trucks equipped with digital tachograph
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 17
Communication project:
DG TREN intends to set up a communication project to inform and
educate future users:
How to implement digital tachograph
How to use the digital tachograph
Help desk
Project will focus on national authorities.
In principle for EU Member States, but special workshops for AETR countries.
INTRODUCTION OF THE DIGITAL
TACHOGRAPH

## Slide 18: TYPE APPROVAL
Leo HUBERTS – EC

## Slide 19
Council Regulation (EC) n° 2135/98
Art. 5:
A Member State shall grant EC component type- approval to any type of recording equipment (…), to any model memory card which conforms to the requirements of (…) Annex 1B
TYPE APPROVAL

## Slide 20: TYPE APPROVAL
Commission Regulation 1360/2002 (Annex 1B):
Chapter VIII
Type-approval of recording equipment and tachograph cards
General points
Security certificate
Functional certificate
Interoperability certificate
Type approval certificate
Exceptional procedure: first interoperability tests

## Slide 21: TYPE APPROVAL
Type approval consists of four steps:
  Security evaluation
  Functional tests
  Interoperability tests
  Issuing of type approval certificate

## Slide 22: Security evaluation
ITSEC body
Accredited
ITSEC
Laboratory
Security tests in
accordance with
Appendix 10
Tachograph
recording equipment
or smart card
manufacturer
Test request
Successfully
passed
tests
Yes
Test
result
ITSEC
certificate
ITSE
certificate
TYPE APPROVAL

## Slide 23: Functional tests
Type approval authority
(Accredited)
Laboratory
Functional tests in
accordance with
Appendix 9
Tachograph
recording equipment
or smart card
manufacturer
Test request
Successfully
Passed
tests
Yes
Functional
certificate
Test
result
TYPE APPROVAL

## Slide 24: Interoperability tests
JRC laboratory
Ispra, Italy
Interoperability tests in
accordance with
Appendix 9
Tachograph
recording equipment
or smart card
manufacturer
Test request
ITSEC certificate
Functional certificate
Successfully
Passed
tests
Yes
Provisional Interoperability
Certificate valid for a maximum
of 6 months
JRC laboratory
Ispra, Italy
Test
result
TYPE APPROVAL

## Slide 25: TYPE APPROVAL
Exceptional procedure: first interoperability tests

## Slide 26: EC Type Approval
MS type approval authority
- ITSEC certificate
Functional certificate
Definitive Interoperability certificate
Certificate of Type Approval
TYPE APPROVAL

## Slide 27: Type Approved Tachograph equipment/cards
Copy of Certificate
of Type Approval
MS
type approval authority
JRC
Public web site
with list of type approved
recording equipment
and tachograph cards
models
TYPE APPROVAL

## Slide 28: HOW TO PUT A DIGITAL TACHOGRAPH INTO SERVICE ?
Andrew KELLY - UK

## Slide 29: DIGITAL TACHOGRAPH WORKSHOP APPROVAL
Approval for Digital Tachograph workshops will be SEPARATE / ADDITIONAL to analogue approval
Workshops will need Workshop Smart Cards for each technician
Technicians will need appropriate training before being issued with Smart Cards

## Slide 30
DIGITAL TACHOGRAPH WORKSHOP APPROVAL
There will be enhanced Security requirements for Digital tachograph workshops
Required equipment and work procedures need to be agreed with manufacturers before Approval Requirements can be set
Workshops will need to be conversant with handling and storing digital data

## Slide 31: New equipment*
Before a new recording equipment comes into full operation,
it must be installed in a vehicle, activated and calibrated.
When new equipment is installed in a new vehicle, these
three operations may take place at different times and/or in
different places
When new equipment is installed in an existing vehicle, these
three operations will be combined in one.
Installation
Activation
Calibration
Operation
End of life
* meaning a new 1B tachograph as opposed to a second hand 1B tachograph

## Slide 32: New equipment / Installation
The installation is performed by vehicle manufacturers, approved fitters or approved workshops
The vehicle manufacturer should pre-set, in the data memory, the vehicle parameters he knows (theoretical calibration)
Note: This does not require a workshop card
Unknown parameters (such as VRN) will default and appear as “?”
Security of signals is achieved by encryption, no mechanical seals are required other than securing the mechanical fitting of the sensor on the gearbox
At this stage the recording equipment accepts any vehicle parameters entered, and does not record activities, events or faults.
Installation
Activation
Calibration
Operation
End of life
Mounting of the recording equipment in a vehicle.

## Slide 33: New equipment / Activation
Installation of new equipment must be followed by activation
Activation is triggered by the first insertion of a workshop card into the Vehicle Unit
A vehicle manufacturer having installed new recording equipment must activate the same before the vehicle leaves the factory (Vehicle manufacturers therefore need workshop cards)
Installation
Activation
Calibration
Operation
End of life
Operation of activating the security enforcing functions
and the recording functions.

## Slide 34: New equipment / Calibration
This operation is performed by approved fitters or approved workshops and requires the use of a workshop card,
This operation is mandatory for new vehicles (confirmation of pre-set parameters and entry of parameters previously unknown such as VRN) as well as for second hand vehicles,
The recording equipment is then ready for full operation.
Installation
Activation
Calibration
Operation
End of life
Updating / Confirming vehicle parameters held in data memory
Vehicle parameters include identification:- VIN, VRN,
Characteristics:- w, k, l, speed limiter value, odometer value, time)

## Slide 35: Recording calibration data and activity
Within the memory of the recording equipment:
  Data relating to first calibration
  Data relating to last 5 calibrations*
  * Only the last one of a particular calendar day if several have been performed within that day.
Within the memory of the workshop card:
  Data relating to last 88 calibrations
  Sequential counter of all calibrations carried performed with that card
Installation
Activation
Calibration
Operation
End of life
Notes: <number>
<footer>
<header>
29/07/26
  The time span of those records should be largely sufficient to cover the time span of driver activities recorded (up to one year) and therefore to allow control officers to assess the validity of these activities.

## Slide 36: CARD ISSUING
Alison DAVIES - UK

## Slide 37
Personalised for use by the Driver
5 Year Validity Period
Holds an average of 28 days data
Driver must hold one card only
The Driver Card

## Slide 38
Used by approved tachograph fitters to install, activate, calibrate and
download the recording equipment.
One year validity period
Personalisation recommended
Issued with a PIN
The Workshop Card

## Slide 39
Allows the company to ‘Lock and Download Data’ recorded in the vehicle
unit.
5 year validity period recommended
The Company Card

## Slide 40
Used by enforcers to carry out roadside compliance checks.
2 year validity period recommended
Personalisation recommended
The Control Card

## Slide 41
Card Application Types
First Issue - First application for a tachograph card
Replacement - Issued when a card is lost, stolen or malfunctions
Exchange - Change of administrative data
Renewal - Issued when a card is renewed after 5 years

## Slide 42
Card Issuing Authority (CIA) Organisation
Centralised - database, application processing system, card personalisation & issue
De-Centralised - administrative desks for application processing with centralised database. Card personalisation either from central office or at administrative desks

## Slide 43
Considerations for setting up a CIA
Application processing system
Database to hold & maintain records
Contract with smart card supplier/personaliser
Certification Authority

## Slide 44
Best Practice Guide
Process Flow
Card Application
Manual Checks System Processing

## Slide 45
Best Practice Guide Categories
Mandatory Requirements
Best Practice Recommendations
Alternative Approach

## Slide 46
Best Practice Guide -
additional information
Contact Points
Terms and Definitions
Reference Documents
CD ROM

## Slide 47: TACHONET
Cyril MICHEL - France

## Slide 48: TACHOnet Project Objectives
Create a telematics network aiming at falicitating data exchange between national administrations in charge of the tachographs cards (as stated in Regulation n°3821/85 amended by Regulation n°2135/98)
TACHOnet network will:
  Ensure a reliable and secure exchange of necessary and sufficient data between the Member States issuing tachograph cards
  Make sure the exchange is done in the legal framework envisaged
  Impose only a set of limited constraints on the local systems managing the driver cards in the Member States
  Use the infrastructure and tools of the market (security, workflow…)
TACHOnet project is owned by European Commission DG TREN

## Slide 49: TACHOnet Business Actors
Clerks working for National Card Issuing Authorities (CIA)
Enforcers working for National Enforcement Authorities
Clerk @ CIA
Enforcer
Truck driver
Owns & uses
Applies for a card, asks for exchange, declare card status modification
Issues,
Checks,
Modifies
Checks,
Modifies
Controls during road checks
TACHOnet
XML Messaging
System

## Slide 50: Scope and Exclusions of TACHOnet
Organisational:
  Included:
    Central secure and reliable XML messaging system allowing competent authorities to exchange information about tachograph cards based on well defined and published interfaces
    Intelligent router between Member States (hub & spoke)
    Central logging/tracking for non-repudiation & statistics
    Access granted at Member State level using digital certificates handled by IDA PKI services.

## Slide 51: Scope and Exclusions of TACHOnet
Organisational:
  Not included:
    Establishment of drivers national file(s) is the responsibility of each Member State
    Access to the TACHOnet network from within the Member States is under the responsibility of each Member State

## Slide 52: Scope and Exclusions of TACHOnet
Business processes:
  Included:
    Check that an applicant for a card in a Member State does not already hold a valid card in another Member State
    Check the actual status of a tachograph card based on its number (useful for enforcement authorities)
    Information interchange about lost, stolen, defective or recovered cards, exchange of driver cards

## Slide 53: Scope and Exclusions of TACHOnet
Business processes:
  Included:
    Information interchange about the usage of a driving license number for an issued card
    Provide a central Greek or Latin to US/Ascii transliteration service
    Provide a central service for getting the Phonex search keys of a driver’s surname and first of first names
    Produce irrefutable statistics about activities (response by request, average response time/delay,…) for every Member State

## Slide 54: Scope and Exclusions of TACHOnet
Business processes:
  Not included:
    Check for driver license number by integrating calls to external systems

## Slide 55: Scope and Exclusions of TACHOnet
Technology:
  Included:
    Independent from the technical infrastructure hosting each national database
    Use of internet standards (XML, HTTP, Web Services) to make an easy and seamless integration with the Member States card issuing applications
    Strong security requirements (confidentiality, authentication and integrity using digital certificates)
    Asynchronous transactions (request, acknowledgement, response). The central XML Messaging system is designed to handle this

## Slide 56: Scope and Exclusions of TACHOnet
Technology:
  Not included:
    Each Member State card issuing application should be designed to handle such asynchronous TACHOnet transactions

## Slide 57: Scope and Exclusions of TACHOnet
Interfaces with other systems:
  Included:
    Interface with the different Member States card issuing applications using the TESTA-II network and the IDA PKI services

## Slide 58: Scope and Exclusions of TACHOnet
Interfaces with other systems:
  Not included:
    Development of the interfaces between the Member States card issuing applications and the central TACHOnet system is not in the scope of TACHOnet but under the responsibility of each Member State according the set of documentation supplied by TACHOnet
    TESTA-II network management is not under TACHOnet responsibility (TACHOnet is a user of TESTA-II)
    IDA PKI management is not under TACHOnet responsibility (TACHOnet is a user of IDA PKI)

## Slide 59: TACHOnet Timeline
Timeline:
  2001: Feasibility Study
  10/2002-03/2003: “Planning & Design” phase
    Carried out by Getronics
    Deliverables:TCN XML Messaging Reference Guide and TCN Network & Security Reference Guide
  10/2003-05/2004: “Implementation & Deployment” phase + “Integration Assistance” phase
    To be carried out by Getronics
  05/2004-…: Help Desk, Hosting & Maintenance phases

## Slide 60
1
2
TACHOnet Project Background & Objectives
TACHOnet Architecture

## Slide 61: TACHOnet Architecture
TACHOnet
XML Messaging
System

## Slide 62: TACHOnet Architecture

## Slide 63: TACHOnet Architecture
Centralized architecture (but no central database)
XML Messaging System (asynchronous)
Based on standard Internet protocols (XML, HTTP, Web Services)
Use of IDA PKI Services
Use of TESTA-II network

## Slide 64: TACHOnet Name Encoding Rules
The whole solution encompassing Name Encoding Rules is a combined application of the following principles :
  Manual Name Spelling Rules
  Transliteration of the driver’s surname, first names, place of birth and driving license number
  Computing Phonex search keys for a driver’s surname and first names

## Slide 65: TACHOnet Name Spelling Rules
Applying manual Name Spelling Rules when
   the CIA clerk, at first issue, keys in driver’s surname and first name read in their original encoding (Greek or Latin) from the driver’s driving license
   the enforcer, during road check, keys in driver’s surname and first name either read in their original encoding (Greek or Latin) from the driver’s driving license or told by the driver if he pretends having lost his paper

## Slide 66: TACHOnet Name Spelling Rules
Rules:
  Driver’s surname and first names spelled as on the driving license
  Name prefixes (d’, de, Mac, Von, Van,…) typed in first
  Name suffixes (Jr, II,…) typed in last
  Multiple names (Jean-Jacques, José Luis,…) fully keyed in
  Special characters (é, è, ä, ‘, -,…) fully keyed in

## Slide 67: TACHOnet Transliteration
Applying Transliteration when
   The CIA clerk or the enforcer wants to have the driver’s details transliterated into a more readable US/Ascii version (using the web interface that will be provided by TACHOnet for the transliteration services)
   The CIA application wants to store (in its local data store) the driver’s details in a US/Ascii version more understandable by its local data store and users (using the XML web services that will be provided by TACHOnet for the transliteration services)

## Slide 68: TACHOnet Transliteration
TACHOnet will provide transliteration service as:
  XML Web services so to be accessed “programmatically” by any CIA application
  A Web interface (on top of the XML Web services) so to be accessed by the CIA clerks via their browser
Examples:
  A given Latin-encoded surname like Obenlüneschloß will be transliterated into Obenluneschloss
  A given Greek-encoded surname like Παπαδοπουλος will be transliterated into Papadopoylos

## Slide 69: TACHOnet Phonex Search Keys
The Phonex search keys should be computed on a driver’s surname and first names in the following circumstances
   At first issue or when exchanging a driver’s card, the CIA application must store the driver’s details (along with the search keys) in its local data store. The CIA application may compute these search keys using its own algorithm
   TACHOnet receives a request (XML message) from a CIA application for checking a driver’s issued cards. TACHOnet should then compute the search keys for the given driver’s surname and first name, and insert them in the XML message it’s gonna broadcast to the other Member States (CIA applications).

## Slide 70: TACHOnet Phonex Search Keys
TACHOnet will provide Phonex service as:
  XML Web services so to be accessed “programmatically” by any CIA application
  A Web interface (on top of the XML Web services) so to be accessed by the CIA clerks via their browser

## Slide 71: TACHOnet Network
Use of EC private & secure TESTA-II network
TESTA-II connections:
  Either via National network
   free of charge (except National level)
   Equant provides only services concerning the connection between the national network router and the Eurogate.
   The responsibility of the connection between the Card Issuing Authority (CIA) and the national network is under the CIA and the National network contact. Equant will not intervene in that scenario.

## Slide 72: TACHOnet Network
Or via Direct leased-line connection
   free for 1st year only
   Installation charges + Monthly charges afterwards
   For France, Switzerland and maybe Sweden (others MS
  could benefit from a connection via a National Network)
Bandwidth required: 128 Kbits/s

## Slide 73: TACHOnet Sizing & Performance
Sizing (estimates):
  About 7500 daily issued driver cards in Europe
  About 4000 daily enforcer checks on foreign drivers in Europe
  The central TACHOnet system should support peak of 30 messages/sec
  Member States systems should support up to 50 messages/min
Perfomance (estimates):
  High availability (TACHOnet & Member States systems)
  High response time for online transaction (the end-user should have an answer in less than 1 minute)

## Slide 74: TACHOnet Business Processes
Card Issuing Authorities (CIA)
  Tachograph card – First issue
    Need for checking whether the applicant driver does already hold a card in another Member State.
    Warn the Member State having issued the driving license that a tachograph card has been issued using the driving license number.

## Slide 75: TACHOnet Business Processes
  Tachograph card – Exchange
    Warn the Member State having issued the card about the exchange of the card (InExchange and Exchanged).
  Tachograph card – Status modifications
    Warn the Member State having issued a card that it has been declared as lost, stolen, defective or handed in.

## Slide 76: TACHOnet Business Processes
Enforcers during road checks (accessing TACHOnet via the CIA system)
  The driver can show his card:
    Check the validity of the card (using its number and the code of the Member State having issued the card).
  The driver cannot show his card (lost or stolen):
    Check whether the driver does actually hold a valid card (as he pretends to) using the driver’s surname, first names, date of birth and the code of the Member State where the driver swears having received his lost card from.

## Slide 77: TACHOnet Business Processes
  Check the validity of the workshop card:
    Check the validity of the card (using its number and the code of the Member State having issued the card).
  Declare Card Status modification
    Warn the Member State having issued a card that it has been declared as lost, stolen, defective or handed in.
Others: statistics, auditing,…

## Slide 78: TACHOnet XML Transactions
Used to support TCN Business Processes
XML Transaction Types:
  CheckIssuedCards:
    Check based on driver’s surname, first names, date of birth [and driving license].
  CheckCardStatus:
    Check based on an existing card number and issuing MS code.
  ModCardStatus:
    Warn about card status modification (exchange, lost,…).
  IssuedCardDL:
    At card issuance, warn the MS having issued the driving license that a card has been issued using that driving license number.

## Slide 79: TACHOnet XML Messages
Message Types (XML messages):
  MS2TCN_<TransactionType>_Req:
    Initial XML message sent by a CIA/enforcer to TACHOnet
  TCN2MS_< TransactionType >_Req:
    XML message forwarded/broadcated by TACHOnet to a specific/all Member State(s)

## Slide 80: TACHOnet XML Messages
  MS2TCN_< TransactionType >_Res:
    XML message sent by the Member State(s) in response to the previous TCN2MS_<TransactionType>_Req message
  TCN2MS_< TransactionType >_Res:
    XML message sent by TACHOnet as final response (after having collected all answers or timeout) to the initial MS2TCN_< TransactionType >_Req message
Asynchronous exchange of XML messages

## Slide 81: USE OF THE DIGITAL TACHOGRAPH
Lars ANDERSSON – Sweden
Thierry GRANTURCO – G&P

## Slide 82: USE OF THE DIGITAL TACHOGRAPH
The digital tachograph, as a system, will have a deep and horizontal impact
in the field.
Its introduction will affect:
the way it will be type approved;
the way it will be put on the market, repaired and decommissioned;
the approval and the work of the approved workshops;
the enforcement methods;
the day-to-day business of industry.

## Slide 83
The digital tachograph, as a system will also introduce new problems
dealing amongst others with:
data protection;
security;
card issuing.
USE OF THE DIGITAL TACHOGRAPH

## Slide 84: USE OF THE DIGITAL TACHOGRAPH
THE TACHOGRAPH RECORDS DRIVERS ACTIVITIES
WHICH ONES ?

## Slide 85: USE OF THE DIGITAL TACHOGRAPH
DRIVING TIME:
The daily driving time period shall not exceed 9 hours.
It may be extended twice in a week to 10 hours.

## Slide 86: USE OF THE DIGITAL TACHOGRAPH
CONTINUOUS DRIVING TIME:
After 4,5 hours’ driving, the driver shall observe a break of at least 45 minutes, unless he begins a rest period.
This break may be replaced by breaks of at least 15 minutes each distributed over the driving period or immediately after this period.

## Slide 87: USE OF THE DIGITAL TACHOGRAPH
REST TIME:
In each period of 24 hours, the driver shall have a daily rest period of at
least 11 consecutive hours, which may be reduced to a minimum of nine consecutive hours not more than three times in any one week, on condition
that an equivalent period of rest be granted as compensation before the end
of the following week.
On days when the rest is not reduced, it may be taken in 2 or 3 separate
periods during the 24-hour period, one of which must be of at least eight consecutive hours. In this case the minimum length of the rest shall be increased to 12 hours.

## Slide 88: USE OF THE DIGITAL TACHOGRAPH
WORKING TIME/AVAILABILITY TIME:
Not clearly defined in the Regulation (EEC) n° 3820/85 but generally understood as being :
the time from the beginning to the end of work, during which the mobile worker is at his workstation, at the disposal of the employer and exercising his functions or activities;
The time during which he cannot dispose freely of his time and is required to be at his workstation, ready to take up normal work, with certain tasks associated with being in duty.

## Slide 89: USE OF THE DIGITAL TACHOGRAPH
The digital tachograph and/or the driver cards will have to record and store drivers’ activities :
Driving time (including continuous driving time)
Working time/availability
Rest
The activities are supposed to be recorded and stored so that the compliance
of these activities with the rules laid down in the AETR can be checked by
the enforcement officers.

## Slide 90: USE OF THE DIGITAL TACHOGRAPH
What are the main characteristics of the digital tachograph as described in
the proposed Appendix 1B of the AETR ?
It will be totally digital
It will be (as a device) tamper-proof
It will work with smart cards
It will output data through a printer, a downloading connector and
a display
It will allow drivers to enter manually some data
It will have an average of 365 days capacity memory

## Slide 91
THE DATA RECORDED
USE OF THE DIGITAL TACHOGRAPH
Notes: <number>
<footer>
<header>
29/07/26

## Slide 92
USE OF THE DIGITAL TACHOGRAPH
BY THE TACHOGRAPH
Notes: <number>
<footer>
<header>
29/07/26

## Slide 93
BY THE TACHOGRAPH
- concerning the vehicle : parameters, VRN and VIN
- concerning the tachograph : part number, manufacturer’s name, faults
- concerning the driver : name, first names and his/her diver card number
USE OF THE DIGITAL TACHOGRAPH
Notes: <number>
<footer>
<header>
29/07/26

## Slide 94
BY THE TACHOGRAPH
concerning the driving time: every driving time (if the driver does not insert
his driver card in the tachograph and starts driving, driving without a driver
card will be recorded)
- concerning the other drivers’ activities: rest, availability and work will be
recorded through manual entries in real time (mode switch)
USE OF THE DIGITAL TACHOGRAPH
Notes: <number>
<footer>
<header>
29/07/26

## Slide 95
ON THE DRIVER CARD
USE OF THE DIGITAL TACHOGRAPH
Notes: <number>
<footer>
<header>
29/07/26

## Slide 96
same information than in the tachograph concerning the vehicle and the
tachograph characteristics
concerning the driving time: every driving time but nothing when the driver
card is not inserted
- concerning the other drivers’ activities: rest, availability and work will be
recorded through manual entries “a posteriori” in the driver card but without
erasing anything already recorded
USE OF THE DIGITAL TACHOGRAPH
Notes: <number>
<footer>
<header>
29/07/26

## Slide 97: USE OF THE DIGITAL TACHOGRAPH
But the drivers’ activities will also be recorded with some other data
identifying notably:
his location at the start and at the end of his journey (entered manually by
the driver)
distances travelled through the odometer values
speed (detailed speed and over speeding)
events and faults (malfunctioning of the tachograph, the sensor, the card,
etc…)

## Slide 98: Data organisation V.U.
Equipment Identification
VU:
  Manufacturer Name, Address,
  Part number,
  Serial number,
  Software version,
  Date of manufacture,
  Approval number,
  Speed measurement range,
  First installation date
Sensor:
  Serial number,
  Approval number.
  First installation date
Drivers identification
Per insertion/withdrawal cycle:
  Driver name, first name,
  Card number, nation, expiry date,
  Insertion date & time, slot, odometer,
  Previously used vehicle:
    VRN & Nation
    Withdrawal date & time,
  Withdrawal date & time, odometer.
Midnight Odometer
Date, Odometer
Location
Driver card number, date & time,
  Country, region,
  Odometer
Activity data
Per activity:
  Card inserted (Yes/No),
  Slot (Driver/Co-Driver),
  Crew (Yes/No),
  Activity code Dr/Wk/Av/Re,
  Date & time start or duration.
Events
Per event:
  Dr. and Co-Dr. Card numbers at start and end,
  Date & time start and end,
  Nb of similar events this day.
Time adjustments
Per event:
  Workshop card number,
  Date & time old and new settings;
Overspeed
  Date of last speed control,
  Date of first event and Nb of events since,
Per longest event on a day:
  Card numbers,
  Date & time start and end,
  Maximum and average speeds,
  Nb of similar events this day.
Faults
Per fault:
  Dr. and Co-Dr. card numbers at start and end,
  Date & time start, end
Control activity
Date & time, Control card number, Type
Company data locks
Date & time, In Out
Company Card number, Name, Address
Speed (24 hours)
  per second
Repair
Security elements
Installation/Periodic inspection
  Date and time,
  Test station identification:
    Name, Address,
    Card number and expiry date,
  k,
  Vehicle identification:
    VIN, VRN & Registration country,
  Vehicle characteristics:
    w, l, speed limit.
  Time adjustment. Old and new values
Download control
Last download date and time,
Company identification:Name, Card number,
Download software version.

## Slide 99: Data organisation - Card
Card Information
ID
Chip:
  IC serial number
  IC manufacturing reference
Manufacturer:
  Card serial number
  Card manufacturer number
  Card personaliser ID
  IC identifier
Version:
  Application (=Driver card)
  Structure_Version (= 8K)
Driving License
  Lic Authority Nation
  Lic Issue Number
  Lic Authority Name
Vehicles used
Per calendar day and vehicle change:
  First use date & time, odometer,
  Last use date & time, odometer,
  VRN, Nation.
Activity Data
Per calendar day:
  Date,
  Distance travelled,
  Per Activities:
    Card inserted (Yes/No),
    Slot (Driver/Co-Driver),
    Crew (Yes/No),
    Activity Code (Dr/Wk/Av/R),
    Start time.
Location
Per daily work period begin and end:
    Date & time, Odometer,
    Country, (region).
Security elements
Control
Date & time,
  Control Card number,
  Control Type,
  VRN, Nation.
Events
Event code,
  Date &time begin and end,
  VRN, Nation.
Faults
Fault code,
  Date &time begin and end,
  VRN, Nation.
Driver card info
  Issuing Nation
  Card Number, Repl, Index
  Issue Date
  Issuing Authority Name
  Driver Name, First names
  Driver Birth date
  Beginning of validity date
  Expiry date

## Slide 100: USE OF THE DIGITAL TACHOGRAPH
Vehicle’s related data
the tachograph
the calibration data
the vehicle
the drivers
the activities of all the drivers who drove the vehicle
locations
odometers
detailed speed and over speeding
events and faults of both the VU and the DC
the enforcement officers/bodies and the type of
control
VU
DC
Card holder’s related data
identity of the driver
driving license number
the activities performed by the diver in all the
vehicles he drove
locations
odometers
events and faults of both the VU and the DC
the enforcement officers/bodies and the type of
control

## Slide 101: USE OF THE DIGITAL TACHOGRAPH
Equipment identification data
Security elements
Driver card insertion and withdrawal data
Driver activity data
Places where daily work periods start and/or end
Odometer data
Detailed speed data
Events and faults data
Calibration data
Time adjustment data
Control activity data
Company locks data
Download activity data
Specific conditions data
VU
Card identification data
Card holder identification
Driving license information
Driver card holder activity data
Places where daily work periods start and/or end
Odometer data
Events and faults data
Vehicles used data
Card session data
Control activity data
Specific conditions data
DC

## Slide 102: USE OF THE DIGITAL TACHOGRAPH
Examples of important data missing in the VU as far
as enforcement is concerned :
the activities performed by the driver, object of the
control, in other vehicles → see his/her driver card
the activities performed by the driver when away
from a vehicle → see eventually his/her driver card
VU
DC
Examples of important data missing in the DC as far
as enforcement is concerned :
- driving without his driver card → see eventually the
VU
- detailed speed

## Slide 103: Operational Modes / Data Read Access Rights
With his/her driver card, a driver can display, print all data related to him/herself, the other ones being “anonymous”
With his/her control card, a control officer can display, print, download ALL data,
With his/her workshop card, a fitter can display, print, download ALL data,
With its company card, a company can display and print all data not locked by another company,
Without card, all data can be displayed or printed except personal identification (Names and Card numbers) which is blinded. Access limited to 8 days.
Notes: <number>
<footer>
<header>
29/07/26

## Slide 104: Operational Modes / Data Read Access Rights
No Card
Driver Card
Control Card
Company Card
Download
Forbidden
Forbidden
All data
All data except for periods locked by other companies
Print Display
All data with personal identifiers blinded
All data except for periods locked by other companies
+
Idem No Card
All own data
+
Idem No Card
All data
Notes: <number>
<footer>
<header>
29/07/26

## Slide 105: USE OF THE DIGITAL TACHOGRAPH
ACCESS TO THE DATA

## Slide 106: USE OF THE DIGITAL TACHOGRAPH
The ways to get access to the data for the enforcement officers are:
- To download the VU’s and the driver card’s data to any laptop they could be
equipped with.
A control card is needed.
- To print the data from both the VU and the driver card.
No need to have a control card but without a control card, there are restrictions
to the access of the VU’s data.
- To display the data on the VU’s screen

## Slide 107: VU DATA DOWNLOADING / DEFINITION
Downloading the data from the VU and/or the DC will probably be the
most efficient way for the enforcement officers to have access to the data
Notes: <number>
<footer>
<header>
29/07/26
Current definition in Annex 1B also includes the memory of the driver card for downloading. DG VII propose to restrict downloading to VU only (because law enforcement on card data can not be considered as valid. Cards are anyway freely readable.

## Slide 108: VU Data Downloading / Physical Elements
IDE
VU
Cable
Connector
Company card
Control card
or Workshop card
Notes: <number>
<footer>
<header>
29/07/26

## Slide 109: VU Data Downloading / Physical Elements (Alternate Solutions)
Connection of IDE to a CAN connector,
Remote download from company premises (GSM based for example)
  Company card in IDE
  Allow VU to be “Multi-User” :one user using standard MMI and one
  user (company only) connected through back connector
  Security principles can remain the same
IDE
VU
Company card
CAN Bus
Notes: <number>
<footer>
<header>
29/07/26

## Slide 110: VU Data Downloading / Operational Procedure
The IDE is managing the download session (all orders come from the IDE).
The software running on the IDE will allow to start the download session (through a button, a menu option, ...)
Notes: <number>
<footer>
<header>
29/07/26

## Slide 111: VU Data Downloading / Operational Procedures
VU answers with data helping the control officer (or the operator or the workshop) to decide what he wants to download

## Slide 112: VU Data Downloading / Operational Procedures

## Slide 113: VU Data Downloading correspondence VU Data storage - Download Messages
Equipment Identification
VU:
  Manufacturer Name, Address,
  Part number,
  Serial number,
  Software version,
  Date of manufacture,
  Approval number,
  Speed measurement range,
  First installation date
Sensor:
  Serial number,
  Approval number.
  First installation date
Drivers identification
Per insertion/withdrawal cycle:
  Driver name, first name,
  Card number, nation, expiry date,
  Insertion date & time, slot, odometer,
  Previously used vehicle:
    VRN & Nation
    Withdrawal date & time,
  Withdrawal date & time, odometer.
Midnight Odometer
  Date, Odometer
Location
Driver card number, date & time,
  Country, region,
  Odometer
Activity data
Per activity:
  Card inserted (Yes/No),
  Slot (Driver/Co-Driver),
  Crew (Yes/No),
  Activity code Dr/Wk/Av/Re,
  Date & time start or duration.
Events
Per event:
  Dr. and Co-Dr. Card numbers at start and end,
  Date & time start and end,
  Nr of similar events this day.
Time adjustments
Per event:
Workshop card number,
  Date & time old and new settings;
Overspeed
  Date of last speed control,
  Date of first event and Nr of events since,
Per longest event on a day:
Card numbers,
  Date & time start and end,
  Maximum and average speeds,
  Nr of similar events this day.
Faults
Per fault:
  Dr. and Co-Dr. card numbers at start and end,
  Date & time start, end
Control activity
  Date & time, Control card number, Type
Company data locks
Date & time, In Out
  Company Card number, Name, Address
Speed (24 hours)
  per second
Repair
Security elements
Installation/Periodic inspection
Date and time,
  Test station identification:
    Name, Address,
    Card number and expiry date,
  k,
  Vehicle identification:
    VIN, VRN & Registration country,
  Vehicle characteristics:
    w, l, speed limit.
  Time adjustment. Old and new values
Download control
Last download date and time,
Company identification:
  Name, Card number, Download software version.
Notes: <number>
<footer>
<header>
29/07/26

## Slide 114: VU Data Downloading Correspondence VU Data storage Download Messages
Equipment Identification
VU:
  Manufacturer Name, Address,
  Part number,
  Serial number,
  Software version,
  Date of manufacture,
  Approval number,
  Speed measurement range,
  First installation date
Sensor:
  Serial number,
  Approval number.
  First installation date
Drivers identification
Per insertion/withdrawal cycle:
  Driver name, first name,
  Card number, nation, expiry date,
  Insertion date & time, slot, odometer,
  Previously used vehicle:
    VRN & Nation
    Withdrawal date & time,
  Withdrawal date & time, odometer.
Midnight Odometer
Date, Odometer
Location
Driver card number, date & time,
  Country, region,
  Odometer
Activity data
Per activity:
  Card inserted (Yes/No),
  Slot (Driver/Co-Driver),
  Crew (Yes/No),
  Activity code Dr/Wk/Av/Re,
  Date & time start or duration.
Events
Per event:
  Dr. and Co-Dr. Card numbers at start and end,
  Date & time start and end,
  Nr of similar events this day.
Time adjustments
Per event:
  Workshop card number,
  Date & time old and new settings;
Overspeed
  Date of last speed control,
  Date of first event and Nr of events since,
Per longest event on a day:
  Card numbers,
  Date & time start and end,
  Maximum and average speeds,
  Nr of similar events this day.
Faults
Per fault:
  Dr. and Co-Dr. card numbers at start and end,
  Date & time start, end
Control activity
Date & time, Control card number, Type
Company data locks
Date & time, In Out
  Company Card number, Name, Address
Speed (24 hours)
  per second
Repair
Security elements
Installation/Periodic inspection
Date and time,
  Test station identification:
    Name, Address,
    Card number and expiry date,
  k,
  Vehicle identification:
    VIN, VRN & Registration country,
  Vehicle characteristics:
    w, l, speed limit.
  Time adjustment. Old and new values
Download control
Last download date and time,
Company identification:
  Name, Card number, Download software version.

## Slide 115: VU Data Downloading Correspondence VU Data storage - Download Messages
Equipment Identification
VU:
  Manufacturer Name, Address,
  Part number,
  Serial number,
  Software version,
  Date of manufacture,
  Approval number,
  Speed measurement range,
  First installation date
Sensor:
  Serial number,
  Approval number.
  First installation date
Drivers identification
Per insertion/withdrawal cycle:
Driver name, first name,
  Card number, nation, expiry date,
  Insertion date & time, slot, odometer,
  Previously used vehicle:
    VRN & Nation
    Withdrawal date & time,
  Withdrawal date & time, odometer.
Midnight Odometer
Date, Odometer
Location
  Driver card number, date & time,
  Country, region,
  Odometer
Activity data
Per activity:
  Card inserted (Yes/No),
  Slot (Driver/Co-Driver),
  Crew (Yes/No),
  Activity code Dr/Wk/Av/Re,
  Date & time start or duration.
Events
Per event:
  Dr. and Co-Dr. Card numbers at start and end,
  Date & time start and end,
  Nr of similar events this day.
Time adjustments
Per event:
Workshop card number,
  Date & time old and new settings;
Overspeed
  Date of last speed control,
  Date of first event and Nr of events since,
Per longest event on a day:
Card numbers,
  Date & time start and end,
  Maximum and average speeds,
  Nr of similar events this day.
Faults
Per fault:
  Dr. and Co-Dr. card numbers at start and end,
  Date & time start, end
Control activity
  Date & time, Control card number, Type
Company data locks
Date & time, In Out
  Company Card number, Name, Address
Speed (24 hours)
  per second
Repair
Security elements
Installation/Periodic inspection
  Date and time,
  Test station identification:
    Name, Address,
    Card number and expiry date,
  k,
  Vehicle identification:
    VIN, VRN & Registration country,
  Vehicle characteristics:
    w, l, speed limit.
  Time adjustment. Old and new values
Download control
Last download date and time,
Company identification:
  Name, Card number, Download software version.

## Slide 116: VU Data Downloading Correspondence VU Data storage - Download Messages
Equipment Identification
VU:
  Manufacturer Name, Address,
  Part number,
  Serial number,
  Software version,
  Date of manufacture,
  Approval number,
  Speed measurement range,
  First installation date
Sensor:
  Serial number,
  Approval number.
  First installation date
Drivers identification
Per insertion/withdrawal cycle:
  Driver name, first name,
  Card number, nation, expiry date,
  Insertion date & time, slot, odometer,
  Previously used vehicle:
    VRN & Nation
    Withdrawal date & time,
  Withdrawal date & time, odometer.
Midnight Odometer
Date, Odometer
Location
  Driver card number, date & time,
  Country, region,
  Odometer
Activity data
Per activity:
  Card inserted (Yes/No),
  Slot (Driver/Co-Driver),
  Crew (Yes/No),
  Activity code Dr/Wk/Av/Re,
  Date & time start or duration.
Events
Per event:
Dr. and Co-Dr. Card numbers at start and end,
  Date & time start and end,
  Nr of similar events this day.
Time adjustments
Per event:
Workshop card number,
  Date & time old and new settings;
Overspeed
  Date of last speed control,
  Date of first event and Nr of events since,
Per longest event on a day:
  Card numbers,
  Date & time start and end,
  Maximum and average speeds,
  Nr of similar events this day.
Faults
Per fault:
  Dr. and Co-Dr. card numbers at start and end,
  Date & time start, end
Control activity
  Date & time, Control card number, Type
Company data locks
Date & time, In Out
  Company Card number, Name, Address
Speed (24 hours)
  per second
Repair
Security elements
Installation/Periodic inspection
Date and time,
  Test station identification:
    Name, Address,
    Card number and expiry date,
  k,
  Vehicle identification:
    VIN, VRN & Registration country,
  Vehicle characteristics:
    w, l, speed limit.
  Time adjustment. Old and new values
Download control
Last download date and time,
Company identification:
  Name, Card number, Download software version.

## Slide 117: USE OF THE DIGITAL TACHOGRAPH
Alternative for the control officers to get access to the VU’s and card’s data : the printouts.

## Slide 118: USE OF THE DIGITAL TACHOGRAPH
PRINTOUTS :
There are 6 types of printouts :
2 relate to the drivers’ activities: one comes from the VU, the other one from
the driver card;
2 relate to the events and faults: one from the VU, the other one from the
driver card;
1 concerns the technical data (vehicle, VU, etc…)
1 concerns the over speeding.

## Slide 119: Driver Activities - Print-out from the driver card

## Slide 120: Driver Activities - Print-out from the driver card

## Slide 121: Driver Activities - Print-out from the driver card

## Slide 122: Driver Activities - Print-out from the VU

## Slide 123: Driver Activities - Print-out from the VU

## Slide 124: Driver Activities - Print-out from the VU

## Slide 125: Driver Activities - Print-out from the VU

## Slide 126: Driver Activities - Print-out from the VU

## Slide 127: Driver card events & faults print-out

## Slide 128: Driver card events & faults print-out

## Slide 129: VU events & faults print-out

## Slide 130: VU events & faults print-out

## Slide 131: VU technical data print-out

## Slide 132: VU technical data print-out

## Slide 133: Overspeed print-out

## Slide 134: Overspeed print-out

## Slide 135: USE OF THE DIGITAL TACHOGRAPH
Third and last way to have access to the data :
via the display, the data being readable, two lines by two lines, in the same
order than the way they are shown on the various printouts

## Slide 136: MAINTENANCE OF THE DIGITAL TACHOGRAPH
Andrew KELLY - UK

## Slide 137
Maintenance of the digital tachograph
INSPECTIONS & DECOMMISSIONING

## Slide 138: Repairs
Any repair of the equipment must be followed by a calibration
Recording equipment manufacturers have not yet defined what elements will be repairable
It is likely that any workshop undertaking repairs would need ITSEC approval
Downloading of the VU data may be required before any repair is commenced
Installation
Activation
Calibration
Operation
End of life
Repairs
Any operation on a component of the recording equipment that requires to disconnect its power supply
or to disconnect it from other components, or to open it.

## Slide 139: Periodic Inspections
Must be performed at least once
within two years of the last inspection
Finalised by updating or confirmation of current parameters in data memory ( = calibration)
Also performed after any alteration to the vehicle parameters
Installation
Activation
Calibration
Operation
End of life
Periodic
Inspection
2 years Max
Set of checks to ensure the recording equipment works properly and that its settings correspond to the vehicle characteristics

## Slide 140: 2nd hand equipment
2nd hand equipment (removed
from another vehicle) may be
installed in any other vehicle
The equipment is still activated,
and therefore needs only to be
calibrated after installation.
Installation
Activation
Calibration
Operation
End of life
Periodic
Inspection
2 years
Max
Repairs /
Sale
Installation
2nd hand
equipment

## Slide 141: Data download
Installation
Activation
Calibration
Operation
End of life
Periodic
Inspection
2 years
Max
Repairs /
Sale
Installation
2nd hand
equipment
When a VU reaches the end of its life the data contained within the memory MUST be downloaded and kept for 12 months
Workshops will need to be able to supply downloaded data form the VU to the company that owns the data
In event of not being able to download data, a certificate of un-downloadability will be issued. [copy will be kept for 1 year]

## Slide 142
    All workshops across Contracting Parties can provide the necessary services from Day 1;
    Control of workshop activities by the Competent Authorities can be effective from Day 1
    Transport operators can get the service they need from any Contracting Party
Implementation of a full network of workshops would ensure that:
Network of workshops

## Slide 143
    Effective legislation will ensure compliance and a level playing field
    All qualified technicians will have received proper training and will continue to do so
    That the legal obligations to meet the deadlines of implementation can be supported by a full and effective network of workshops
Network of workshops

## Slide 144
In order for the implementation of digital tachographs to be effective, consideration should be given to a number of issues which will need to be in place, nationally, prior to the introduction of the digital tachograph in the AETR- (non-EU) countries for international road transport
A crucial implementation element which should be examined more closely are:
    Timing
Final observations

## Slide 145
It will be particularly important that,nationally, a network of approved workshops, trained fitters and on-line support services is available prior to the introduction of digital tachographs
Therefore, each country must give thought to how they will:
    Enable the provision of relevant national legislation concerning the authorisation of workshops and staff
    Ensure the availability and control of workshop cards
    Implement the processes required to approve and certify workshops
TIMING

## Slide 146
    Implement the setting up of a training programme for individual technicians in the use of workshop cards and the functions to be undertaken
    Address the requirements and installation of downloading equipment necessary for workshops to comply with the technical annex
    Ensure that other areas (such as the legal arrangements for handling downloaded data) can be dealt with
TIMING

## Slide 147: CONCLUSIONS
We have presented rapidly :
how a digital tachograph will be type approved;
how it will be put into service;
how cards will be issued;
how it will be used;
how its maintenance will be ensured.

## Slide 148: DIGITAL TACHOGRAPH : INFORMATION DAY
ANY QUESTIONS ?

## Slide 149
BYE BYE
Notes: <number>
<footer>
<header>
29/07/26