## Slide 1
History of Development of the Flexible Pedestrian Legform Impactor (Flex-PLI)
November 3rd, 2011
Japan
GTR9-C-04

## Slide 2
1. Back ground
2. History of Flex-PLI Development (Overview)
Contents

## Slide 3
1. Back ground

## Slide 4
- Pedestrian Injured Body Regions -
(USA, Germany, Japan, and Australia : All Age Groups : AIS 2-6)
1. Back ground
Head Protection Tests
Lower Limb Protection Test

## Slide 5
- Lower Limb Injured Parts and Contact Locations -
(USA, Germany, Japan, and Australia : Pedestrian Lower Limb : AIS 2-6)
1. Back ground, contd.

## Slide 6
- EEVC Pedestrian Lower Legform Impactor -
1. Back ground, contd.
Structure
Main unit
Femur (Rigid)
 Low Biofidelity
Tibia (Rigid)
 Low Biofidelity
Exterior
Knee Shearing
Displacement
Knee Bending
Angle
64 mm
Knee center
Upper Tibia
Acceleration
Instrumentation
Tibia Middle/Lower
No measurement Items
Injury Assessment
Items
Flesh
 Disposable Flesh Foam
 Sensitive to Temperature and Humidity
Confor FoamTM
Knee (Hard)
 Low Biofidelity
Knee Ligaments
(Steel plate)
Real-world
Accident Analysis
Otte et al, 2007
Main Concerns: (1) Low biofidelity and (2) Insufficient Measurement Items

## Slide 7
2. History of Flex-PLI Development (Overview)

## Slide 8
The Japan Automobile Research Institute (JARI) and the Japan Automobile Manufacturers Association, Inc. (JAMA) initiated the development regarding a biofidelic flexible pedestrian legform impactor (Flex-PLI) from 2001.
In 2002, its first version, Flex-PLI 2002, was made.
The impactor has Flexible Long bones (Femur/Tibia) and knee ligament restraint system like human ones.
Besides, the impactor has an capability to measure bending moment at multiple locations at Tibia and Femur.
Flex-PLI 2002
Femur
Flexible
Tibia
Flexible
Knee
spring
Knee
ligaments
Knee
Ligament Restraint
System
2. History of Flex-PLI Development (Overview), contd.
Measurement cables:
To measure bending moment at multiple locations at tibia and femur

## Slide 9
After the Flex-PLI 2002 development, several improvements were applied.
GRSP/Pedestrian Safety Informal Working Group (IG-PS WG) interested in the capability of Flex-PLI, then, Flex-PLI technical Evaluation Group (Flex-TEG) were settled in 2005 under the GRSP/IG-PS WG to evaluate the Flex-PLI capabilities as a regulatory tool from Flex-G.
Finally, the prototype of final version of Flex-PLI (Flex-GTR) were developed in 2009.
Flex-TEG members were evaluated Flex-GTR capabilities, then they approved the Flex-GTR capabilities in 2010.
After that, Flex-TEG chair country, Japan, submitted amendments regarding gtr and ECE to the GRSP using the Flex-GTR specifications, etc..
Flex-PLI
2003
Flex-PLI
2004
Flex-G
Flex-GT
Flex-GTR
Flex-PLI 2002
Femur
Flexible
Knee
spring
Knee
ligaments
Tibia
Flexible
Knee
Ligament Restraint
System
2. History of Flex-PLI Development (Overview), contd.

## Slide 10
Instrumentation
374 mm
Knee-PCL
Elongation
Knee-MCL
Elongation
Knee-ACL
Elongation
Knee-LCL
Elongation
137 mm
217 mm
297 mm
134 mm
214 mm
294 mm
Upper end of tibia
Femur-3
BM
Femur-2
BM
Femur-3
BM
Tibia-1
BM
Tibia-2
BM
Femur-3
BM
Femur-4
BM
BM: Bending Moment
Femur (Flexible)
High Biofidelity
Structure
Main unit
Exterior
Injury Assessment
Items
Tibia (Flexible)
High Biofidelity
Real-world
Accident Analysis
Otte et al, 2007
Knee (Ligaments restraint system)
High Biofidelity
MCL
LCL
ACL
PCL
MCL: Medial Collateral Ligament
ACL: Anterior Cruciate Ligament
PCL: Posterior Cruciate Ligament
LCL: Lateral Collateral Ligament
Flesh
Reusable
Low Sensitive to Temperature and Humidity
Synthetic Rubber
Specifications of Flex-GTR-prototype
Main Achievements: (1) High biofidelity and (2) Multiple Measurement Items

## Slide 11
The Flex-GTR had been developed based on the discussions with the Flex-TEG members.
Detailed information on discussions and achievements of the Flex-TEG regarding
  Biofidelity
  Performance/Injury Criteria
  Benefit
  Durability
  Reproducibility and Repeatability
  Vehicle Countermeasures
  of Flex-PLI are provided by another document.
2. History of Flex-PLI Development (Overview), contd.

## Slide 12
Thank you for your attention!