## Slide 1: U.S. TIRE STANDARDS RULEMAKING George J. Soodoo U.S. DOT/NHTSA
51st GRRF
February 4-8, 2002
Geneva, Switzerland

## Slide 2: TREAD ACT
HR 5164 signed into law on November 1, 2000
Transportation Recall Enhancement, Accountability, and Documentation (TREAD) Act
3 Sections relate to tire performance items

## Slide 3: SECTION 10 - TIRE STANDARD UPGRADE
Revise and Update tire standards FMVSS 109 and FMVSS 119
Rulemaking must be completed by June 1, 2002

## Slide 4: SECTION 11 - IMPROVED TIRE INFORMATION
Tire Labeling
  Improve labeling for consumers to easily identify tires involved in a recall
  Initiate rulemaking within 30 days
  Complete rulemaking by June 1, 2002
Inflation Levels and Load Limits
  Consumer information on tire load limits
  Consumer information on maintaining proper tire inflation levels
  No statutory deadlines established

## Slide 5: SECTION 13 - TIRE PRESSURE WARNING
Require a warning system in the vehicle to indicate when the tire is significantly under-inflated
Complete rulemaking by November 1, 2001
Requirement must become effective 2 years after completion of rulemaking

## Slide 6: NHTSA TIRE TESTING – PHASE 1
Purpose: To focus on developing proposals for a high speed test and endurance test.
Tested 12 brands with different sizes, speed ratings.
Shearography analysis before and after testing
Compared with a baseline FMVSS 109 or GTS-2000 proposal

## Slide 7: 9 P-METRIC TIRES TESTED
Bridgestone Potenza RE92
Pirelli P4000
Michelin Energy MXV4
Hankook Optimo Plus II
Dunlop D65 Touring
BFS Futura 2000 ATD
Firestone Wilderness AT
Cooper National XT 5000
Firestone ATX
P205/65R15 92H
P205/60R15 90H
P205/65R15 94H
P205/65R15 92H
P205/70R14 93T
P205/75R14 95S
P255/70R16 109S
P225/60R16 97S
P235/75R15 105S

## Slide 8: 3 LT TIRES TESTED
Michelin XPC 4x4
  LT235/70R16 105H; Load Range C
Goodyear Wrangler AT/S
  LT235/75R15; Load Range C
Yokohama Geolander H/T
  LT225/75R16 110S; Load Range D

## Slide 9: NHTSA TIRE TESTING – PHASE 2
Purpose: To focus on likely agency proposal for a high speed test and endurance test.
Tested 12 brands with different sizes, speed ratings.
Shearography analysis before and after testing

## Slide 10: 8 P-METRIC TIRES TESTED
Toyo Proxes H4
Uniroyal Tiger Paw
Dunlop D65 Touring
Goodyear Regatta 2
BF Goodrich Cientra Plus
Cooper Lifeliner II
Firestone Wilderness AT
Michelin XH4
P225/60R16 97H
P225/60R16 97H
P205/65R15 92T
P205/65R15 92T
P235/75R15 105S
P235/75R15 105S
P235/75R15 105S
P235/75R15 105S

## Slide 11: 4 LT TIRES TESTED
Pirelli Scorpion P/T
  LT235/75R16 104S; Load Range C
Yokohama Geolander A/T
  LT235/75R15 104S; Load Range C
Goodyear Wrangler H/T
  LT245/75R16 120R; Load Range E
Bridgestone R273 SWPII
  LT245/75R16 120Q; Load Range E

## Slide 12: BRIEF SUMMARY OF TEST RESULTS
Agency plans to place test results in the public docket when NPRM is published.
Expected date of NPRM publication: February/March 2002
All tires completed baseline Endurance test
As expected, more failures occurred at higher speed and at lower inflation pressure

## Slide 13: BRIEF SUMMARY OF TEST RESULTS
All tires completed baseline High Speed test (GTR proposal)
As expected, more failures occurred at combination of high load, low inflation and long duration
Failures included tread separation, belt separation, sidewall blowout, chunking

## Slide 14: PROPOSALS FOR REVISED FMVSS
Light Vehicle Standard for vehicles up to 10,000 lbs GVWR
  High Speed test: Upgraded
  Endurance test: Upgraded
  Low Pressure Performance test: New
  Bead Unseating test: Upgraded
  Road Hazard Impact test: Upgraded
  Aging Effects test: New

## Slide 15: HIGH SPEED TEST
ECE R30/proposed GTR method: Use rated speed of tire as basis for test speeds
FMVSS 109 method: Same minimum requirement for all tires but at higher speeds
Other alternatives: Use proposed GTR method but with specified limits for rated speeds
Examined all test variables: ambient temperature, load, inflation pressure, speed, and duration

## Slide 16: ENDURANCE TEST
Examine all test variables and appropriateness of values
FMVSS 109 method: Use same minimum requirement for all tires but with more stringent variables

## Slide 17: LOW PRESSURE PERFORMANCE TEST
Purpose: To evaluate tire performance at TPMS threshold
Endurance or high speed test for short duration
Test method: Establishes minimum requirements independent of speed rating of tire

## Slide 18: BEAD UNSEATING TEST
Considering alternative to current FMVSS 109 test
  Toyota Wedge test
  Vehicle testing conducted to assess correlation with bench test alternative

## Slide 19: ROAD HAZARD IMPACT TEST
Considering SAE J1981, Road Hazard Impact Test for Wheel and Tire Assemblies
Replacement for Strength (plunger) test
Test simulates a tire impacting a road hazard such as a pothole or curb

## Slide 20: AGING EFFECTS TEST
Three alternatives being considered for aging effects test:
  Oven aging
  Peel (Adhesion) strength using ASTM Standard D 413-98, “Standard Test Methods for Rubber Property-Adhesion to Flexible Substrate”
  Long-term durability endurance

## Slide 21: Effective Date
Agency considering a variety of options for effective dates including:
  Multi-year phase-in beginning with P-metric tires
  Would require production data to enforce
  Allow more time for LT tires
  Tie-in effective dates with TPMS effective dates

## Slide 22: PROPOSALS FOR LABELING REQUIREMENTS
NPRM issued on December 19, 2001
  NHTSA Docket No. 11157
  Applicable to vehicles with GVWR <10,000 lbs.
  Tire Identification Number
  Load Limits/Load Index
  Maximum inflation pressure
  Vehicle placard content & location
Next Step: Comment period closes February 19, 2002

## Slide 23: SUMMARY
Three Rulemakings in progress:
  Labeling NPRM
    Issued December 19, 2001
    Comment period closes February 19, 2002
    Final Rule by June 2002
  TPMS Final Rule: February 2002
  Comprehensive revision to the tire standards; NPRM expected February/March 2002