## Slide 1: Tire Pressure Monitoring Systems NHTSA Final Rule George J. Soodoo U.S.DOT/NHTSA
51st GRRF
Geneva, Switzerland
February 4-8, 2002

## Slide 2: Background
Congress mandated a final rule to require a warning system “in motor vehicles to indicate to the operator when a tire is significantly under-inflated” be completed by November 1, 2001
Congress mandated that this rule must take effect by November 1, 2003

## Slide 3: NHTSA Tire Pressure Survey
February 2001 nationwide survey of more than 11,000 vehicles at gas stations
Purpose was to learn about real-world inflation pressure levels
  Learned that trucks are typically more under-inflated than cars
  More than one-third of vehicles were at least 20% under for one tire
  More than one-fourth of vehicles were at least 25% under for one tire

## Slide 4: Under-inflated tires on cars
DP<= -10 psi # of tires | -10<DP<= -6 # of tires | -6<DP<= -3 # of tires | -3<DP<= 0 # of tires
1 or more: 17.4% | 1 or more: 24.5% | 1 or more: 39.7% | 1 or more : 46.7%
2 or more: 5.8% | 2 or more: 10.7% | 2 or more: 20.6% | 2 or more: 26.7%
3 or more: 2.5% | 3 or more: 5.8% | 3 or more: 9.0% | 3 or more: 12.6%
All 4 tires: 1.8% | All 4 tires: 2.8% | All 4 tires: 4.1% | All 4 tires: 5.0%

## Slide 5: Under-inflated tires on LTVs
DP<= -10 psi # of tires | -10<DP<= -6 # of tires | -6<DP<= -3 # of tires | -3<DP<= 0 # of tires
1 or more: 19.7% | 1 or more: 30.1% | 1 or more: 43.7% | 1 or more : 44.2%
2 or more: 8.4% | 2 or more: 13.7% | 2 or more: 25.7% | 2 or more: 25.0%
3 or more: 3.2% | 3 or more: 7.8% | 3 or more: 12.5% | 3 or more: 12.7%
All 4 tires: 2.0% | All 4 tires: 4.8% | All 4 tires: 5.1% | All 4 tires: 6.1%

## Slide 6: NHTSA Tire Pressure Research
Met with all known suppliers of tire pressure monitoring systems
Met with vehicle and tire manufacturers to learn of their experience with these systems
Evaluated our data to identify crashes and injuries that could be addressed by these monitoring systems

## Slide 7: Types of TPMS
Indirect Systems
  Work with ABS wheel speed sensors; as inflation pressure drops, radius of tire decreases and rotational speed of wheel increases
  As relative rotational speed increases above programmed level, system warns driver of under-inflation
  Currently offered on a few cars (e.g., Oldsmobile Alero) and some vans (Toyota Sienna and Ford Windstar)

## Slide 8: Types of TPMS
Direct Systems
  Use a pressure sensor in each wheel to directly measure pressure in each tire
  Transmit data via a wireless radio frequency transmitter to a central receiver that monitors the data and connects to a display mounted inside the vehicle
  Currently offered on a few high-end cars (Chevrolet Corvette and BMW and Mercedes models)

## Slide 9: Definition of Significantly Under-inflated
There is no “bright line” divide where a tire is “significantly under-inflated”
  As tire becomes more under-inflated, stress on tire increases and risk of failure increases
Proposed two alternative definitions of “significantly under-inflated” to reflect different possible views of that term

## Slide 10: Alternative 1 in NPRM
Require driver to be notified when 1 to 4 tires are 20% under recommended inflation pressure or at 20 psi, whichever is greater
  Essentially requires direct systems in the near term
  This choice requires the most-capable current system, so it both ensures the greatest safety benefits and costs more

## Slide 11: Alternative 2 in NPRM
Require driver to be notified when 1 to 3 tires are 25% under recommended inflation pressure or at 20 psi, whichever is greater
  Permits both direct systems and improved indirect systems
  This choice permits continued use of indirect systems, so it results in lower costs, but the lesser performance results in lesser safety benefits

## Slide 12: Low Tire Pressure Activation
Tire Type | Max. Inflation Pressure (kPa) | Min. Activation Pressure (kPa)
P-metric - Standard | 240 300 350 | 140 140 140
P-metric – Extra Load | 280 340 | 160 160
LT load range C | 350 | 200
LT load range D | 450 | 260
LT load range E | 550 | 320

## Slide 13: Benefits and Costs Estimate
NHTSA estimates that Alternative 1 would prevent 79 deaths and 10,635 injuries, annually, at an average cost of $66 per vehicle.
Alternative 2 would prevent 49 deaths and 6,585 injuries, annually, at an average cost of $31 per vehicle.
When fuel and tread-wear costs factored in, net costs per vehicle are $23 and $9 respectively

## Slide 14: Comments on NPRM
Comment period closed September 6, 2001
Received 153 comments from private citizens, vehicle manufacturers, tire manufacturers, TPMS manufacturers, consumer advocacy groups
No surprises – advocacy groups and tire mfrs want better-performing system, vehicle mfrs want least-expensive system, TPMS mfrs want whatever they produce to be specified, and the public is split
Four major issues

## Slide 15: Major Issue 1 – Benefits and Costs
Vehicle manufacturers and one TPMS manufacturer commented that the agency has understated the costs of both direct and indirect systems and dramatically overstated the safety benefits
Agency has revised Benefits and Costs estimates for the final rule

## Slide 16: Major Issue 2 – TPMS Reliability
Ford and a manufacturer of indirect TPMS commented that NHTSA’s assumption that direct TPMS is highly reliable is not consistent with their experience
TRW makes both direct and indirect systems, says reliability is unknown, but doesn’t believe it will be a problem
Agency acknowledges that these systems are new technology that are not widely used now and reliability is unknown – Proposed phase-in (Issue 5) allows gradual introduction so we can monitor real-world reliability

## Slide 17: Major Issue 3 – Choice of Alternatives
Alternative 1 – Requires Direct Systems (20% underinflation of 1 to 4 tires)
Comments
  Strongly endorsed by consumer advocacy groups, tire manufacturers, and manufacturers of direct TPMS – best system that gives driver best information
  Vehicle mfrs generally say it’s too early in development of tire sensing technology to rule out a technology at this time + benefits of this are not substantially greater than allowing indirect systems as well

## Slide 18: Major Issue 3 – Alternative 2
Alternative 2 – Permits either Direct Systems or Improved Indirect Systems (25% under-inflation of 1 to 3 tires)
Comments
  Vehicle manufacturers prefer flexibility to use both types of systems, but argue that this alternative is too stringent to permit continued use of current indirect systems
  They asked agency to consider an alternative that requires system to detect 30% underinflation of 1 tire only

## Slide 19: Major Issue 3 – Alternative 2 (Cont’d)
Comments
  Indirect TPMS mfr (Sumitomo) supports Alternative 2 and supports 1 to 3 tires
  TRW says indirect can be improved to detect 25% below placard, but not by Nov. 2003 – modifications will make system cost 60% of direct system
  Toyota noted Congressional sponsor of this provision cited Toyota’s indirect system as what mfrs should provide on all vehicles – suggests Congress didn’t want indirect systems to be excluded

## Slide 20: Major Issue 3 – Alternative 3
Alternative 3 – In response to comments, establish a requirement that permits the performance achievable by currently-offered indirect TPMS on Toyota Sienna, etc. (30% underinflation on any 1 tire)
Comments
  Supported by by vehicle manufacturer associations, based on legislative intent and belief benefits are equivalent to Alternative 1
  Continental Teves (indirect TPMS supplier) also favors this option

## Slide 21: Major Issue 4 – Phase-in
NPRM proposed to make this effective for all vehicles under 10,000 lbs GVWR in 2 years (Nov 2003), asked for comments on need for phase-in
Comments
  Most vehicle manufacturers proposed a 4-year phase-in: 15%, 35%, 70% and 100% of production
  Honda proposed a 4-year phase-in at 10%, 40%, 70% and 100%
  Subaru and TRW supported the agency’s NPRM suggested 3-year phase-in of 35%, 65% and 100%

## Slide 22: Vehicle Applicability
NPRM Proposed applicability for light vehicles with a gross vehicle weight rating (GVWR) of 10,000 lbs or less
Comments
  Limit to vehicles under 8500 lbs
  Exempt vehicles built in more than one stage

## Slide 23: Replacement Tires/Rims
NPRM Proposed
  TPMS must meet requirements with all optional and replacement tire/rim sizes recommended by vehicle manufacturer for that vehicle
Comments
  Vehicle manufacturers want to limit applicability to tires (brands and sizes) and rims specified by the vehicle manufacturer
  Aftermarket firms/Consumer groups want TPMS to work with all replacement tires and rims

## Slide 24: Summary – Decision Issues
Agency to decide on the following in Final Rule:
  Warning activation threshold
  Number of tires monitored; include spare tire??
  Duration of warning
  Telltale symbol: ISO or other symbol
  TPMS operation with replacement tires and rims
  Vehicle application
  Effective date by production volume; duration of phase-in