## Slide 1: Motorcycle Brake Testing
U.S. DOT/NHTSA
George J. Soodoo
February 2002

## Slide 2: Introduction
Purpose: To assess state of motorcycle braking performance
Tested motorcycles in each of 5 categories: Sport, Cruiser, Touring, Dual Purpose, Scooter
Performance evaluated with application of front brake, rear brake, and both brakes together
Evaluated antilock brake system (ABS) on Touring bike
Evaluated linked braking system (LBS) on Sport bike

## Slide 3: Motorcycle Crashes 1990-1999
Over-40 age group accounted for 39% of fatalities in single vehicle crashes in 1999, up from 14% in 1990
42% of all age group fatalities involved intoxicated riders
Bikes with engine displacement above 1000 cc were involved in 33% of fatalities in 1999, up from 22% in 1990
Single vehicle crashes account for about 45% of all motorcycle fatalities

## Slide 4: Crash Avoidance Maneuvers
Steps rider took to avoid crash
  22% of motorcycle fatalities were related to braking or steering maneuvers
  Fatalities related to braking has fluctuated slightly between 1990 and 1999 but remains at 13%
  30% of fatalities were attributed to no maneuver taken to avoid crash
Vehicle maneuver prior to crash
  One-half of the motorcycle fatalities occurred when the vehicle was negotiating a curve

## Slide 5: NHTSA Plans??
To understand causes of increased motorcycle fatalities by additional crash data analysis
To understand role crash avoidance systems play in potential crash reduction
To continue research to evaluate brake system performance
To seek ways to improve brake performance through harmonization and/or upgrade of FMVSS 122

## Slide 6: Category/Test Vehicles
Sport: Honda VRF800F with linked braking system (LBS)
Cruiser: Harley-Davidson Superglide Sport
Touring: BMW R1100 RT with antilock braking system (ABS)
Dual Purpose: Kawasaki KLR 650
Scooter: Yamaha Riva 125

## Slide 7: Braking Test Maneuvers
30 mph on Dry Asphalt SN 85
60 mph on Dry Asphalt SN 85
80 mph on Dry Asphalt SN 85
30 mph on Wet Asphalt SN 55
30 mph on Polished Concrete
30 mph in a corner on Dry Asphalt
30 mph on Dry Belgian Block
30 mph on Wet Belgian Block
30 mph on Dry Asphalt with wetted brakes
Brake Fade and Recovery Evaluation

## Slide 8: Evaluation Criteria
Brake temperatures
Brake lever/pedal application load
Average Stopping distance

## Slide 9: Dry Asphalt – 30 mph
Test conditions: Braking from 30 mph
ABS bike had shortest stop with front brake applied
LBS bike had shortest stop with rear brake applied
ABS bike had shortest stop with both brakes applied
With LBS off, rear only braking produced longest stop
Scooter had longest stops in all three segments, when compared with other bikes with systems operational

## Slide 10: Dry Asphalt – 60 mph
Test Conditions: Braking from 60 mph
LBS bike had shortest stops with front, rear, and combined brake application
LBS uses both front and rear brakes even when one lever/pedal is applied
Performance tires on Sport bike with LBS also helped stopping distance performance

## Slide 11: Dry Asphalt – 80 mph
Only ABS and LBS bikes tested from this speed
ABS bike had shorter stop with front brake application and also with both brakes applied
When rear pedal alone was used, LBS bike performed better than the ABS bike
LBS bike exhibited consistently short stops regardless of whether front, rear or both brakes were applied

## Slide 12: Wet Asphalt – 30 mph
ABS bike had shortest stop when either front brake or both brakes were applied
ABS bike had highest brake application load due to increased rider confidence in ABS

## Slide 13: Dry Polished Concrete – 30 mph
Surface has lower coefficient of friction than dry asphalt
ABS equipped bike outperformed other bikes, with front or both brakes applied
Driver is able to make a hard brake application without concern for wheel lockup since ABS optimizes brake force for given road surface

## Slide 14: Braking in a Corner – 30 mph
Curve: 200-ft radius on dry asphalt
Sport bike with LBS had shortest stop for rear brake application only
Touring bike with ABS had shortest stops when front or both brakes applied
ABS increased rider confidence
However, during ABS activation, it was difficult for rider to maintain lane position due to different ABS modulation on front and rear wheels

## Slide 15: Conclusions – ABS Considerations
Touring bike with ABS did not show a clear advantage when braking in straight line stops
ABS improved rider confidence when braking on wet or curved surface because system prevents wheel lockup
In panic stops, riders typically apply front brake with a high application force
ABS bike experienced different ABS cycling on the front and rear wheels, which caused difficulty in maintaining lateral stability in the lane

## Slide 16: Conclusions – LBS Considerations
No unsettling characteristics found with LBS bike
LBS used only with hydraulic brake system at both front and rear
Many bikes have hybrid brake system with hydraulic actuation on front wheel and cable actuation on rear wheel

## Slide 17: Recommendations
Consider ABS requirements for front wheel only
Evaluate additional ABS-equipped bikes for braking in a curve performance
Evaluate ABS on rough road surface
Perform additional testing to evaluate effectiveness of burnish procedure
Develop test specifically for LBS

## Slide 18: Next Steps
Objectives of additional testing
  To further assess ABS performance
  To develop a test specifically to evaluate LBS
  To evaluate and compare stringency of FMVSS No. 122, ECE R78, and Japanese Standard
NHTSA is open to suggestions about test plan
  Method for comparing standards
  Type of maneuver to evaluate ABS performance