## Slide 1
REESS SCOPE as a first step
<number>
RESS-6-13
Notes: <number>

## Slide 2
This sub-group has addressed to develop the new REESS safety requirements for higher BEV/PHEV/HEV production volumes in the near future
Several types of REESS exist.
  Non-water based electrolyte (e.g. Li-ion)
  Water based electrolyte (e.g. NiMH, Lead-acid)
  Molten salt, Molten metal (e.g. ZEBRA, NaS)
  Capacitors, etc.
At present and foreseeable future, the most of REESS for BEV/PHEV/HEV will use electro-chemical battery with Non-water based electrolyte or Water based electrolyte
REESS SCOPE to be addressed as a first step
<number>
Notes: <number>

## Slide 3
  The major risks considered by the group is Fire/Explosion, while other safety aspect has been covered by existing regulations (ref. RESS-1-4)
  Flammability of the electrolyte is the key element to assess the potential risks of Fire/Explosion
  The potential risks are significantly different between
    Flammable, non-water based electrolyte (Li-ion )
    and
    Non-flammable, water based electrolyte (NiMH, Lead-acid)
REESS SCOPE to be addressed as a first step
<number>
Notes: <number>

## Slide 4
 | Li-ion | NiMH | Lead-acid
Reaction mechanism |  |  | 
carrier | Lituim-ion | Hydroxide-ion | Proton
cathode | Lithium metal oxide | Nickel oxyhydroxide | Lead dioxide
anode | Carbon | Hydrogen storage alloy | Lead
Flash point |  |  | 
charger
separator
charge
discharge
Lithium ion（Li＋）
＋
－
electrolyte
separator
Hydroxide（OH-）
＋
－
charger
charge
discharge
separator
＋
－
charger
charge
discharge
electrolyte
Proton（H＋）
electrolyte
Organic electrolyte (Flammable)
Aqueous alkaline (non-Flammable)
20-30℃
None
No ignition point
No ignition point
Non-Flammable
Dilute sulfuric acid (non-Flammable)
Non-Flammable
About 450℃(High volatile)
2.6-14.4 vol%
Auto-flammable limit
Electrolyte
Auto-ignition point
None
Difference between Flammable and non-Flammable
<number>
Notes: <number>

## Slide 5
Organic electrolyte for Lithium ion cell
Aqueous alkaline electrolyte for Nickel Metal Hydride cell
Flammability Test of electrolyte
Difference between Flammable and non-Flammable
<number>
Notes: <number>

## Slide 6
<number>
The R100/02 draft has been discussed focusing on the Li-ion which uses flammable electrolyte.
It is inappropriate to simply apply to the other batteries without assessing the degree of the potential risks and the expected effect of the regulatory requirements. *The potential risk of non-flammable electrolytes are far below than that of flammable electrolyte, as those has no flash point nor auto-ignition point.
Conclusion
The appropriate requirements for non-flammable should be developed for REESS as a next step after through examination of the potential risks and the effectiveness.
Notes: <number>

## Slide 7
End
Notes: <number>