Informal document N:28

29th GRSP, may 2001.

Agenda item 2.3.

COMPLEMENTARY PARAGRAPHS TO THE JAPAN PROPOSAL

- PROPOSAL:

Add a new paragraph 6.2.7

6.2.7: Retractors must fulfil, after durability test according to paragraph, 6.2.5.2.3 or 6.2.3.3.5, and immediately after the retracting force measurement according to 6.2.5.2.2 or 6.2.5.3.4, all next two specifications:

6.2.7.1: When the dummy is tilted 45º frontward and released to the initial position, being clothed with a cotton shirt, the retractor must be able to avoid any slack between torso and belt, and,

6.2.7.2: When the buckle is unlatched and the tongue is released, the retractor alone must be able to retract all webbing.