## Slide 1: Experience in using scanners
K.S. Abdiev
Statistics Agency of the Republic of Kazakhstan
Computer information center

## Slide 2: First National Census
Establishment of 5 data process sectional centers
Over 3 mln. forms processed in each center
CIC (Almaty) – creation of central census database

## Slide 3
Table1 Main indices of data processed
Process center | Scanners, No | Number of report forms, No | Number of potrfolio No | Number of forms processed by 1 scanner, No | Process duration, days | Forms processed per day, No
Almaty | 3 | 4743300 | 15800 | 1581100 | 102 | 46503
Aktobe | 2 | 3402191 | 11420 | 1701096 | 110 | 30929
East-Kazakhstan | 2 | 3000123 | 10040 | 1500062 | 90 | 33335
Karaganda | 2 | 4590000 | 14027 | 2295000 | 120 | 38250
South-Kazakhstan | 2 | 3710657 | 12847 | 1855329 | 90 | 41230
Total | 11 | 19446271 | 64134 |  |  | 

## Slide 4
Table 2 Number of personnel participating in data process
Process center | Editors | Form preparation operators for scanner | Maintenance personnel | Total, person
Almaty | 90 | 36 | 3 | 129
Aktobe | 60 | 21 | 3 | 84
East-Kazakhstan | 68 | 12 | 2 | 82
Karaganda | 66 | 16 | 2 | 84
South-Kazakhstan | 68 | 16 | 4 | 88
Total | 352 | 101 | 14 | 467

## Slide 5: ScanStar 5045C
Scan rate – up to 50 forms a min., actual – 30 forms
Page size – А4, resolution 200 pixels per inch
150 forms per one tray (max – 300)
software
BUSY
ImagePort
JobScan
RecoStar

## Slide 6: Technological process scheme
Recognizing station
Ethernet-LAN local network
JobScan Software
File Server
Recostar Software
BUSY Software
ScanStar5045 Scanner
PC with ImagePort
Preprocess work places

## Slide 9: Goals of sectional centers
Report forms scanning
Forms content recognition
Editing in BUSY medium, in 3 stages - initial, basic and with image usage
Data integrity control - arithmetic, logical and inter-forms
Automated coding, data conversion
Converted data downloading into Database Access
Editing in Database Access medium with image usage
Information control by regions by basin indices
Archiving, recording to CD-ROM or floppy discs and transfer to the republican center

## Slide 10: Central Level Goals
Receipt of information from regional centers
Information control for completeness and basic indices by regions (Database Access )
Creation of database for oblast (Database MS SQL Server )
Tabulation by sections
File backup
Data analysis and their checkup with oblast offices
Oblast database download into central database
Summary tabulation and generation of reports

## Slide 11: Applications developed to ensure process stages
Image Port , JobScan, Recostar, BUSY:
Description of documents
Information entered control system
Data editing programs
Data conversion programs and programs for transferring information from Busy system into final database
Visual C++ , Access , MS SQL:
Programs for data control, data editing downloaded from system , Busy into Access
Complementary programs for census materials processing

## Slide 12: Applications developed to ensure process stages
Set of applications aimed at general information flows management in the system
Data conversion programs
Programs for formation and maintaining reference information
Programs for recording and transfer of information from field offices to the center
Set of programs for operational tabulation
Development of programs for formation of technological files with aggregated census information
Reports generation programs

## Slide 13: Main problems
Recognition error was highly affected by the census reports quality
Tight deadlines
Lack of experience
Pilot census used other technology
Base software – narrow specialization