## Slide 1: Energy Wood Potential of Forests in the European Union
Ján Ilavský
Finnish Forest Research Institute, Joensuu Research Centre
Yliopistokatu 6, 80101 Joensuu, Finland
Tel.: +358 10 211 3296, e-mail: jan.ilavsky@metla.fi

## Slide 2
Aim:
  estimation of energy wood potential in EU25, based on available statistics and reports reflecting the situation in late 1990’s - early 2000
Contract from VTT Processes:
  results utilised in BioFuture project: Impact of increased use of bioenergy in Europe on forest and energy industries
Notes: EU 15 plus 10 new member countries

## Slide 3
  EU15
  6% renewables
  biomass 62% of the renewables
  new member countries
  4.6% renewables
  biomass 84% of the renewables
  most of the biomass used for energy is wood

## Slide 4: Three parts of analysis:
3) Estimation of felling residues from forests
available for wood supply
1) Estimation of roundwood balance on forest available for wood supply, i.e. estimation of unutilised roundwood potential that could be used for energy purposes, but also for manufacturing conventional products in the forest based industries or not harvested
Roundwood balance calculated as a difference between net annual increment and fellings
2) Roundwood and conventional fuelwood production

## Slide 5: Methods
background data
  data for net annual increment (NAI), fellings, and balance between NAI and fellings from the UN-ECE/FAO Forest Resources Assessment 2000 report (national data adjusted to fit internationally agreed terms and definitions)
  data for Cyprus from 1980’s – early 1990’s, for the other countries from mid 1990’s
  Estimation of roundwood and fuelwood production based on the data from the Finnish Statistical Yearbooks 1999-2001 (FAOSTAT Forestry Data)

## Slide 6: Results on roundwood balance
fellings 68% of the NAI
  72% in conif.
  59% in broadl.
roundwood balance 186 million m3/yr, i.e. unutilised increment 32% of the NAI
more than 16% of the fellings used for energy production (industrial residues and recovered products)
use of rounwood for energy purposes would depend on the prices of roundwood, wood-based products, energy

## Slide 7
In relative terms, RB smallest in the Baltics (15%), largest in South & South-Eastern Europe (48%).
Althogether 39% of the roundwood balance is in two countries, in Germany and France (72.5 mill. m3)

## Slide 8: Roundwood production (RP)
wood over bark harvested from forests and used for commercial wood processing and fuelwood purposes during a year
368 million m3 per year in late 1990s (15% higher in 2000 than in 1997)
  Approximately 69% softwood
  Relative proportion of softwood logs 63% and hardwood logs 52%
  62% in Sweden, Finland, Germany and France
Conventional fuelwood production – 48,4 million m3 per year
or – 13% of RP

## Slide 9: Estimation of felling residues from fellings of forests available for wood supply
Residues from fellings of roundwood (branches, needles, tops, off cuts)
Potential residues from felling balance
Stumps and coarse roots
Main sources of felling residues:
Notes: coarse=grossolano

## Slide 10
Estimation of biomass components:
Notes: coarse=grossolano

## Slide 11: Results
Theoretical forest fuel resources of EU25:
logging residues + balance = 560 mill. m3 (+144%)
Notes: coarse=grossolano

## Slide 12
Theoretical forest fuel potential in EU25

## Slide 13: Estimation of technically harvestable forest fuel potential
On 75% of clearcut sites and on 45% of thinning sites, residues can be harvested
65% of residues from mechanized cutting are recoverable
50% of residues from manual cutting are recoverable
REDUCTION FACTORS:
20% of volume of roots from clearcuts are harvestable
25% of volume of balance is harvestable
(roots volume of balance is not taken under consideration)
Notes: coarse=grossolano

## Slide 14
Volume of available forest fuels by country

## Slide 15
Volume of technically available forest fuels in EU25:
71.6 mill. m3 from felling residues
+ 67.3 mill m3 from balance = 138.9 mill. m3
= approximately 25% of the theoretical potential 560 mill. m3
above ground
36% of
residues
25% of above ground balance
14% on top of above ground available
felling residues

## Slide 16: Economically available
Calculations only for four countries
available forest fuels at costs
10 €/MWh or 20€/m3
15 €/MWh or 30 €/m3
available forest fuels from radius
100 km
200 km

## Slide 17: New projects on biofuels resources, market and trade
Forest Energy Resources, Energy Technology Market and Biofuel Trade in EU
Tekes Project 2004 - 2007
2 subprojects:
Wood Energy Potencial in EU and Market for Energy Wood Harvesting Technology
International Bioenergy Trade
Methodology and detailed case studies in 3 – 5 countries
Five European RES-heat pilots
EU EIE Project 2005 – 2007
Regions involved: North Karelia, Finland; Brandenburg, Germany; Catalonia, Spain; Svencionys, Lithuania; Castelo de Vide, Portugal

## Slide 18
The whole study is available in PDF
format at:
http://www.metla.fi/julkaisut/workingpapers/2004/mwp006.htm
Thank you for your attention