## Slide 1
Carbon – Ceramic Brake Discs UNECE R90:02
Presentation to 81st GRRF
February 2016
Geoffrey A Ross - CLEPA
1

## Slide 2: Carbon – Ceramic Brake Discs
Not to be confused with Carbon – Carbon brakes as used on FI cars,
Carbon – Ceramic (CSiC) brake discs are developed for road going cars and have “normal” friction levels & a user friendly operating temperature envelope
Construction
Carbon – Ceramic (CSiC) braking ring
Aluminium mounting hub
Benefits
Weight savings of up to 70%
High thermal competence
Low wear
Corrosion free
    Requirements for proper function
    Special brake pads
    High temperature bedding (pre-use conditioning)
2

## Slide 3: Carbon – Ceramic Brake Discs
Cast Iron & Carbon – Ceramic : two different friction couples - the elements are not interchangeable
Brake Disc | Brake Pad | Result
Cast Iron | Conventional | OK
Carbon - Ceramic | C – C Compatible | OK
Cast Iron | C – C Compatible | NOK
Carbon - Ceramic | Conventional | NOK

## Slide 4: Carbon – Ceramic Brake Discs
C - C friction couples fade less than cast iron friction couples
To offset the resulting higher surface temperatures slightly larger diameter discs are often employed when replacing a cast iron brake with a C- C brake
Chart: C - C Friction Couple
µ-average | 0.52309 | 0.54402 | 0.55582 | 0.52813 | 0.51862 | 0.50067 | 0.50455 | 0.50759 | 0.512 | 0.52925 | 0.53896 | 0.54311 | 0.55358 | 0.56183 | 0.55997




Diff | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Cast Iron Friction Couple
µ-average | 0.49285 | 0.52621 | 0.52693 | 0.5015 | 0.45984 | 0.41968 | 0.39043 | 0.3674 | 0.34682 | 0.32885 | 0.30919 | 0.29303 | 0.27823 | 0.26621 | 0.25008




Diff | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
4

## Slide 5: Carbon – Ceramic Brake Discs
Increasing market adoption
  Fitted as standard on “Supercars”
  Offered as customer option to conventional (cast iron) brakes on many high performance vehicles
  Available as replacement market “performance upgrade” for “enthusiasts” for track and road use
  Fitment predicted to grow > 20 x during next decade
5

## Slide 6: Carbon – Ceramic Brake Discs
With growing market adoption we need to consider replacement market
By current definition they need to comply with R90
  1.1.This Regulation applies to the basic braking function of the following replacement parts: Replacement brake drums and discs intended for use in friction brakes forming part of a braking system of vehicles of category M, N and O which have a type approval in accordance with Regulation No. 13 or Regulation No. 13‑H
But R90 written around conventional (cast iron) brakes and the way they function
6

## Slide 7: Carbon – Ceramic Brake Discs
With appropriate bedding and axle loading C-C brake discs and compatible brake pads successfully meet UNECER90:02 criteria
UN ECER90:O2 Requirement (M1) | Carbon – Ceramic Friction Couple
Compliance with R13H | OK
Comparison with OE fitment (within 10%) | OK
Thermal Fatigue Test ( ≥ 150 cycles) | OK
High Load Test (≥ 500 applications) | OK
7

## Slide 8: Carbon - Ceramic Brake Discs
Three cases to consider –
1) where C-C are fitted as original fitment
2) where C-C are offered as original fitment customer option
3) where companies wish to offer performance upgrades for road use
8

## Slide 9: Carbon – Ceramic Brake Discs
OEM Production Vehicles |  |  |  |  |  |  |  |  |  |  | 
Type of Vehicle |  | Standard OEM Fitment |  | Replacement (AM) Fitment |  |  |  |  |  |  | Possible Action
 |  | Brake Disc | Brake Pad | Brake Disc | Brake Pad | Approval Process |  |  | Issues/Problems |  | 
 |  |  |  |  |  | Brake Disc |  | Brake Pad |  |  | 
Normal Car |  | Cast Iron | Conventional | Cast Iron | Conventional | R90 |  | R90 | None |  | 
High Performance Car |  | Cast Iron | Conventional | Cast Iron | Conventional | R90 |  | R90 | None |  | 
 |  | Carbon - Ceramic | Carbon - Ceramic Compatible | Carbon - Ceramic | Carbon - Ceramic Compatible | R90 - "Interchangeable" category with OEM or R90 Approved Carbon – Ceramic brake pad |  | R90 | Bedding process in R90 (A3/2.2.2.3) not suitable for CC couple. Inertia mass (A11/3.2.1.2) not relevant to vehicle type |  | Add specific C-C bedding regime. Modify A11/3.2.1.2)
Super Car |  | Carbon - Ceramic | Carbon - Ceramic Compatible | Carbon - Ceramic | Carbon - Ceramic Compatible | R90 - "Interchangeable" category with OEM or R90 Approved Carbon – Ceramic brake pad |  | R90 | Bedding process in R90 (A3/2.2.2.3) not suitable for CC couple. Inertia mass (A11/3.2.1.2) not relevant to vehicle type |  | Add specific C-C bedding regime. Modify A11/3.2.1.2)
Post OEM Production Vehicles |  |  |  |  |  |  |  |  |  |  | 
High Performance Car - Braking Performance Upgrade | Cast Iron |  | Conventional | Carbon - Ceramic | Carbon - Ceramic Compatible | ? |  | ? | Disc Size & design |  | Individual Vehicle Type Approval ?
9