## Slide 1
UI
1234567
Challenges according to the implementation and usage of the
UNIQUE IDENTIFIER
Informal document GRE-82-31
(82nd GRE, 22-25 October 2019
agenda item 4)
Transmitted by IWG SLR

## Slide 2
UNIQUE IDENTIFIER
Current markings required on the device
The approval marking specify:
The contracting party (country) who is responsible for the type approval
The Regulation Number the device was type approved to
The status of the Regulation at the time of type approval
The number of the type approval
The different functions that are included in the device
Any possible restrictions in mounting height
Any possible restrictions in mounting position
Any possible restriction to the number of devices necessary (D or Y)
IMPORTANT:
ALL these markings must be visible after the installation of the device on the vehicle
The additional marking specify:
The trade name or mark of the manufacturer
The category(ies) of the light source(s) used, if available
The light source module identifier, if available
The rated voltage or range of voltage
……
These markings must not be visible when the device is installed on the vehicle
E4
148R00-1111
IA 2bY R1 F2
2DE-2345-02PA
ECME
EUROPEAN COMPANY
MANUFACTURING EVERYTHING
P21/5W
P21W
P21W
11-14V

## Slide 3
Current approval marking problem and UNIQUE IDENTIFIER solution
The idea behind the Unique Identifier
E6
112233
F3 K PL
00 00
00 XEWR 11111 22222 33333 44444
00 XCV 55555 66666 77777
00 XCWT 88888 99999
00 XCVR 121210 112211
00 XCWR 14441 14442
00 XCWR 552200 552201
Approval marking of a device used as a beam contributor for different AFS systems
UI
1234567
Once: we had a dream!
(On any fixed part visible after installation i.e. lens)
(On any fixed part visible after installation i.e. lens)
Unique Identifier marking of a device used as a beam contributor for different AFS systems
Electronic database (DETA)
Information
Information
Information
Database
+
Marking
60+ mm
35+ mm
20 mm
9 mm
The presence of the marking in front of the optics could even have a huge influence on the quality of the real optical system

## Slide 4
The approval marking tells you:
The contracting party (country) who is responsible for the type approval (E4)
The Regulation Number the device was type approved to (148)
The status of the Regulation at the time of type approval (00)
The number of the type approval (1111)
The different functions that are included in the device (IA, 2b, R1, F2)
Any possible restrictions in mounting height on the vehicle
Any possible restrictions in mounting position on the vehicle
Any necessary other devices that should be present (D or Y lamps)
UI
1234567
DETA Information
+
In the database (internet)
The Unique Identifier tells you:
The UI number under which the device information is available in the electronic database.
E4
148R00-1111
IA 2bY R1 F2
On the device
(approval markings + additional markings)
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
UNIQUE IDENTIFIER
Current status
SECRET
Only available to Type Approval Authority
Now: we face reality!
Paragraph 3.3.3. (148) „The approval marking may be replaced by the Unique Identifier (UI), if available.“
On the device
(UI number + additional markings)
Y

## Slide 5
E4
148R00-1111
IA 2bY R1 F2
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
UNIQUE IDENTIFIER
Information required
Conclusion: Benefit of the Unique Identifier is indivisibly connected to the access rights of the database!
-> Different interest groups need different parts of the available information
  Manufacturer -> all information for own type approvals, some information for all type approvals
  Type Approval Authority -> all information for own type approvals, some information for all type approvals
  Periodical technical inspection -> some information for all type approvals
  Maintain law and order -> some information for all type approvals
  Repair shop(s) -> some information for all type approvals
  Vehicle owner -> some information for all type approvals
UI
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
1234567
≠
DETA Information
+
On the device
(approval markings + additional markings)
On the device
(UI number + additional markings)

## Slide 6
WP.29 – 177th session – March 2019
98. WP.29 decided on the detailed access rights as noted in annex V of this report. WP.29 would revisit the matter at its June 2019 session, if necessary.
NO ACCESS LEVEL BEYOND CONTRACTING PARTY / MANUFACTURER, BUT MAYBE LATER
UNIQUE IDENTIFIER
Current status of the Database
WP.29 – 178th session – June 2019
E. Development of an electronic database for the exchange of type approval documentation (DETA) (agenda item 4.5)
Documentation: Informal documents: WP.29-178-22, WP.29-178-23, WP.29-178-24, WP.29-178-25 and WP.29-178-26-Rev.1
59. … He recommended that WP.29 invite GRs, in the context of UI, to consider whether current additional marking provisions were still to be considered part of the approval marking and could be replaced by the UI marking, or these additional markings have an information character and could be provided by alternative means (e.g. insertion in the Communication Form). WP.29 agreed with this suggestion.
GRE TO DECIDE WHAT MARKING MAY BE REPLACED BY UNIQUE IDENTIFIER

## Slide 7
UNIQUE IDENTIFIER
Options for improvement
Options for the future of the UI
Change the text of the Regulations to adapt current situation of the UI and the electronic database.
Wait for improvement of the access rights of the database and adapt text as necessary afterwards.
Leave everything as it is and see what happens.
UN-R148: Paragraph 3.3.3.:
„The approval marking may be replaced by the Unique Identifier (UI), if available.“
WP.29 (178):
„WP.29 invite GRs … to consider whether current additional marking provisions were still to be considered part of the approval marking and could be replaced by the UI marking”
WP.29 (177):
„Note: IWG on DETA will look at expanding access rights for further phases.“
…
A
B
C

## Slide 8
Original marking
on the device
2DE-2345-02PA
ECME
EUROPEAN COMPANY
MANUFACTURING EVERYTHING
P21/5W
P21W
P21W
11-14V
Marking(s) on device
UI
270650
E4
148R00-1111
IB 2aY R1 F2
UNIQUE IDENTIFIER
Possible improvement – Text of the Regulation(s)
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
Information included:
The UI number
The trade name or mark of the manufacturer
The category(ies) of the light source(s) used
The rated voltage or range of voltage
Benefit:
- Smaller marking
- Missing Information?
A
Add mandatory information
(e.g. Symbols)
Remove mandatory information
(e.g. additional symbols)
Possible changes to the current text
Current text of UN-R148
(pending on the availability and accessibility of DETA)

## Slide 9
 | CERT (communication on type approval) | TR (test report) | IF (information document) | OTHER (other document) | Summary & description
Approval granting TAA (for granted approval) | W | W | W | W | W
CP applying the UN Reg. for which approval was granted | R | R | R | R | R
CP applying UN Reg. 0 (access to the approvals of R0 and the annexed Regulations | R | R | R | R | R
CPs not applying that Reg. | R | - | - | - | R
Manufacturer (only for own approvals) | R | R | R | R | R
Periodical technical inspection | - | - | - | - | R
Organizations to maintain law and order | - | - | - | - | R
Repair shop(s) / Vehicle owner | - | - | - | - | R
Public | - | - | - | - | R
UNIQUE IDENTIFIER
Options for improvement – Update DETA
Summary & description
UI
270650
E6
F3 K PL
00 00
00 XEWR 11111 22222 33333 44444
00 XCV 55555 66666 77777
00 XCWT 88888 99999
00 XCVR 121210 112211
00 XCWR 14441 14442
00 XCWR 552200 552201
Additional information
….
….
…
Access rights as accepted by WP.29 177
Explanation:
R = read only
W = read + write + delete
B

## Slide 10
UNIQUE IDENTIFIER
Options for improvement – Do nothing and see what happens
C
?