## Slide 1: Supporting document for GRE/2019/21
2019-10-24
W. Schlager, Ph. Plathner
Submitted by the experts from IEC
Informal document GRE-82-45
(82nd GRE, 22-25 October 2019,
agenda Item 5)

## Slide 2
Questions on footnote 3, raised during GRE82:
#1: Justification for choosing elevated ambient air temperature of 60°C
#2: Justification for choosing luminous flux limit of at least 70%
Extract from GRE/2019/21

## Slide 3: #1: Justification for elevated ambient air temperature of 60°C
The temperature of 60°C was chosen to make this light source suitable for applications that require an ambient temperature range up to 60°C, e.g. electric cars, motorcycles, …
During the design-in of an H11 solution, the set-maker and carmaker decide, whether the substitute option with 60°C temperature range is suitable (or not)
  Note 1: the use of an LED substitute is optional / voluntary and is subject to dual approval
As LED technology is expected to develop further, categories with higher ambient temperature range can be defined in future (using the interlock to prohibit interchangeability)
  Note 2: the 60°C proposal reflects current state-of-the-art (given the specified cap size)

## Slide 4: #2: Justification for 70% luminous flux limit
The choice of the luminous flux limit of at least 70% is supported by:
Lumen ratio of other LED (substitute) categories in R.E.5 at elevated temperature
Life-time definition in IEC 60810 for LED light sources
Luminous flux maintenance in SAE J2560 for halogen light sources
Real world conditions

## Slide 5: Example for defined temperature ranges in R.E.5 today
Category in UNECE | Temperature range up to … | Luminous flux limit
PY21W/LED | 80°C | 65%
W5W/LED | 80°C | 70%
WY5W/LED | 80°C | 70%
C5W/LED | 80°C | 70%
R5W/LED | 80°C | 70%
Example: C5W/LEDK

## Slide 6: IEC 60810 lifetime for LED light sources  L70*
*The lifetime of a LED light source is defined as the time it takes until its light output, or lumen maintenance, reaches 70% of the initial output. This is called L70.

## Slide 7: SAE J2560 Halogen Luminous Flux Maintenance

## Slide 8: Comparison of minimum luminous flux under real world conditions
H11 Filament light source
  Objective luminous flux tolerance: - 10% (see H11 category sheet, 1350 lm ± 10%)
  ~ no dependency on ambient temperature: 0% (typical halogen bulb property)
  Lumen maintenance @350 h: - 30% (see manufacturer information, resp. SAE J2560)
 Worst case (= min. flux @350h): 0,9  1,0  0,7  - 37 % of nominal
H11/LED Substitute light source
  Objective luminous flux tolerance: - 10% (GRE/2019/21)
  Maximum drop at 60°C: -30% (GRE/2019/21)
  Lumen maintenance @350 h: - 2% (typical white LED property)
 Worst case (= min. flux @60°C @350h): 0,9  0,7  0,98  - 38 % of nominal
Irreversible !
Temporarily
e.g. when vehicle
is stationary

## Slide 10: Details: why 80°C for LSD application and 60°C for RID application
For Substitutes like W5W/LEDK or PY21W/LED the “bottom-heating” by a Halogen bulb was taken into account  80°C
  For H11/LED Substitutes, no “bottom heating”, additionally the significant self-heating of the Halogen bulb removed
Direction Indicator
Passing Beam
H11 fil.
PY21W
/LED
<80°C
Direction Indicator
Passing Beam
H11 fil.
~60W
~80°C
H11/LED
~20W
~55°C
Substitute