## Slide 1: Update from RDE IWG GRPE June 2020 From the sponsors: European Union Japan Korea
Informal document GRPE-81-17
81st GRPE, 9-11 June 2020
Agenda item 3(c)

## Slide 2: Summary
During GRPE meeting in June 2018, EU, Japan and Korea requested the creation of an RDE IWG and the proposal was accepted.
Creation of RDE IWG accepted by AC.3 in its June 2018 meeting
1st milestone achieved by submission of UNR RDE proposal in March 2020
Work on GTR RDE continues

## Slide 3: Meetings
The group met on:
  11-12 September 2018 in Brussels
  27-28 November 2018 in Brussels
  9 January 2019 in Geneva
  1-2 April 2019 in Tokyo
  22 May 2019 in Geneva
  9-10 July 2019 in Vienna
  30-31 October 2019 in Seoul
  14-15 January 2020 in Geneva
  25-26 February 2020 in Ispra (webex due to COVID)
  9-10 March 2020 (webex)
  27, 29 May 2020 (webex)

## Slide 4: UNR RDE-1
A draft for UN Regulation was prepared by EU and Japan based on the most recent version of the RDE Regulations in EU and Japan
Proposal was discussed in Seoul, Geneva and all subsequent meetings with RDE IWG
The proposal for the UN Regulation was submitted by EU and Japan in March 2020 as ECE/TRANS/WP.29/GRPE/2020/15
Further improvements via Informal Document GRPE-81-16

## Slide 5: UNR RDE-2
Improvements made in:
  Definitions
  Text logic
  Testing facilitation
Common boundaries developed that reflect both EU and Japan conditions
Moderate altitude conditions | Altitude lower or equal to 700 meters above sea level.
Extended altitude conditions | Altitude higher than 700 meters above sea level and lower or equal to 1300 meters above sea level.
Moderate temperature conditions | Greater than or equal to 273.15 K (0 °C) and lower than or equal to 308.15 K (35 °C).
Extended temperature conditions | Greater than or equal to 266.15 K (– 7 °C) and lower than 273.15 K (0 °C) or greater than 308.15 K (35 °C) and lower than or equal to 311.15 K (38 °C).

## Slide 6: UNR RDE-3
One RDE trip to check both against 4 phase WLTC and EU emission limits and 3 phase WLTC and Japanese emission limits
If one trip is not valid for both 4 and 3 phases evaluation, then a second trip is needed
Appropriate speed bins defined for both 4 and 3 phase evaluation
Single data reporting file created and will be found in the same space as the UNR RDE
Information package developed

## Slide 7: UNR RDE-4
Table A7/1 with u values recalculated
Methodology developed to analyse single trip for 3 phase WLTC by cutting all points higher than 100 km/h
Issue with PEMS Margin for NOx [0.43]
  Currently under discussion in EU due to a court decision
  Request to transmit the text to WP29 with PEMS margin NOx [0.43] pending the decision in EU

## Slide 8: GTR Status report
GTR being developed to be appropriate for many CPs
Decision in February to focus on the UNR
Develop the GTR according to the same structure and making use of the developments made in the UNR
Work on GTR will continue in September
Aim to submit Working Document for January 2021

## Slide 9: Summary:
Work progresses well and UNR RDE submitted in time for June 2020 GRPE
GTR will be reformatted according to the new structure and developments in UNR
Items still missing, like PM method
Aim to submit it for January 2021 GRPE session
Second phase of development will start in 2021

## Slide 10: Thank you for your attention! From the sponsors: European Union Japan Korea