## Slide 1: Proposal for a new UN GTR on Determination of Electrified Vehicle Power (DEVP)
IWG on EVE
81st GRPE Virtual Meeting
9-11 June 2020
Informal document GRPE-81-33
81st GRPE, 9-12 June 2020
Agenda item 9(a)

## Slide 2: History
Second mandate of the EVE IWG was approved in November 2014
WLTP had stated a need for an improved procedure to determine system power for classification and downscaling of light-duty hybrid vehicles
  Hybrid electric vehicles
  Pure electric vehicles with more than one motor
Part B of the mandate directed EVE to develop an Annex to GTR No. 15
EVE consulted with organizations doing similar work (SAE, ISO, KATRI)
  ISO 20762 was selected as basis for the procedure
  Initial draft was developed in 2017-2018 based closely on ISO 20762
Later, contracting parties stated a preference for a standalone GTR
In March 2019 AC.3 approved the decision to develop a standalone GTR

## Slide 3: Validation
JARI validation tests
  Commissioned by JAMA in 2016, in support of ISO 20762 development
  JARI tested several HEVs with good results
  JARI test report and technical expertise was provided to EVE IWG
Phase 1
  EVE conducted testing in 2018 using a draft based closely on ISO 20762
  Participants: JRC, Environment Canada, KATRI, US EPA
  Phase 1 revealed some differences in results of TP1 and TP2, and suggested other ways the procedure could be improved for use as a GTR
EVE proposed Phase 2 validation, and one year schedule extension
  Procedure was revised and evaluated for improved reliability of results
  Participants: JRC, Environment Canada

## Slide 4: Validation
Validation program led to restructuring of procedure and provided key results
  Further demonstrated that the method of eliciting maximum power is reliable
  Determined relative applicability of TP1 and TP2 to diverse powertrain types
  Strong theoretical basis for equivalence of TP1 and TP2 is now embodied in the procedure
  Where equivalence cannot be fulfilled, TP1 or TP2 alone is now specified
  If both are applicable, then if measurements are accurate, TP1 and TP2 should be very similar
Any validation program has limitations
  A fully authentic type approval situation is very difficult to duplicate
    Dependencies on level of manufacturer involvement, support and consultation
    Dependencies on ready availability of specific input data needed by the procedure
  Not every current and future variation in architecture or calibration can be tested
A strong case for validity may be based on good engineering judgment informed by the testing experience and its results
We are confident in its technical basis, and will likely learn more from its use in practice

## Slide 5: Status
Proposed DEVP GTR is Working Document GRPE/2020/12
Amended by informal document GRPE-81-27e_track
  Section I is Statement of Technical Rationale and Justification
    It is intended that this will serve as the “Technical Report”
      Detailed background on the technical development of the current procedure
      Review of validation program
      In-depth validation test reports have previously been shared via EVE website
    For an outline of the most significant changes from ISO 20762, see Section E.1
  Section II is the test procedure itself
  Annex 1 and 2 concern identification of reference points and test speed
  Annex 3 reserved for future text on determination of method equivalency

## Slide 6: Amendments
Most amendments accept bracketed text in working document
  Marked via Track Changes and comments in GRPE-81-27e_track
  List of amendments: see informal document GRPE-81-27e_list
New amendments concern:
  Minor edits (added abbreviation; clarified unit ‘kph’; typos)
  Correction of wording relating to 10-second measurement window
  Clarification that UNR 85 is equivalent to ISO 1585 for purpose of GTR
  Addition of RESERVED Annex 3 for determination of method equivalency
    Placeholder for future work on candidate method or equivalent

## Slide 7: Possible future work
Candidate method
  A candidate method (based on component tests rather than chassis test) could reduce test burden
  Annex 3 is reserved for future text on method equivalency or candidate method
WLTP expects to specify the DEVP GTR for determining a power value for classification and downscaling of hybrid vehicles
  EVE IWG anticipates working with WLTP for this purpose

## Slide 8: Acknowledgements
Thank you to the drafting team, and to the many technical experts and staff who supported this effort by participating in the EVE IWG
Thank you also to the laboratories who performed validation testing and provided other critical resources:
  Japan Automobile Research Institute (JARI)
  Joint Research Centre (JRC) VeLA 8, Ispra, Italy
  Korea Automobile Testing and Research Institute (KATRI)
  Environment and Climate Change Canada (ECCC) River Road Facility, Ottawa
  U.S. EPA National Vehicle and Fuel Emissions Laboratory, Ann Arbor, USA