## Slide 1
Analysis of Dooring accidents and a proposal for a corresponding Driver Assistance System
Informal document GRSG-118-08
(118th GRSG, 15–17 July 2020 Agenda item 5)

## Slide 2: Structure
Accidentology
  National statistic
  In-Depth (GIDAS)
  Derivation of cyclist stopping distance
Proposal for Driver Assistance System

## Slide 3: Accident Analysis – National statistic
 | Accidents | Killed | Seriously injured | Slightly injured
Total | 2209 | 1 | 283 | 1967
Daylight | 1907 | 1 | 250 | 1692
Dark / twilight | 303 | 0 | 33 | 275
Average Dooring accidents per year extrapolated for Germany (2007-2016)
Main accident types

## Slide 4: Accident Analysis – In-Depth (GIDAS)
Results from GIDAS analysis for years 2000-2019
In 95% of all accidents the involved vehicle type is passenger car
80% of Dooring accidents occur in daylight situations
Around 80% of Dooring accidents occur on the vehicles driver side

## Slide 5: Accident Analysis – In-Depth (GIDAS)
Average bicycle speed is around 16 km/h
50% of all cyclist have an initial velocity prior to the crash between 15 and 20 km/h
Around 95% of all cyclists have an initial velocity prior to the crash <= 25 km/h

## Slide 6: Derivation of cyclist stopping distance
Assumptions:
Bicycle speed vbicycle = 25 km/h
Bicycle deceleration abicycle = 3.5 m/s² according to DIN EN ISO 4210-2
Reaction time treaction = 1.2 s
Calculations:
Braking distance to standstill: sbraking = = 6.9 m
Thinking distance: sreaction = treaction × vbicycle = 8.3 m
Stopping distance: sstop = sreaction + sbraking = 15.2 m
Cyclist needs 15.2 m to reach standstill from an initial velocity of 25 km/h
vbicycle
abicycle
2
0.5×

## Slide 7: Proposal for Driver Assistance System
1 m
Critical area up to 15m
Proposal:
Speed adaptive critical area up to 15m with intensive warning of exiting car occupants or temporary blockade of the door
Adressing lateral distance up to 1m
Working under daylight as well as lowlight conditions
Working on driver as well as front seat passenger side